| WELL: | Childers Cove-1 | REPORT No.: | 7 | DAYS FROM SPUD: | 7 | DATE: | 25/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 1327 | Last Depth: | 765 | 24 HR PROGRESS: | 0 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 26/09/05 - 1439m – Drilling 8 ½” main hole in the Paaratte Formation. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | 1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |  |  |  |  |  |  |  |
| Skull Creek Mudstone |  |  | 1756.5 | -1705.0 |  |  |  | -1643.7 |  |  |
| Nullawarre Green |  |  | 1922.5 | -1871.0 |  |  |  | -1740.2 |  |  |
| Belfast Mudstone |  |  | 2028.5 | -1977.0 |  |  |  | -1757.0 |  |  |
| Top Amplitudes |  |  | 2345.5 | -2294.0 |  |  |  | -1965.8 |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 775.5 | - | 1191.0 | 0.3-36.2 (1.1) | SANDSTONE with Interbedded SILTSTONE. SANDSTONE, translucent to clear, opaque pale brown, frosted, fine to very coarse, dominantly medium to coarse, moderately well sorted, sub-rounded to sub-angular, rounded very coarse grains, weak to moderately calcareous cement, rare brown argillaceous matrix, localized common pyrite nodules, loose and clean, minor unconsolidated, fair to good inferred porosity, no fluorescence. SILTSTONE, medium to dark brown, grayish brown, pale to medium grey, argillaceous, trace arenaceous, occasional pyrite nodules, trace black lithics, soft to dispersive, localized firm, sub-blocky to amorphous. |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 1191.0 | - | 1225.0 | 0.6-9.2 (1.7) | SILTSTONE, with interbedded SANDSTONE. SANDSTONE, clear to translucent, frosted, pale grey, trace yellowish grey, very fine to medium, minor coarse, dominantly fine, moderately well to localized well sorted, sub-angular to sub-rounded, trace angular very coarse fractured grains, trace weak calcareous and siliceous cement, trace grayish brown argillaceous matrix, common muscovite flecks, loose and predominantly clean, fair porosity, no fluorescence. SILTSTONE, medium greenish grey to dark greenish grey, olive grey, brownish black, argillaceous, minor pyrite, predominantly soft to dispersive, rare firm to moderately hard, sub-blocky to blocky, amorphous. |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |

| 1225.0 | - | 1287.0 | 0.4-2.9 (1.3) | SANDSTONE with SILTSTONE interbeds SANDSTONE, translucent to transparent, clear, minor yellowish grey, predominantly medium to fine grains, coarse grains /p, moderately well sorted, strong siliceous cement, no visual matrix, trace carbonaceous specks, trace pyrite nodules, loose, moderately hard to hard aggregates, fair inferred and poor visual porosity, no fluorescence. SILTSTONE, light to medium grey, slightly brownish grey, argillaceous, arenaceous, grading to very fine SANDSTONE, common micromicaceous, soft to minor firm, common dispersive to soft, blocky to sub-blocky, trace sub-fissile in part, common amorphous. |
| --- | --- | --- | --- | --- |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |

| 1287.0 | - | (1439.0) | 0.7-6.8 (1.6) | Interbedded SANDSTONE and SILTSTONE. SANDSTONE, translucent to clear, frosted, opaque to milky in part, medium to coarse, common very coarse, occasional fine, sub-angular to sub-rounded, occasional angular, moderately sorted, weak siliceous cement, trace nod pyrite, carbonaceous fragments, loose and clean, good inferred porosity, no fluorescence. SILTSTONE, medium to dark grey, grayish brown, argillaceous, minor to common carbonaceous specks, occasional disseminated pyrite, trace glauconite, soft, dispersive in part, rare firm, sub-blocky to blocky, common amorphous. |
| --- | --- | --- | --- | --- |
| Gas | Units: | Nil | Composition (%): | - | / | - | / | - | / | - | / | - |
| Show Details / %CO2 | Nil |