| WELL: | Childers Cove-1 | REPORT No.: | 11 | DAYS FROM SPUD: | 11 | DATE: | 29/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2377 | Last Depth: | 2246 | 24 HR PROGRESS: | 131 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 30/09/05 – 2451m –Drill 8 ½” main hole in the Top Amplitude. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |  |  |  |  |  |  |  |
| Skull Creek Mudstone | 1757.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1919.5 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2027.0 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes | 2335.0 | -2283.5 | 2345.5 | -2294.0 | 10.5 | L |  | -1965.8 | 317.7 | L |
| ??? | 2360.0 | -2308.5 | - | - | - | - |  |  |  |  |
| ??? | 2381.0 | -2329.5 | - | - | - | - |  |  |  |  |
| ??? | 2403.0 | -2351.5 | - | - | - | - |  |  |  |  |
| Base Amplitudes |  |  | 2482.5 | -2431.0 |  |  |  | - |  |  |
| TD CDL-7 (shallow) |  |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation |  |  | 2703.5 | -2652.0 |  |  |  | -2028.2 |  |  |
| TD CDL-7 (success case) |  |  | 2743.5 | -2692.0 |  |  |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 2027.0 | - | 2335.0 | 1.1-25.5 (2.9) | Massive SILTSTONE with minor SANDSTONE lenses and trace LIMESTONE. SANDSTONE, off white to brownish grey, very fine, occasional fine, generally very well sorted, sub-angular to sub-rounded, very weak calcareous cement, generally sill, abundant argillaceous matrix, common glauconite, unconsolidated, very poor to tight visual porosity, no fluorescence. SILTSTONE, predominantly grey to brownish grey, dark brownish grey, slightly greenish grey in part, very argillaceous, grading to CLAYSTONE in part, localized common glauconite in part, trace carbonaceous material in part, generally soft to firm in part, slightly moderately calcareous, sub-fissile to sub-blocky. LIMESTONE, cream, minor argillaceous/fossiliferous, soft to brittle. |
| Gas | Units: | 1-23 | Composition (%): | 97 | / | 3 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 2335.0 | - | 2360.0 | 1.6-8.8 (3.7) | Massive SILTSTONE with minor SANDSTONE interbeds. SANDSTONE, translucent, pale yellow, slightly pale grey, clear, very fine to medium, rare coarse to very coarse grains, moderately to well sorted, angular to sub-rounded, trace strong siliceous cement, white to pale grey argillaceous matrix, rare and very coarse fractured grains, carbonaceous specks, glauconite, loose, moderately hard aggregates, poor inferred and very poor visual porosity, no fluorescence. SILTSTONE, medium to dark grey, grayish brown, olive grey, dark greenish grey, argillaceous, arenaceous in part, carbonaceous specks, soft to firm, moderately hard to hard, sub-blocky, abundant sub-fissile to fissile in part. |
| Gas | Units: | 8-27 | Composition (%): | 99 | / | 1 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| 2360.0 | - | 2381.0 | 1.4-4.4 (1.9) | Interbedded SILTSTONE and SANDSTONE. SANDSTONE, clear to translucent, pale grey, dusky yellowish green, grayish green, frosted, fine to medium, rare coarse grains, moderately well sorted, sub-angular to sub-rounded, weak siliceous cement, pale greenish argillaceous matrix, abundant glauconite and chlorite, loose, poor to localized fair visual and inferred porosity, no fluorescence. SILTSTONE, dark greenish grey, dusky green, medium to dark grey, argillaceous, minor arenaceous, soft to firm, sub-blocky to sub-fissile, fissile in part. |
| --- | --- | --- | --- | --- |
| Gas | Units: | 4-14 | Composition (%): | 100 | / | 0 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| 2381.0 | - | 2403.0 | 1.4-5.4 (5.4) | Massive SILTSTONE, SILTSTONE, pale reddish brown, grayish brown, common brick red, very argillaceous, common grading to CLAYSTONE, minor arenaceous in part, moderately calcareous in part, , predominantly amorphous with occasional blocky aggregates. |
| --- | --- | --- | --- | --- |
| Gas | Units: | 4-11 | Composition (%): | 100 | / | 0 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| 2403.0 | - | (2451.0) | 2.5-12.6 (4.4) | SILTSTONE with SANDSTONE interbeds. SANDSTONE, medium to dark grayish brown, minor very light brownish cream, common mottled with green and dark lithics, very fine, very well sorted, sub-angular to sub-rounded, moderately strong calcareous cement, dominantly argillaceous to silty matrix, common lithics and minor chlorite, common friable to moderately firm, in part, occasional firm to moderately hard, very poor to tight visual porosity, no fluorescence. SILTSTONE, light to medium grey, grayish brown, minor mottled grey and green in part, very argillaceous grading to CLAYSTONE in part, minor arenaceous in part, moderately calcareous in part, common sticky, generally very soft to trace firm, fissile – dispersive, common dispersive. |
| --- | --- | --- | --- | --- |
| Gas | Units: | 4-11 | Composition (%): | 99 | / | 1 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |