| WELL: | Childers Cove-1 | REPORT No.: | 12 | DAYS FROM SPUD: | 12 | DATE: | 30/09/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2545 | Last Depth: | 2377 | 24 HR PROGRESS: | 168 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 01/10/05 – 2545m –POOH after reaching TD at 19:00hrs on 30/09/2005. Preparing for Precision Wireline. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: | 19:00hrs 30/09/05 | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = |  | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |
| Skull Creek Mudstone | 1757.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1919.5 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2027.0 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes | 2335.0 | -2283.5 | 2345.5 | -2294.0 | 10.5 | L |  | -1965.8 | 317.7 | L |
| ??? | 2360.0 | -2308.5 | - | - | - | - |  |  |  |  |
| ??? | 2381.0 | -2329.5 | - | - | - | - |  |  |  |  |
| ??? | 2403.0 | -2351.5 | - | - | - | - |  |  |  |  |
| Base Amplitudes | 2471.0 | -2419.5 | 2482.5 | -2431.0 | 11.5 | H |  | - |  |  |
| TD CDL-7 (shallow) | 2545.0 |  | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation | 2481.0 | -2429.5 | 2703.5 | -2652.0 | - | - |  | -2028.2 | 401.3 | L |
| TD CDL-7 (success case) | N/A | N/A | 2743.5 | -2692.0 | - | - |  | - |  |  |

Tops are wellsite picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 2403.0 | - | 2471.0 | 2.5-12.6 (4.4) | SILTSTONE with SANDSTONE interbeds. SANDSTONE, medium to dark grayish brown, minor very light brownish cream, common mottled with green and dark lithics, very fine, very well sorted, sub-angular to sub-rounded, moderately strong calcareous cement, dominantly argillaceous to silty matrix, common lithics and minor chlorite, common friable to moderately firm, in part, occasional firm to moderately hard, very poor to tight visual porosity, no fluorescence. SILTSTONE, light to medium grey, grayish brown, minor mottled grey and green in part, very argillaceous grading to CLAYSTONE in part, minor arenaceous in part, moderately calcareous in part, common sticky, generally very soft to trace firm, fissile – dispersive, common dispersive. |
| Gas | Units: | 4-11 | Composition (%): | 99 | / | 1 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 2471.0 | - | 2545.0 | 1.3-22.9 (7.0) | SILTSTONE with interbedded SANDSTONE. SANDSTONE, translucent, pale yellow, clear, pale grey, pale green in part, medium to very coarse, poor to localized moderately sorted, weak to localized moderately calcareous and weak siliceous cement, trace white and very pale grey argillaceous matrix, common angular fractured very coarse grains, trace whitish orange lithics, loose, unconsolidated, moderately hard to hard aggregates, fair inferred and tight to very poor visual porosity, no fluorescence, trace mineral fluorescence at base of interval, dull yellow, bluish, no cut. SILTSTONE, light grey, greenish grey, medium grey in part, light brown, light orange, yellowish to light orange, medium reddish brown, arenaceous, argillaceous, calcareous in part, occasional grading to very fine SANDSTONE in part, glauconite, chlorite, pyrite nodules (more prevalent at base of interval), micromicaceous, dispersive, moderately hard to very hard in part, dispersive, blocky to sub-fissile, predominantly sub-blocky to sub-fissile, amorphous. |
| Gas | Units: | 2-259 | Composition (%): | 94 | / | 5 | / | 1 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |