| WELL: | Childers Cove-1 | REPORT No.: | 13 | DAYS FROM SPUD: | 13 | DATE: | 01/10/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2545 | Last Depth: | 2545 | 24 HR PROGRESS: | 0 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 02/10/05 – 2545m – RIH to drill 8 ½” main hole. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = | 2545.0 | Metres R.T. |
| TD Reached Date: | 19:00hrs 30/09/05 | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = | 544.5 | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 645.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 775.0 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1191.0 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1225.0 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1287.0 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |
| Skull Creek Mudstone | 1757.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1919.5 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2027.0 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes | 2335.0 | -2283.5 | 2345.5 | -2294.0 | 10.5 | L |  | -1965.8 | 317.7 | L |
| ??? | 2360.0 | -2308.5 | - | - | - | - |  |  |  |  |
| ??? | 2381.0 | -2329.5 | - | - | - | - |  |  |  |  |
| ??? | 2403.0 | -2351.5 | - | - | - | - |  |  |  |  |
| Base Amplitudes | 2471.0 | -2419.5 | 2482.5 | -2431.0 | 11.5 | H |  | - |  |  |
| TD CDL-7 (shallow) | 2545.0 | -2493.5 | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation | ?2481.0 | ?-2429.5 | 2703.5 | -2652.0 | - | - |  | -2028.2 | 401.3 | L |
| TD CDL-7 (success case) | N/A | N/A | 2743.5 | -2692.0 | - | - |  | - |  |  |

Tops are wellsite picks- changes may be made after town confirmation with wireline logs.

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| Gas | Units: | 4-11 | Composition (%): | 99 | / | 1 | / | 0 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |