| WELL: | Childers Cove-1 | REPORT No.: | 14 | DAYS FROM SPUD: | 14 | DATE: | 02/10/05 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0000hrs Depth: | 2616 | Last Depth: | 2545 | 24 HR PROGRESS: | 71 | PTD: | 2536.0mRT(1) |
| 0600 OPS: | 03/10/05 – 22647m – Drilling 8 ½” main hole in the Eumeralla Formation to TD. |
| REMARKS: |  |

| PRIMARY OBJECTIVES: | Prognosed | SECONDARY OBJECTIVES: | Prognosed |
| --- | --- | --- | --- |
| Flaxman/Waarre Formation | 2349.0 m R.T. |  |  |
| Spud Date: | 18:00hrs 19/09/05 | Surface Latitude: | 38°29’31.96” | T.D. = |  | Metres R.T. |
| TD Reached Date: |  | Surface Longitude: | 142°44’46.66” | G.L. = | 46.2 | Metres ASL |
| Rig release Date: |  | Surface E (MGA94): | 0 652 295.0 | R.T. = | 51.5 | Metres ASL |
| Rig | Century Rig-7 | Surface N (MGA94): | 5 738 126.0 |  |  |
| Nearby Wells / Facilities are | 244mm Casing Shoe = | 544.5 | Metres R.T. |
|  | 178mm Casing Shoe = |  | Metres R.T. |

| Fm. Tops | Wellsite | Wellsite | Prognosed Depth | Diff | H/L |  | Sub-Sea Depth Comparisons |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (* Geophysical Picks) | (mRT) | (mSS) | (mRT) | (mSS) |  |  |  | P-1ST1 | Diff | H/L |
| Port Campbell Limestone | 5.3 | 46.2 | 5.3 | 46.2 |  |  |  | 5.3 |  |  |
| Gellibrand Marl | 213.0 | -161.5 | 144.5 | -93.0 | 68.5 | L |  | -149.2 | 12.3 | L |
| Clifton Formation | 595.5 | -544.0 | 562.5 | -511.0 | 33.0 | L |  | -526.8 | 17.2 | L |
| Narrawaturk Marl | 623.0 | -571.5 | 592.5 | -541.0 | 30.5 | L |  | -546.2 | 25.3 | L |
| Mepunga Formation | 659.0 | -593.5 | 661.5 | -610.0 | 16.5 | H |  | -664.0 | 70.3 | H |
| Dilwyn Formation | 743.4 | -723.5 | 750.5 | -699.0 | 24.5 | L |  | -717.4 | 6.1 | L |
| Pember Mudstone | 1056.3 | -1139.5 | 1136.5 | -1085.0 | 54.5 | L |  | -936.3 | 203.2 | L |
| Pebble Point Formation | 1137.3 | -1173.5 | 1195.5 | -1144.0 | 29.5 | L |  | -1021.1 | 152.4 | L |
| Paaratte Formation | 1237.4 | -1235.5 | 1285.5 | -1234.0 | 1.5 | L |  | -1175.2 | 60.3 | L |
| Skull Creek Mudstone | 1746.0 | -1705.5 | 1756.5 | -1705.0 | 0.5 | L |  | -1643.7 | 61.8 | L |
| Nullawarre Green | 1926.0 | -1868.0 | 1922.5 | -1871.0 | 2.0 | H |  | -1740.2 | 127.8 | L |
| Belfast Mudstone | 2013.9 | -1975.5 | 2028.5 | -1977.0 | 1.5 | H |  | -1757.0 | 218.5 | L |
| Top Amplitudes | 2318.7 | -2283.5 | 2345.5 | -2294.0 | 10.5 | L |  | -1965.8 | 317.7 | L |
| Base Amplitudes | 2471.0 | -2419.5 | 2482.5 | -2431.0 | 11.5 | H |  | - |  |  |
| TD CDL-7 (shallow) | 2545.0 | -2493.5 | 2532.5 | -2481.0 |  |  |  | - |  |  |
| Eumeralla Formation | ?2481.0 | ?-2429.5 | 2703.5 | -2652.0 | - | - |  | -2028.2 | 401.3 | L |
| TD CDL-7 (success case) | N/A | N/A | 2743.5 | -2692.0 | - | - |  | - |  |  |

Tops are wellsite picks

Wireline picks

| Interval | ROP (ave) | Lithology Description |
| --- | --- | --- |
| 2471.0 | - | 2551.0 | 1.3-22.9 (6.9) | SILTSTONE with interbedded SANDSTONE. SANDSTONE, translucent, frosted, milky, pale yellow, pale greenish, minor clear, very poor sorted, coarse to very coarse, minor to trace medium grains, angular to sub-rounded, dominantly angular very coarse fractured grains, moderately to localized strong calcareous cement, trace to rare white argillaceous matrix, minor pyrite nodules, minor pale green and dark greenish black lithics, loose, poor to localized good porosity, no fluorescence. SILTSTONE, light grey, greenish grey, medium grey in part, light brown, light orange, yellowish to light orange, medium reddish brown. Arenaceous, argillaceous, calcareous in part, occasional grading to very fine SANDSTONE in part, glauconite, chlorite, pyrite nodules (more prevalent at base of interval), micromicaceous. Dispersive, moderately hard to very hard in part, dispersive, blocky to sub-fissile, predominantly sub-blocky to sub-fissile, amorphous. |
| Gas | Units: | 5-683 | Composition (%): | 94 | / | 5 | / | 1 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |
| Interval | ROP (ave) | Lithology Description |
| 2551.0 | - | 2622.0 | 1.1-26.3 (7.2) | SILTSTONE with interbedded SANDSTONE. SANDSTONE, translucent to clear, milky, frosted, minor clear, very fine to medium, predominantly fine, moderately well sorted, sub-angular to sub-rounded, strong calcareous and trace to rare pyrite cement, white argillaceous kaolinite matrix, nodular and disseminated pyrite, loose, unconsolidated, moderately hard to very hard aggregates, poor to fair and very poor to tight visual porosity, no fluorescence. SILTSTONE, 1) light grey, brownish grey, light brownish grey, olive grey, dark grey in part, minor dark olive grey, argillaceous, minor arenaceous, minor carbonaceous specks and laminations, chlorite in part, trace LIMESTONE specks and material, disseminated and nodular pyrite, firm to moderately hard, hard in part, sub-fissile to sub-blocky, amorphous in part. SILTSTONE, 2) (TUFF?) white to very pale grey, very argillaceous, dispersive, amorphous. |
| Gas | Units: | 1-259 | Composition (%): | 88 | / | 7 | / | 4 | / | 1 | / | 0 |
| Show Details / %CO2 | FLUORESCENCE (Trace): 2589-2596 – dim – moderately bright whitish blue, pinpoint, very slow whitish blue blooming crush cut, very thin dull yellowish white ring residue. |

| 2622.0 | - | (2647.0) | 3.3-38.1 (10.5) | Massive TUFF. TUFF, light greenish grey, off white, trace greenish red, trace yellowish orange, very argillaceous, very calcareous in part, common chlorite in part, common dispersive, very soft, occasional slightly firm in part, abundant amorphous, rare sub-blocky aggregates. |
| --- | --- | --- | --- | --- |
| Gas | Units: | 6-17 | Composition (%): | 94 | / | 5 | / | 1 | / | 0 | / | 0 |
| Show Details / %CO2 | Nil |