Report for : Greg Doty / Richard Moore

Compiled by : Mark Smith

| WELL | CBA A15B |
| --- | --- |
| DATE | 22-08-2009 |
| REPORT # | 9 |
| MIDNIGHT ACTIVITY | Back ream out of hole at 907.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3120.0 mMDRT |  | MINIMUM | 9.3 | 3039.5 |
| TVD | 2486.3 mTVDRT |  | MAXIMUM | 57.5 | 3117.0 |
| PROGRESS LAST 24 hrs | 140.0 m |  | AVERAGE | 36.8 | 2980.0 – 3120.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top of Lakes Entrance Formation | 2715.0 | 2174.6 | -2133.6 | 3.6m L | 2712.0 | 2171.0 |
| Top of Latrobe Group | 3022.5 | 2411.9 | -2370.9 | 3.9m L | 3018.0 | 2408.0 |
| TCC / M112 | 3024.0 | 2413.0 | -2372.0 | 3.0m L | 3020.0 | 2410.0 |
| M131A | 3028.0 | 2416.1 | -2375.1 | 4.1m L | 3023.0 | 2412.0 |
| M131B | 3031.0 | 2418.4 | -2377.4 | 3.4m L | 3027.0 | 2415.0 |
| M132 Upper | 3034.0 | 2420.8 | -2379.8 | 0.8m L | 3033.0 | 2420.0 |
| M132 Lower | 3038.0 | 2423.8 | -2382.8 | 0.2m H | 3038.0 | 2424.0 |
| M141 | 3048.0 | 2431.6 | -2390.6 | 2.6m L | 3044.0 | 2429.0 |
| OOWC | 3056.4 | 2438.0 | -2397.0 | 0.4m L | 3056.0 | 2438.0 |
| Total Depth | 3120.0 | 2486.3 | -2445.3 | 2.3m L | 3116.0 | 2484.0 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3025.5 | 74.4 | 0.351 | 0.098 | 0.149 | 0.108 | 0.035 | - |
| MAX (GFF) | 3026.5 | 49.3 | 0.250 | 0.075 | 0.139 | 0.119 | 0.045 | - |
| BG (Reserval) | 2980.0-3120.0 | 21.9 | 0.144 | 0.033 | 0.029 | 0.024 | 0.008 | 0 |
| BG (GFF) | 2980.0-3120.0 | 12.3 | 0.100 | 0.031 | 0.014 | 0.012 | 0.004 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 5 | 4RR |
| SIZE (in) | 9.875 | 9.875 |
| MANUFACTURER/TYPE | REED / RSX616M-11 | REED / RSX616M-A14 |
| JETS (/32 inch) | 6 x 18 | 6 x 20 |
| DEPTH IN (m) | 1217.0 | 1215.0 |
| DEPTH OUT (m) | - | 1217.0 |
| METRES ON RUN (m) | 1903.0 | 2.0 |
| HRS ON BTM 24hrs/total | 3.8 / 30.7 | 0.0 / 0.4 |
| BIT CONDITION | - | 7-7-BT-A-X-E-WT-BHA |
| RPM RANGE 24hrs | 149-163 | - |
| Pump Hrs 24 hrs / total | 15.8 / 58.2 | 0.0 / 8.0 |
| Krevs 24 hrs / total | 33 / 272 | 0 / 1 |

| 24 HOUR SUMMARY | Drill and survey 9-7/8” production hole from 2980.0 mMDRT to 3120.0 mMDRT as per Anadrill’s instructions. Circulate and work string while Anadrill downlink to turn off tool. Circulate 2 times bottoms up from 3120.0 mMDRT to 3068.0 mMDRT until shakers clean. Back ream out of hole from 3068.0 mMDRT to 907.0 mMDRT. |
| --- | --- |
| 23-08-2009 5 AM UPDATE | Back ream out of hole from 907.0 mMDRT to 695.0 mMDRT. Pump out of hole from 695.0 mMDRT to inside shoe at 655.0 mMDRT. Circulate and work string until shakers clean. Flow check and pump 15 bbl slug. Pull out of hole from 655.0 mMDRT to 160.0 mMDRT. 5AM DEPTH: 3120.0 mMDRT 2486.3 mTVDRT |