Report for : Richard Moore / Greg Doty / Sam Falkner

Compiled by : Mark Smith

| WELL | CBA A19A |
| --- | --- |
| DATE | 28-04-2009 |
| REPORT # | 15 |
| MIDNIGHT ACTIVITY | Drilling 8½" hole at 2958.0 mMDRT. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3200.0 mMDRT |  | MINIMUM | 3.6 | 3043.0 |
| TVD | 2473.4 mTVDRT |  | MAXIMUM | 66.2 | 3099.0 |
| PROGRESS LAST 24 hrs | 242.0 m |  | AVERAGE | 31.4 | 29580 - 3200.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance |  |  |  |  | 2829.0 | 2206.0 |
| Top of Latrobe Group |  |  |  |  | 3049.0 | 2365.6 |
| Top Coarse Clastics / M111 reservoir |  |  |  |  | 3053.7 | 2370.1 |
| Top M112 reservoir |  |  |  |  | 3063.1 | 2375.4 |
| Top M131 Upper reservoir |  |  |  |  | 3071.4 | 2381.1 |
| Top M132 Upper reservoir |  |  |  |  | 3094.4 | 2396.9 |
| Top M132 Lower reservoir |  |  |  |  | 3105.2 | 2404.2 |
| 3.5FS |  |  |  |  | 3105.2 | 2405.2 |
| M141 reservoir |  |  |  |  | 3111.3 | 2408.5 |
| Halibut Original Oil Water Contact |  |  |  |  | 3154.2 | 2438.0 |
| Total Depth |  |  |  |  | 3194.2 | 2465.2 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3052.0 | 128.5 | 0.583 | 0.209 | 0.282 | 0.192 | 0.062 | - |
| MAX (GFF) | 3052.0 | 146.0 | 0.624 | 0.224 | 0.307 | 0.205 | 0.056 | - |
| BG (Reserval) | 2958.0-3200.0 | 35 | 0.170 | 0.053 | 0.064 | 0.049 | 0.018 | - |
| BG (GFF) | 2958.0-3200.0 | 35 | 0.181 | 0.049 | 0.061 | 0.045 | 0.013 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4RR | 3 |
| SIZE (in) | 8½ | 8½ |
| MANUFACTURER/TYPE | REED HYCALOG RSX616M | REED HP21G |
| JETS (/32 inch) | 6 x 18 | 3 x 18 |
| DEPTH IN (m) | 732.0 | 615.0 |
| DEPTH OUT (m) |  | 732.0 |
| METRES ON RUN (m) | 2468.0 | 117.0 |
| HRS ON BTM 24hrs/total | 7.7 / 55.2 | 11.1 |
| BIT CONDITION |  | 1-1-WT-A-E-E-E-In-No-BHA |
| RPM RANGE 24hrs | 80-160 |  |
| Pump Hrs 24 hrs / total | 73.2 / 91.8 | 22.0 |
| Krevs 24 hrs / total | 143 / 991 | 208 |

| 24 HOUR SUMMARY | Drill 8½” hole from 2958.0 mMDRT to 3200.0 mMDRT. Circulate hole clean from 3200.0 mMDRT to 3144.0 mMDRT. Take parameters, conduct SCR’s and flow check. Back ream out of hole from 3144.0 mMDRT to 1943.0 mMDRT. |
| --- | --- |
| 29-04-2009 5AM UPDATE | Back ream out of hole from 1943.0 mMDRT to 1409.0 mMDRT. 5AM DEPTH: 3200.00 mMDRT (2473.45 mTVDRT) |