Report for : Dan Daniels / Mark Calicutt / Sam Falkener

Compiled by  : Col Chadwick

| WELL | CBA-A21A |
| --- | --- |
| DATE | 25-03-2009 |
| REPORT # | 11 |
| MIDNIGHT ACTIVITY | POOH HWDP @ 175.0 mMDRT |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3923.0 mMDRT |  | MINIMUM | - | - |
| TVD | 2467.70 mTVDRT |  | MAXIMUM | - | - |
| PROGRESS LAST 24 hrs | 0 m |  | AVERAGE | - | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Lakes Entrance Fm. | 3390.0 | 2185.9 | -2144.9 | 12.1 H | 3406.0 | 2198.0 |
| Top of Latrobe Grp | 3665.5 | 2337.7 | -2296.7 | 7.7 L | 3648.0 | 2330.0 |
| Top Coarse Clastics / M111 Reservoir | 3668.0 | 2339.0 | -2298.0 | 5.0 L | 3656.0 | 2334.0 |
| Top M112 Reservoir | 3701.5 | 2355.0 | -2314.0 | 4.0 L | 3689.9 | 2351.0 |
| Top M131 Reservoir | 3716.0 | 2363.0 | -2322.0 | 7.0 L | 3699.9 | 2356.0 |
| Top M132 Upper Reservoir | 3746.0 | 2378.1 | -2337.1 | 5.1 L | 3733.8 | 2373.0 |
| Top M132 Lower Reservoir | 3755.0 | 2382.6 | -2341.6 | 5.6 L | 3741.8 | 2377.0 |
| 4AFS Marker | 3777.0 | 2393.8 | -2352.8 | 5.8 L | 3763.8 | 2388.0 |
| M145 Reservoir | 3812.0 | 2411.6 | -2370.0 | 9.0 L | 3791.7 | 2402.0 |
| Halibut Org OWC | 3846.4 | 2438.0 | -2397.0 | - | 3863.5 | 2438.0 |
| Total Depth | 3923.00 | 2467.63 | -2426.63 | 9.63 L | 3903.5 | 2458.0 |

| Current Formation | 90% CLAYSTONE ; 10% SANDSTONE |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | - | - | - | - | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | - | - | - | - | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | 3581 | 16.40 | 0.050 | 0.014 | 0.022 | 0.025 | 0.013 | - |
| TRIP GAS (GFF) | 3520 | 5.30 | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 9 7/8" | 9 7/8" |
| MANUFACTURER/TYPE | Reed Hycalog RSX616M-A11 | Reed Hycalog RSX616M-A11 |
| JETS (/32 inch) | 6 x 18 | 6 x 18 |
| DEPTH IN (m) | 3700.0 | 638.0 |
| DEPTH OUT (m) | 3928.0 | 3700.0 |
| METRES ON RUN (m) | 223 | 3062.0 |
| HRS ON BTM 24hrs/total | 0 / 6.3 | 0 / 87.1 |
| BIT CONDITION | - | 8-8-RO-A-X-IN-HC-PR/PP |
| RPM RANGE 24hrs | N/A | / |
| Pump Hrs 24 hrs / total | 12.5 / 28 | 0 / 135.3 |
| Krevs 24 hrs / total | 0 / 47 | 0 / 590 |

| 24 HOUR SUMMARY | Backream out of hole from 3670.0 mMDRT to 613.0 MMDRT @ 5 mins per stand. Pump slug. Pull out of hole 5.5” drill pipe on elevators from 613.0 mMDRT to 235.0 mMDRT. Pull out of hole 5.5” HWDP from 235.0 mMDRT to 175.0 mMDRT. |
| --- | --- |
| 26-03-2009 5AM UPDATE | Pull out hole 5.5” HWDP and BHA from 175.0 mMDRT to 38.0 mMDRT. Lay out directional tools and BHA from 38.0 mMDRT to surface. Clean and clear rig floor. Pull wear bushing. Function test BOP’s and jet stack. 3923.0 mMDRT (2467.70 mTVDRT) 0.0 mMDRT Bit Depth |