Report for : Andy Choy / Mark Calicut / Richard Moore

Compiled by : Gareth Munro

| WELL | CBA A28 |
| --- | --- |
| DATE | 14-07-2009 |
| REPORT # | 14 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3860.0 mMDRT |  | MINIMUM | 7.25 | 3423.0 |
| TVD | 2170.10mTVDRT |  | MAXIMUM | 71.92 | 3476.0 |
| PROGRESS LAST 24 hrs | 437.0 m |  | AVERAGE | 30.99 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.0m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Top Lakes Entrance | 3435.0 | 2175.7 | -2134.7 | -27.3 | 3490.0 | -2203 |
| Top of Latrobe Group | 3770.5 | 2346.2 | -2305.2 | -0.8 | 3774.0 | -2347 |
| Top Coarse Clastics | 3772.5 | 2347.2 | -2306.2 | -0.8 | 3776.0 | -2348 |
| Top M112 Reservoir | 3824.0 | 2373.3 | -2332.3 | -6.7 | 3839.0 | -2380 |
| Top M131 Reservoir | 3828.0 | 2375.3 | -2334.3 | -6.7 | 3843.0 | -2382 |
| Top M132 Upper Reservoir | 3857.5 | 2390.2 | -2349.2 | -7.8 | 3875.0 | -2398 |
| Top M132 Lower Reservoir | 3869.0 | 2396.1 | -2355.1 | -6.9 | 3885.0 | -2403 |
| Top M141 Reservoir |  |  |  |  | 3904.0 | -2413 |
| Top M145 Reservoir |  |  |  |  | 3938.0 | -2430 |
| Original Oil Water Contact |  |  |  |  | 3954.0 | -2438 |
| Total Depth |  |  |  |  | 4014.0 | -2468 |

| Current Formation | Latrobe Group |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3830.0 | 78.0 | 0.454 | 0.171 | 0.130 | 0.089 | 0.030 | 0 |
| MAX (GFF) | 3830.0 | 56.0 | 0.381 | 0.138 | 0.103 | 0.076 | 0.027 | 0 |
| BG (Reserval) | 3423.0-3860.0 | 16.4 | 0.153 | 0.025 | 0.017 | 0.011 | 0.004 | - |
| BG (GFF) | 3423.0-3860.0 | 13.2 | 0.149 | 0.013 | 0.015 | 0.011 | 0.004 | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 4 | 3 |
| SIZE (in) | 9.875 | 14.75 |
| MANUFACTURER/TYPE | REED / RSX61M-A14 | REED / Mill Tooth |
| JETS (/32 inch) | 6 x 15 | 3 x 20, 1 x 18 |
| DEPTH IN (m) | 587.0 | 229.0 |
| DEPTH OUT (m) | - | 587.0 |
| METRES ON RUN (m) | 3273.0 | 358.0 |
| HRS ON BTM 24hrs/total | 14.1 / 85.6 | - /3.1 |
| BIT CONDITION | - | I-I-WT-A-E-In-No-TD |
| RPM RANGE 24hrs | 89-165 | - |
| Pump Hrs 24 hrs / total | 20.1 / 120.5 | - /10.7 |
| Krevs 24 hrs / total | 115 / 717 | - / 4 |

| 24 HOUR SUMMARY | Drill ahead 9-7/8” hole as per Schlumberger instructions from 3423.0 mMDRT to 3487.0 mMDRT. Work string and monitor well on trip tank whilst making repairs to Scomi’s equipment. Drill ahead 9-7/8” hole as per Schlumberger instructions from 3487.0 mMDRT to 3616.0 mMDRT. Control drill at 50 m/hr from 3616.0 mMDRT to 3631.0 mMDRT. Pick up off bottom and circulate at reduced rate whilst working on Scomi’s equipment. Drill ahead 9-7/8” hole as per Schlumberger instructions from 3631.0 mMDRT to 3646.0 mMDRT. Circulate up bottoms up at 3646.0 mMDRT and take Slow Circulation Rates prior to entering the Latrobe Group. Drill ahead 9-7/8” hole as per Schlumberger instructions from 3646.0 mMDRT to 3696.0 mMDRT. Work string at 3696.0 mMDRT whilst working on Scomi’s equipment. Drill ahead 9-7/8” hole as per Schlumberger instructions from 3696.0 mMDRT to 3860.0 mMDRT. |
| --- | --- |
| 15-07-2009 5 AM UPDATE | Drill ahead 9-7/8” hole as per Schlumberger instructions from 3860.0 mMDRT to 3900.0 mMDRT. 5AM DEPTH: 3900.0 mMDRT: 2407.32 mTVDRT |