Culverin-1

| Date: | 31-12-2005 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 12 | Leak Off Test: | 1.89 sg EMW @ 1528.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 311 mm (12 1/4”) |
| Depth @ 2400 Hrs: | 3473.0 mMDRT | Mud Weight: | 1.22 sg |
| Last Depth: | 3402.0 mMDRT | ECD: | 1.22 sg |
| Progress: | 71 m | Mud Type: | KCl-NaCl-Polymer |
| TD Lithology: | Argillaceous Sandstone, Siltstone and Coal | Mud Chlorides: | 82, 000 ppm |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 3.6 cc |
| RT Elevation: | 21.5 m | Bit Type: | PDC (Reed-Hycalog) |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | RIH to 3330.0 mMDRT. Logged down over sandstone at 3340.0 mMDRT. Reamed down to bottom. Commenced drilling ahead from 3402.0 mMDRT. Drilling ahead at 3473.0 mMDRT at midnight. |
| --- | --- |
| 06:00 Update | Drilling ahead at 3524.0 mMDRT. |
| NEXT 24 HOURS: | Drill ahead 311 mm (12 ¼”) hole. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
| 3400 - 3410 ROP 1.56 – 44.3 m/hr Ave 19.9 m/hr | Siltstone with interbedded Sandy Claystone and minor Coal SILTSTONE (70-90%): light brownish grey to brownish grey, soft to firm, sub-blocky to amorphous, abundant carbonaceous specks, very argillaceous, disseminated pyrite in part, no fluorescence. SANDY CLAYSTONE (10-30%): very light grey to white, occasionally greenish-white, soft to firm, amorphous to sub-blocky, trace lithics, 5-20% fine, well rounded quartz sand, grading into Argillaceous Sandstone, quite calcareous in part, no fluorescence. COAL (Trace): black to dark brown, soft to firm, dull to bright, rare conchoidal fracture, commonly laminated, grading into carbonaceous siltstone, firmly pyrite cemented in part. |
| 3410-3430 ROP 1.1 – 65.9 m/hr Ave 22.6 m/hr | Argillaceous Sandstone with interbedded Siltstone ARGILLACEOUS SANDSTONE (40-70%): white to pale grey in aggregates, mainly loose, clear to translucent when loose, friable when in rare aggregates, fine to coarse grained, mainly medium grained, poorly sorted, sub-angular to angular, abundant white argillaceous clay matrix, generally non-calcareous matrix, poor inferred visual porosity, trace pyrite, trace carbonaceous fragments and laminations, trace firm calcite cement fragments, no fluorescence. SILTSTONE (30-60%): light grey to light brownish grey, soft to firm, sub-blocky to amorphous, abundant carbonaceous specks, very argillaceous, disseminated pyrite in part, no fluorescence. |
| 3430-3475 ROP 1 – 40 m/hr Ave 11 m/hr | Siltstone with minor Argillaceous Sandstone and trace Coal ARGILLACEOUS SANDSTONE (10-30%): clear to translucent, loose, very fine to coarse grained, mainly fine grained, very poorly sorted, sub-angular to angular, abundant white argillaceous matrix, trace pyrite, trace carbonaceous specks, poor to moderate visual inferred porosity, no hydrocarbon fluorescence. SILTSTONE (70-90%): light brownish grey to brownish grey, soft to firm, sub-blocky to amorphous, abundant carbonaceous specks, grading into carbonaceous siltstone, very argillaceous, disseminated pyrite in part, no fluorescence. COAL (Trace): black to dark brown, soft to firm, dull to bright lustre, rare conchoidal fracture, commonly laminated, grading into carbonaceous siltstone. |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
|  | Nil. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | C5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3400-3410 | 0.15 | 2028 | 778 | 53 | 31 | 35 | 24 |
| 3410-3430 | 0.12 | 630 | 77 | 43 | 26 | 30 | 9 |
| 3430-3475 | 0.186 | 876 | 150 | 82 | 33 | 43 | 47 |
| 3436 PEAK | 0.28 | 1715 | 207 | 108 | 32 | 43 | 44 |
| 3469 PEAK | 0.308 | 1849 | 261 | 124 | 54 | 52 | 44 |
| 3473 PEAK | 0.324 | 2435 | 255 | 90 | 31 | 38 | 37 |

- SURVEYS

| MD | ANGLE | Azi |  | MD | ANGLE | Azi |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2285.35 | 4.14 | 37.21 |  | 2887.70 | 3.86 | 45.65 |  |  |
| 2314.02 | 4.15 | 34.69 |  | 2916.43 | 3.87 | 45.26 |  |  |
| 2342.60 | 4.24 | 35.48 |  | 2944.96 | 3.83 | 45.79 |  |  |
| 2371.30 | 4.20 | 37.23 |  | 2973.53 | 3.73 | 46.71 |  |  |
| 2399.91 | 4.28 | 37.06 |  | 3002.19 | 3.72 | 46.75 |  |  |
| 2428.46 | 4.30 | 38.32 |  | 3059.49 | 3.72 | 46.57 |  |  |
| 2457.14 | 4.30 | 37.54 |  | 3088.21 | 3.81 | 46.46 |  |  |
| 2511.27 | 4.09 | 38.40 |  | 3116.08 | 3.75 | 45.37 |  |  |
| 2543.24 | 4.05 | 40.48 |  | 3145.07 | 3.74 | 48.33 |  |  |
| 2572.00 | 4.01 | 40.97 |  | 3173.79 | 3.67 | 49.59 |  |  |
| 2600.65 | 3.91 | 40.54 |  | 3202.65 | 3.71 | 48.97 |  |  |
| 2629.39 | 3.86 | 40.58 |  | 3231.77 | 3.53 | 48.2 |  |  |
| 2658.02 | 3.89 | 41.3 |  | 3260.37 | 3.66 | 49.86 |  |  |
| 2686.60 | 3.77 | 41.46 |  | 3346.36 | 3.65 | 50.41 |  |  |
| 2715.15 | 3.77 | 40.42 |  | 3375.03 | 3.69 | 54.03 |  |  |
| 2743.83 | 3.80 | 42.10 |  | 3404.40 | 3.54 | 54.90 |  |  |
| 2772.65 | 3.83 | 43.73 |  | 3432.80 | 3.59 | 51.96 |  |  |
| 2801.66 | 3.84 | 42.76 |  | 3461.32 | 3.48 | 51.53 |  |  |
| 2830.44 | 3.89 | 43.81 |  | 3490.24 | 3.38 | 50.31 |  |  |
| 2859.14 | 3.95 | 44.31 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | TVDSS | THICK | MDKB | TVDSS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 607 | 585 | 1975 | 606.5 | 585.0 | 0.0 | 1899.9 | 0.0 |
| Lakes Entrance | 2582.0 | 2560.0 | 325 | 2508.0 | 2484.9 | 75.1 H | 315.1 | -10.0 |
| Latrobe | 2907.0 | 2885.0 | 30 | 2824.0 | 2800.0 | 85.0 H | 11.0 | -19.0 |
| Base TF Channel | 2937.0 | 2915.0 | 10 | 2835.0 | 2811.0 | 104.0 H | 1.0 | -8.0 |
| Top 67.5 Ma Sand | 2947.0 | 2925.0 | 310 | 2836.0 | 2812.0 | 113.0 H | 266.5 | -43.5 |
| Near 68.5 Ma Sand | 3257.0 | 3235.0 | 226 | 3103.0 | 3078.5 | 156.5 H | 374.3 | -148.3 |
| Near 70.3 Ma Sand | 3482.5 | 3461.0 |  | 3478 | 3452.8 | 8.2 H |  |  |
| Near 74 Ma Sand | Not prog |  |  |  |  |  |  |  |
| TD | 3612.0 | 3590.0 |  |  |  |  |  |  |

- COMMENTS:

Sperry-Sun LWD sensor to bit distances: (same LWD toolstring run following bit trip)

Directional = 13.13 m

Gamma-Ray = 15.73 m

Resistivity = 18.04 m

Density = 25.66 m

Porosity = 30.97 m

ACAL = 29.93 m

Trip Gas recorded following bit trip at 3402 mMDRT

21 Units TG over a background of 6 Units TG @ 3400.0 mMDRT.

C1 = 2772 ppm C2 =   379 ppm C3 =    76 ppm IC4 =   43 ppm

NC4 = 45 ppm C5 = 137 ppm