Culverin-1

| Date: | 2-01-2006 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 14 | Leak Off Test: | 1.89 sg EMW @ 1528.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 311 mm (12 1/4”) |
| Depth @ 2400 Hrs: | 3571.0 mMDRT | Mud Weight: | 1.22 sg |
| Last Depth: | 3571.0 mMDRT | ECD: | 1.22 sg |
| Progress: | 0 m | Mud Type: | KCl-NaCl-Polymer |
| TD Lithology: | Siltstone | Mud Chlorides: | 82, 000 ppm |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 3.6 cc |
| RT Elevation: | 21.5 m | Bit Type: | Smith Rock-bit |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | POOH to surface. Changed out BHA to a rotary assembly (removed down-hole motor) and a Smith rock-bit. Completed making up new BHA with additional drill-collars and commenced RIH. BHA held up at 2100.0 mMDRT. Washed and reamed down to 2540.0 mMDRT. MWD failed at 2540.0 mMDRT. Commenced pulling out of hole to replace MWD tools and adjust BHA configuration. Pulling out at 2020.0 mMDRT at midnight. |
| --- | --- |
| 06:00 Update | Pulling out of hole (06:00hrs at the BHA) to replace MWD tools and adjust the BHA. |
| NEXT 24 HOURS: | Change out MWD tools, adjust BHA configuration and RIH again to drill ahead 311 mm (12 ¼”) hole. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
|  | No cuttings returned |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
|  | Nil. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | C5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| No drilling. |  |  |  |  |  |  |  |

- SURVEYS

| MD | ANGLE | Azi |  | MD | ANGLE | Azi |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2743.83 | 3.80 | 42.10 |  | 3375.03 | 3.69 | 54.03 |  |  |
| 2772.65 | 3.83 | 43.73 |  | 3404.40 | 3.54 | 54.90 |  |  |
| 2801.66 | 3.84 | 42.76 |  | 3432.80 | 3.59 | 51.96 |  |  |
| 2830.44 | 3.89 | 43.81 |  | 3461.32 | 3.48 | 51.53 |  |  |
| 2859.14 | 3.95 | 44.31 |  | 3490.24 | 3.38 | 50.31 |  |  |
| 2887.70 | 3.86 | 45.65 |  | 3519.26 | 3.32 | 50.11 |  |  |
| 2916.43 | 3.87 | 45.26 |  | 3547.59 | 3.32 | 49.95 |  |  |
| 2944.96 | 3.83 | 45.79 |  |  |  |  |  |  |
| 2973.53 | 3.73 | 46.71 |  |  |  |  |  |  |
| 3002.19 | 3.72 | 46.75 |  |  |  |  |  |  |
| 3059.49 | 3.72 | 46.57 |  |  |  |  |  |  |
| 3088.21 | 3.81 | 46.46 |  |  |  |  |  |  |
| 3116.08 | 3.75 | 45.37 |  |  |  |  |  |  |
| 3145.07 | 3.74 | 48.33 |  |  |  |  |  |  |
| 3173.79 | 3.67 | 49.59 |  |  |  |  |  |  |
| 3202.65 | 3.71 | 48.97 |  |  |  |  |  |  |
| 3231.77 | 3.53 | 48.2 |  |  |  |  |  |  |
| 3260.37 | 3.66 | 49.86 |  |  |  |  |  |  |
| 3346.36 | 3.65 | 50.41 |  |  |  |  |  |  |
| 3375.03 | 3.69 | 54.03 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | TVDSS | THICK | MDKB | TVDSS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 607.0 | 585.0 | 1975.0 | 606.5 | 585.0 | 0.0 | 1899.9 | 0.0 |
| Lakes Entrance | 2582.0 | 2560.0 | 325.0 | 2508.0 | 2484.9 | 75.1 H | 315.1 | -10.0 |
| Latrobe | 2907.0 | 2885.0 | 30.0 | 2824.0 | 2800.0 | 85.0 H | 11.0 | -19.0 |
| Base TF Channel | 2937.0 | 2915.0 | 10.0 | 2835.0 | 2811.0 | 104.0 H | 1.0 | -8.0 |
| Top 67.5 Ma Sand | 2947.0 | 2925.0 | 310.0 | 2836.0 | 2812.0 | 113.0 H | 266.5 | -43.5 |
| Near 68.5 Ma Sand | 3257.0 | 3235.0 | 226.0 | 3103.0 | 3078.5 | 156.5 H | 374.3 | -148.3 |
| Near 70.3 Ma Sand | 3482.5 | 3461.0 |  | 3478.0 | 3452.8 | 8.2 H |  |  |
| Near 74 Ma Sand | Not prog |  |  |  |  |  |  |  |
| TD | 3612.0 | 3590.0 |  |  |  |  |  |  |

- COMMENTS:

Sperry-Sun LWD sensor to bit distances: (note new sensor offsets with new rotary BHA)

Directional = 8.50 m

Gamma-Ray = 11.11 m

Resistivity = 13.41 m

Density = 21.03 m

Porosity = 26.35 m

ACAL = 25.31 m