Culverin-1

| Date: | 4-01-2006 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 16 | Leak Off Test: | 1.89 sg EMW @ 1528.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 311 mm (12 1/4”) |
| Depth @ 2400 Hrs: | 3619.0 mMDRT | Mud Weight: | 1.21 sg |
| Last Depth: | 3571.0 mMDRT | ECD: | 1.22 sg |
| Progress: | 48 m | Mud Type: | KCl-NaCl-Polymer |
| TD Lithology: | Sandstone, Siltstone, Coal | Mud Chlorides: | 78, 000 ppm |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 3.8 cc |
| RT Elevation: | 21.5 m | Bit Type: | Smith Rock-bit |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | RIH to bottom and began drilling ahead 311 mm (12 ¼”) hole from 3571.0 mMDRT. Drilling ahead at 3619.0 mMDRT at midnight. |
| --- | --- |
| 06:00 Update | Drilling ahead 311 mm (12 ¼”) hole at 3643.0 mMDRT. |
| NEXT 24 HOURS: | Drill ahead 311 mm (12 ¼”) hole. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
| 3565 - 3590 ROP 1.1 – 20.0 m/hr Ave 5.6 m/hr | Interbedded Siltstone and Claystone with minor Argillaceous Sandstone and thin Coals ARGILLACEOUS SANDSTONE (5-20%): white to very light grey with carbonaceous laminations, firm to friable, very fine to fine, occasional medium grains, moderately well-sorted, sub-angular to rounded, white argillaceous matrix to 60% (weathered feldspars?), moderate inferred visual porosity, trace pyrite, abundant carbonaceous specks and laminae, glowing white residual crush cut fluorescence inferred to be from carbonaceous material, no hydrocarbon fluorescence noted from clean sand fragments. SILTSTONE (50-80%): light brownish grey to brownish grey, occasionally white, very soft to firm, amorphous to laminated, argillaceous, common carbonaceous specks and carbonaceous laminae, occasionally pyritic, trace very hard black & white finely banded siliceous fragments, grading occasionally into brown claystone. CLAYSTONE (0-40%): very light greenish-grey, firm to moderately hard, sub-blocky to fissile, occasionally splintery shaped fragments, trace glauconite?, trace silty quartz grains, calcareous in nature. COAL (Trace-5%): black, dull black, sub vitreous, firm, blocky, silty in part. |
| 3590 - 3620 ROP 1.2 – 19 m/hr Ave 3.7 m/hr | Interbedded Sandstone and Siltstone with thin Coals SANDSTONE (30-40%): white to very light grey in aggregate form, very firm to firm, occasionally very well cemented with quartz overgrowths, very fine to coarse white to yellowish grains when loose, occasional granular grains, mainly medium-grained, poorly-sorted, sub-angular to angular, abundant white argillaceous and calcareous matrix (weathered feldspars? and calcite cement), silica cemented with quartz overgrowths in part, poor inferred visual porosity, trace pyrite, trace fractured grains, common black and dark brown carbonaceous/woody specks, pale yellow mineral fluorescence from various cements, no hydrocarbon fluorescence. SILTSTONE (60-70%): light brownish grey to brownish grey, occasionally dark brown, soft to firm, amorphous to laminated, argillaceous, common black and dark brown carbonaceous/woody specks and carbonaceous laminae, occasionally pyritic. COAL (Trace): black to very dark brown, hard to very hard, sub-blocky to splintery, dull to bright with vitreous lustre and conchoidal fracture, commonly pyritised. |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
| 3575 - 3580 | Moderately bright, very slow, diffuse, white, crush cut fluorescence (inferred to be from carbonaceous material associated with thin fine sand stringers), thin white residual ring. No direct UV or crush-cut UV hydrocarbon fluorescence noted from clean sand fragments. |
| 3585 - 3590 | Trace weak pale yellowish direct UV fluorescence from carbonaceous laminations. |
| 3590 - 3595 | Pale yellow direct UV fluorescence from calcite-cemented sandstone fragments, no hydrocarbon fluorescence. |
| 3605 - 3620 | Pale yellow direct UV fluorescence from silica and calcareous cemented sandstone fragments, no hydrocarbon fluorescence. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | C5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3565-3590 | 1.0 | 8183 | 595 | 229 | 60 | 57 | 18 |
| 3590 - 3620 | 0.72 | 5086 | 455 | 202 | 53 | 60 | 52 |
| 3582.0 (Peak) | 3.06 | 24035 | 1391 | 371 | 109 | 80 | 15 |
| 3596.5 (Peak) Coal | 4.67 | 35647 | 2135 | 599 | 145 | 130 | 22 |
| 3608.0 (Peak) Coal | 5.43 | 32568 | 3929 | 2084 | 344 | 503 | 124 |

- SURVEYS

| MD | ANGLE | Azi |  | MD | ANGLE | Azi |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2743.83 | 3.80 | 42.10 |  | 3375.03 | 3.69 | 54.03 |  |  |
| 2772.65 | 3.83 | 43.73 |  | 3404.40 | 3.54 | 54.90 |  |  |
| 2801.66 | 3.84 | 42.76 |  | 3432.80 | 3.59 | 51.96 |  |  |
| 2830.44 | 3.89 | 43.81 |  | 3461.32 | 3.48 | 51.53 |  |  |
| 2859.14 | 3.95 | 44.31 |  | 3490.24 | 3.38 | 50.31 |  |  |
| 2887.70 | 3.86 | 45.65 |  | 3519.26 | 3.32 | 50.11 |  |  |
| 2916.43 | 3.87 | 45.26 |  | 3547.59 | 3.32 | 49.95 |  |  |
| 2944.96 | 3.83 | 45.79 |  | 3555.34 | 3.36 | 53.74 |  |  |
| 2973.53 | 3.73 | 46.71 |  | 3583.83 | 3.00 | 50.85 |  |  |
| 3002.19 | 3.72 | 46.75 |  |  |  |  |  |  |
| 3059.49 | 3.72 | 46.57 |  |  |  |  |  |  |
| 3088.21 | 3.81 | 46.46 |  |  |  |  |  |  |
| 3116.08 | 3.75 | 45.37 |  |  |  |  |  |  |
| 3145.07 | 3.74 | 48.33 |  |  |  |  |  |  |
| 3173.79 | 3.67 | 49.59 |  |  |  |  |  |  |
| 3202.65 | 3.71 | 48.97 |  |  |  |  |  |  |
| 3231.77 | 3.53 | 48.2 |  |  |  |  |  |  |
| 3260.37 | 3.66 | 49.86 |  |  |  |  |  |  |
| 3346.36 | 3.65 | 50.41 |  |  |  |  |  |  |
| 3375.03 | 3.69 | 54.03 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | TVDSS | THICK | MDKB | TVDSS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 607.0 | 585.0 | 1975.0 | 606.5 | 585.0 | 0.0 | 1899.9 | 0.0 |
| Lakes Entrance | 2582.0 | 2560.0 | 325.0 | 2508.0 | 2484.9 | 75.1 H | 315.1 | -10.0 |
| Latrobe | 2907.0 | 2885.0 | 30.0 | 2824.0 | 2800.0 | 85.0 H | 11.0 | -19.0 |
| Base TF Channel | 2937.0 | 2915.0 | 10.0 | 2835.0 | 2811.0 | 104.0 H | 1.0 | -8.0 |
| Top 67.5 Ma Sand | 2947.0 | 2925.0 | 310.0 | 2836.0 | 2812.0 | 113.0 H | 266.5 | -43.5 |
| Near 68.5 Ma Sand | 3257.0 | 3235.0 | 226.0 | 3103.0 | 3078.5 | 156.5 H | 374.3 | -148.3 |
| Near 70.3 Ma Sand | 3482.5 | 3461.0 |  | 3478.0 | 3452.8 | 8.2 H |  |  |
| Near 74 Ma Sand | Not prog |  |  |  |  |  |  |  |
| TD | 3612.0 | 3590.0 |  |  |  |  |  |  |

- COMMENTS:

Sperry-Sun LWD sensor to bit distances: (note new sensor offsets with new tools)

Gamma Ray:  16.17m

Resistivity:   18.53m

Density:       26.13m

Porosity:      31.43m

Directional : 13.55m

Caliper :       30.39m