Culverin-1

| Date: | 5-01-2006 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 17 | Leak Off Test: | 1.89 sg EMW @ 1528.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 311 mm (12 1/4”) |
| Depth @ 2400 Hrs: | 3697.0 mMDRT | Mud Weight: | 1.21 sg |
| Last Depth: | 3619.0 mMDRT | ECD: | 1.22 sg |
| Progress: | 78 m | Mud Type: | KCl-NaCl-Polymer |
| TD Lithology: | Sandstone, Siltstone, Coal | Mud Chlorides: | 79, 000 ppm |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 3.6 cc |
| RT Elevation: | 21.5 m | Bit Type: | Smith Rock-bit |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | Drilled ahead from 3619.0 mMDRT to 3697.0 mMDRT at midnight. |
| --- | --- |
| 06:00 Update | Drilling ahead 311 mm (12 ¼”) hole at 3718.0 mMDRT. LWD has failed deepest GR recorded 3699m. |
| NEXT 24 HOURS: | Drill ahead 311 mm (12 ¼”) hole. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
| 3620 - 3650 ROP 1.2 – 16.8 m/hr Ave 2.5 m/hr | Interbedded Sandstone, Siltstone and Coal SANDSTONE (15-65%): white to very light grey in aggregate form, occasionally clear to white when in loose grains, firm to very well cemented in part, blocky to massive, very fine to medium grained, mainly fine-grained, moderately-sorted, sub-angular to angular, common white argillaceous matrix (weathered feldspars?), common quartz overgrowths cementing sandstone, common calcareous cement, poor inferred visual porosity, common pyrite both as cement and in nodular form, trace fractured grains, trace carbonaceous specks and laminations, common pale yellow-dull orange mineral fluorescence from calcite & silica(?) cement, no hydrocarbon fluorescence. SILTSTONE (30-80%): light brownish grey, very light brownish grey, soft to very firm, argillaceous, amorphous to laminated, common carbonaceous specks and laminae, occasional pyrite, gradational to Carbonaceous Siltstone. COAL (Trace-5%): dull black, firm, brittle in part, sub vitreous to rarely vitreous in patches, occasionally pyritic. |
| 3650 – 3667 ROP 1.5 – 9.6 m/hr Ave 4.1 m/hr | Dominantly Siltstone with minor Sandstone and thin Coal SANDSTONE (20-30%): white to very light grey in aggregate form, occasionally clear to white when in loose grains, firm to well-cemented in part, blocky to massive, very fine to medium grained, mainly fine-grained, poorly to moderately-sorted, sub-angular to angular, trace white argillaceous matrix (weathered feldspars?), trace quartz overgrowths, trace calcareous cement, poor inferred visual porosity, trace carbonaceous specks and laminations, trace pale yellow-dull orange mineral fluorescence from calcite(?) cemented fragments, no hydrocarbon fluorescence. SILTSTONE (70-80%): brownish grey to very light brownish grey, occasionally dark brown, soft to very firm, argillaceous, common fine quartz grains, amorphous to laminated, common carbonaceous specks and laminae, occasional pyrite, grading into Carbonaceous Siltstone. COAL (Trace): dull black, firm, brittle in part, sub vitreous to rarely vitreous in patches, occasionally pyritic. |
| 3667 – 3697 ROP 1.1 – 14.5 m/hr Ave 3.0 m/hr | Interbedded Sandstone Siltstone and Coal SANDSTONE: white to very light grey, dominantly soft to friable aggregates, also loose grains, very fine to fine, occasional medium grains, sub angular to well rounded, moderately will sorted, 5 – 80% white argillaceous matrix, occasional carbonaceous grains and siltstone lithics, poor to fair porosity, no fluorescence. SILTSTONE: light brownish grey, very soft to sub firm, amorphous to sub blocky, occasionally sub fissile when carbonaceous, commonly carbonaceous grains and laminae, very argillaceous, trace pyrite, intercalated with very fine sandstone. COAL: dull black, sub vitreous, firm, brittle in part, hackly fracture, silty. |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
| 3620 – 3625 | Trace – 5% dull yellow mineral fluorescence from the calcareous cement. |
| 3625 – 3630 | Trace – 10% dull yellow mineral fluorescence from the calcareous cement. |
| 3645 – 3650 | Common (5%) pale yellow-dull orange mineral fluorescence from calcite/silica cement, no hydrocarbon fluorescence. |
| 3670 – 3690 | Trace pale yellow-dull orange calcite/silica? Mineral fluorescence. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | C5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3620 -3650 | 0.96 | 6049 | 693 | 431 | 99 | 150 | 43 |
| 3650- 3667 | 0.82 | 6625 | 637 | 360 | 91 | 132 | 99 |
| 3667 - 3697 | 0.44 | 2345 | 276 | 197 | 66 | 86 | 80 |

- SURVEYS

| MD | ANGLE | Azi |  | MD | ANGLE | Azi |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2743.83 | 3.80 | 42.10 |  | 3375.03 | 3.69 | 54.03 |  |  |
| 2772.65 | 3.83 | 43.73 |  | 3404.40 | 3.54 | 54.90 |  |  |
| 2801.66 | 3.84 | 42.76 |  | 3432.80 | 3.59 | 51.96 |  |  |
| 2830.44 | 3.89 | 43.81 |  | 3461.32 | 3.48 | 51.53 |  |  |
| 2859.14 | 3.95 | 44.31 |  | 3490.24 | 3.38 | 50.31 |  |  |
| 2887.70 | 3.86 | 45.65 |  | 3519.26 | 3.32 | 50.11 |  |  |
| 2916.43 | 3.87 | 45.26 |  | 3547.59 | 3.32 | 49.95 |  |  |
| 2944.96 | 3.83 | 45.79 |  | 3555.34 | 3.36 | 53.74 |  |  |
| 2973.53 | 3.73 | 46.71 |  | 3583.83 | 3.00 | 50.85 |  |  |
| 3002.19 | 3.72 | 46.75 |  | 3641.38 | 2.98 | 50.16 |  |  |
| 3059.49 | 3.72 | 46.57 |  |  |  |  |  |  |
| 3088.21 | 3.81 | 46.46 |  |  |  |  |  |  |
| 3116.08 | 3.75 | 45.37 |  |  |  |  |  |  |
| 3145.07 | 3.74 | 48.33 |  |  |  |  |  |  |
| 3173.79 | 3.67 | 49.59 |  |  |  |  |  |  |
| 3202.65 | 3.71 | 48.97 |  |  |  |  |  |  |
| 3231.77 | 3.53 | 48.2 |  |  |  |  |  |  |
| 3260.37 | 3.66 | 49.86 |  |  |  |  |  |  |
| 3346.36 | 3.65 | 50.41 |  |  |  |  |  |  |
| 3375.03 | 3.69 | 54.03 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | TVDSS | THICK | MDKB | TVDSS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 607.0 | 585.0 | 1975.0 | 606.5 | 585.0 | 0.0 | 1899.9 | 0.0 |
| Lakes Entrance | 2582.0 | 2560.0 | 325.0 | 2508.0 | 2484.9 | 75.1 H | 315.1 | -10.0 |
| Latrobe | 2907.0 | 2885.0 | 30.0 | 2824.0 | 2800.0 | 85.0 H | 11.0 | -19.0 |
| Base TF Channel | 2937.0 | 2915.0 | 10.0 | 2835.0 | 2811.0 | 104.0 H | 1.0 | -8.0 |
| Top 67.5 Ma Sand | 2947.0 | 2925.0 | 310.0 | 2836.0 | 2812.0 | 113.0 H | 266.5 | -43.5 |
| Near 68.5 Ma Sand | 3257.0 | 3235.0 | 226.0 | 3103.0 | 3078.5 | 156.5 H | 374.3 | -148.3 |
| Near 70.3 Ma Sand | 3482.5 | 3461.0 |  | 3478.0 | 3452.8 | 8.2 H |  |  |
| Near 74 Ma Sand | Not prog |  |  |  |  |  |  |  |
| TD | 3612.0 | 3590.0 |  |  |  |  |  |  |

- COMMENTS:

Sperry-Sun LWD sensor to bit distances: (note new sensor offsets with new tools)

Gamma Ray:  16.17m

Resistivity:   18.53m

Density:       26.13m

Porosity:      31.43m

Directional : 13.55m

Caliper :       30.39m