Culverin-1

| Date: | 21-12-2005 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 2 | Form. Integrity Test: | N/A |
| Report Period: | 24hrs to 24:00 | Current hole size: | 445 mm (17 ½”) |
| Depth @ 2400 Hrs: | 1525.0 mMDRT | Mud Weight: | 1.03 sg |
| Last Depth: | 1525.0 mMDRT | ECD: | N/A |
| Progress: | 0 m | Mud Type: | Seawater/Gel sweeps |
| TD Lithology: | N/A drilled riser-less | Mud Chlorides: | 600 mg/l |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 14 cc |
| RT Elevation: | 21.5 m | Bit Type: | N/A |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | Ran casing in on drill-pipe. Landed 340mm casing at 1511.14 mMDRT. Cemented casing. Laid out cement head. Rigged up riser-handling equipment. Commenced running BOPs and riser. |
| --- | --- |
| 06:00 Update | Running riser. |
| NEXT 24 HOURS: | Run BOPs and riser. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
|  | No returns to surface. |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
|  | No returns to surface. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (%) | C2 (%) | C3 (%) | IC4 (%) | NC4 (%) | C5 (%) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| No returns to surface |  |  |  |  |  |  |  |

- SURVEYS

| MD | ANGLE | Azi |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 681.95 | 1.26 | 227.0 |  |  |  |  |  |  |
| 767.68 | 0.81 | 263.55 |  |  |  |  |  |  |
| 825.04 | 0.93 | 254.57 |  |  |  |  |  |  |
| 911.19 | 1.09 | 257.49 |  |  |  |  |  |  |
| 1027.78 | 0.85 | 252.60 |  |  |  |  |  |  |
| 1056.46 | 0.79 | 254.04 |  |  |  |  |  |  |
| 1085.16 | 0.77 | 260.55 |  |  |  |  |  |  |
| 1113.81 | 0.62 | 255.11 |  |  |  |  |  |  |
| 1142.54 | 0.51 | 257.73 |  |  |  |  |  |  |
| 1171.11 | 0.43 | 257.64 |  |  |  |  |  |  |
| 1228.35 | 0.22 | 250.90 |  |  |  |  |  |  |
| 1257.08 | 0.17 | 244.39 |  |  |  |  |  |  |
| 1342.79 | 0.06 | 257.65 |  |  |  |  |  |  |
| 1371.46 | 0.03 | 247.14 |  |  |  |  |  |  |
| 1428.75 | 0.11 | 336.43 |  |  |  |  |  |  |
| 1486.03 | 0.16 | 21.18 |  |  |  |  |  |  |
| 1509.77 | 0.09 | 0.70 |  |  |  |  |  |  |
| 1525.00 | 0.09 | 0.70 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | SS | THICK | MDKB | SS | HI/LO | THICK | DIFF |
| Sea Floor | 607 | 585 | - | 606.5 | 585.0 | 0.0 | - | 0.0 |
| Lakes Entrance | 2582 | 2560 |  |  |  |  |  |  |
| Latrobe | 2907 | 2885 |  |  |  |  |  |  |
| Base TF Channel | 2937 | 2915 |  |  |  |  |  |  |
| Top 67.5 Ma Sand | 2947 | 2925 |  |  |  |  |  |  |
| Near 68.5 Ma Sand | 3257 | 3235 |  |  |  |  |  |  |
| Near 70.3 Ma Sand | 3542 | 3520 |  |  |  |  |  |  |
| TD | 3612 | 3590 |  |  |  |  |  |  |