Culverin-1

| Date: | 26-12-2005 | Last Casing: | 340 mm (13 3/8”) @ 1511.14 mMDRT |
| --- | --- | --- | --- |
| Report Number: | 7 | Leak Off Test: | 1.89 sg EMW @ 1528.0 mMDRT |
| Report Period: | 24hrs to 24:00 | Current hole size: | 311 mm (12 1/4”) |
| Depth @ 2400 Hrs: | 2641.0 mMDRT | Mud Weight: | 1.20 sg |
| Last Depth: | 2131.0 mMDRT | ECD: | 1.21 sg |
| Progress: | 510 m | Mud Type: | KCl-NaCl-Polymer |
| TD Lithology: | Calcareous Claystone | Mud Chlorides: | 36,000 ppm |
| Water Depth: | 585.0 m | Mud Fluid Loss: | 5.4 cc |
| RT Elevation: | 21.5 m | Bit Type: | PDC (Reed-Hycalog) |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 00:00 - 24:00: | Drilled ahead from 2131.0 mMDRT to 2641.0 mMDRT. Top of the Lakes Entrance Formation picked from LWD logs and cuttings at 2508.0 mMDRT. |
| --- | --- |
| 06:00 Update | Drilling ahead at 2758 mMDRT in the Lakes Entrance Formation. |
| NEXT 24 HOURS: | Drill ahead 311 mm (12 ¼”) hole. |

GEOLOGICAL SUMMARY

- LITHOLOGIC DESCRIPTION:

| Interval mMDRT | Description |
| --- | --- |
| 2130 – 2190 ROP 14 – 49 m/hr Ave 26 m/hr | Massive Calcilutite becoming more silty with depth CALCLUTITE (100%): light olive grey, occasionally light brownish grey, rare medium grey patches, very soft to rarely firm, sub-blocky to amorphous, common calcareous silt and very fine calcareous sand, trace carbonaceous specks, trace microfossils, trace very fine pyrite associated with organic matter. Gradational in part to CALCISILTITE. |
| 2190 – 2340 ROP 12 – 57m/hr Ave 24 m/hr | Dominantly Calcilutite with minor Calcsiltite CALCLUTITE (80-100%): light olive grey, occasionally light brownish grey, rare medium grey patches, very soft to rarely firm, sub-blocky to amorphous, common calcareous silt and very fine calcareous sand, trace carbonaceous specks, trace microfossils, trace very fine pyrite. CALCISILTITE (Nil-20%): olive grey, brownish grey, soft to firm, friable in part, sub blocky, trace calcareous sand, trace carbonaceous specks. |
| 2340 - 2508 ROP 13 – 62m/hr Ave 29 m/hr | Dominantly Argillaceous Calcilutite with minor Calcsiltite and Calcarenite with rare fine glauconite grains ARGILLACEOUS CALCLUTITE (70-100%): light brownish grey, occasionally light grey, rare medium grey patches, very soft to rarely firm, sub-blocky to amorphous, common calcareous silt and very fine calcareous sand, trace carbonaceous specks, trace microfossils, trace very fine glauconite grains, trace very fine pyrite, 15% clay content. CALCISILTITE (Nil-20%): olive grey, brownish grey, soft to firm, friable in part, sub blocky, trace calcareous sand, trace carbonaceous specks. CALCARENITE (Nil-30%): light brownish-grey, firm to moderately hard, sub-blocky, very fine to fine grained, moderately well sorted, angular grains, common to abundant calcareous argillaceous matrix, common fine glauconite grains, poor visual porosity. |
| 2508 - 2640 ROP 16 – 120m/hr Ave 50 m/hr | Massive Calcareous Claystone CALCAREOUS CLAYSTONE (100%): light to medium grey, soft, sub blocky to blocky, trace very fine pyritic patches, occasional medium grey silty patches, rare carbonaceous specks. |

- HYDROCARBON FLUORESCENCE:

| INTERVAL (mMDRT) | FLUORESCENCE |
| --- | --- |
|  | Nil. |

- GAS SUMMARY:

| INTERVAL (mMDKB) | Total GAS (%) | C1 (ppm) | C2 (ppm) | C3 (ppm) | IC4 (ppm) | NC4 (ppm) | C5 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2130 - 2190 | 0.44 | 4350 | 23 | 18 | 29 | 1 | - |
| 2190 - 2340 | 0.37 | 3500 | 13 | 10 | 5 | 3 | - |
| 2340 - 2508 | 0.29 | 2905 | 10 | 9 | 7 | 3 | - |
| 2508 - 2640 | 0.12 | 950 | 12 | 10 | 38 | 5 | - |

- SURVEYS

| MD | ANGLE | Azi |  | MD | ANGLE | Azi |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2027.82 | 3.27 | 25.23 |  | 2629.39 | 3.86 | 40.58 |  |  |
| 2056.65 | 3.24 | 27.04 |  | 2658.02 | 3.89 | 41.3 |  |  |
| 2085.12 | 3.33 | 26.59 |  | 2686.60 | 3.77 | 41.46 |  |  |
| 3113.64 | 3.4 | 27.83 |  | 2715.15 | 3.77 | 40.42 |  |  |
| 2142.04 | 3.46 | 29.61 |  |  |  |  |  |  |
| 2170.63 | 3.6 | 30.30 |  |  |  |  |  |  |
| 2199.17 | 3.77 | 30.65 |  |  |  |  |  |  |
| 2227.87 | 3.85 | 36.05 |  |  |  |  |  |  |
| 2256.54 | 3.99 | 35.43 |  |  |  |  |  |  |
| 2285.35 | 4.14 | 37.21 |  |  |  |  |  |  |
| 2314.02 | 4.15 | 34.69 |  |  |  |  |  |  |
| 2342.60 | 4.24 | 35.48 |  |  |  |  |  |  |
| 2371.30 | 4.20 | 37.23 |  |  |  |  |  |  |
| 2399.91 | 4.28 | 37.06 |  |  |  |  |  |  |
| 2428.46 | 4.30 | 38.32 |  |  |  |  |  |  |
| 2457.14 | 4.30 | 37.54 |  |  |  |  |  |  |
| 2511.27 | 4.09 | 38.40 |  |  |  |  |  |  |
| 2543.24 | 4.05 | 40.48 |  |  |  |  |  |  |
| 2572.00 | 4.01 | 40.97 |  |  |  |  |  |  |
| 2600.65 | 3.91 | 40.54 |  |  |  |  |  |  |

- WELLSITE GEOLOGISTS:

| Mike Woodmansee | Rob Blackmore |
| --- | --- |

- FORMATION TOPS

| WD = 585.0 m RTE = 21.5 m |
| --- |
| FORMATION | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
|  | MDKB | SS | THICK | MDKB | SS | HI/LO | THICK | DIFF |
| Sea Floor/ Gippsland Limestone | 607 | 585 | - | 606.5 | 585.0 | 0.0 | 1899.9 | 0.0 |
| Lakes Entrance | 2582 | 2560 |  | 2508 | 2484.9 | 75.1H |  |  |
| Latrobe | 2907 | 2885 |  |  |  |  |  |  |
| Base TF Channel | 2937 | 2915 |  |  |  |  |  |  |
| Top 67.5 Ma Sand | 2947 | 2925 |  |  |  |  |  |  |
| Near 68.5 Ma Sand | 3257 | 3235 |  |  |  |  |  |  |
| Near 70.3 Ma Sand | 3542 | 3520 |  |  |  |  |  |  |
| TD | 3612 | 3590 |  |  |  |  |  |  |

- COMMENTS:

Sperry-Sun LWD sensor to bit distances:

Directional = 13.13 m

Gamma-Ray = 15.73 m

Resistivity = 18.04 m

Density = 25.66 m

Porosity = 30.97 m

ACAL = 29.93 m