| Date: | 20 August 2006 | Licence / State: | P39 (V) / VIC |
| --- | --- | --- | --- |
| Report Period: | 06:00 - 06:00 Hours | Rig: | Ensign 32 |
| Days from Spud: | 22 | GL: | 2.7m |
| Current Hole Size: | 8.5” | RT: | 8.6m |
| Depth @ 0600 Hrs: | 2250m MDRT | PTD: | 2281m MDRT (-1338mSS) |
|  | -1291m TVDSS | Spud Date: | 04:30 hrs 29/07/06 |
| 24 Hr Progress: | 170m |  |  |
| Current Operation: | Drilling 8.5” directional hole in the Latrobe N. Asperus at average 10 m/hr. |
| Nope Cost (Drill)$ | (C&S)$ |  | Cost To Date: |
|  | (P&A)$ |  |  |

| Casing Data | Hole Size | Depth | Casing Size | Wt: | Type | Shoe Depth | LOT |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (Conductor) |  | 100m | 20” | - | - | 60m |  |
|  | 17.5” | 320m | 13.375” | 54.5 | J55 BTC | 317m | EMW= 20.0 ppg |
|  | 12.25” | 1606m | 9.625” | 47.0 | N80 BTC | 1598m * | EMW= 16.7 ppg |

* 9.625m Casing Shoe revised to 1598m based on MWD log

| Mud Data | Type: | Wt: | Visc: | WL: | PH: | KCl%: | Cl -: | PV/YP: | Rmf: |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | KCL-PHPA | 10.5 | 65 | 5.9 | 9.0 | 6.3 | 37000 | 24 / 39 | 0.12 @ 75(F |

| Bit Data | No. | Make | Type | Size | Hours | Meters | Condition |
| --- | --- | --- | --- | --- | --- | --- | --- |
| (@ 24:00) | 6 | Hycalog | TC | HP21G | 8.5” | - | - | Drill out trip #1 |
|  | 7 | Reed | PDC | RSX272 | 8.5” | 3.0 | 13 | 0-1-RG-G-X-I-NO-BHA |
|  | 8 | Hycalog | PDC | RSX616M | 8.5” | 3.2 | 41 | 2-3-CT-A-X-I-BT-RIG |
|  | 9 | Hycalog | PDC | RSX616M | 8.5” | 3.2 | 20 | 0-0-NO- -X-I-NO-PR |
|  | 9RR | Hycalog | PDC | RSX616M | 8.5” | 14.87 | 201 | 0-0-BU- - X-I-NO-PR |
|  | 10 | Hycalog | Rock | TC11P | 8.5” | 32.7 | 321 | In hole |

| Surveys | Type | MD (m) | Inclination | Azimuth (T) | TVD (m) | Offset (m) | Direction (T) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | MWD | 2168.79 | 9.86 | 104.21 | 1218.95 | 1536.52 | 118.29 |
|  | MWD | 2197.64 | 6.92 | 99.24 | 1247.49 | 1540.56 | 118.25 |
|  | MWD | 2226.47 | 3.33 | 92.87 | 1276.20 | 1542.96 | 118.22 |

OPERATIONS SUMMARY

Previous 24 hrs Operations Summary: Wash & ream from 1763m to 2080m, circulating sweeps to unload cuttings. Drill ahead 8.5” directional hole from 2080m to 2250m dropping angle. Intersected Top Latrobe Clastics at 2124.5m (-1167mSS), 12m Low to prognosis. Anticipated operations: Drill ahead 8.5” directional hole to total depth. Circulate hole clean. Pull out of hole for possible Geotap pressure survey. Sensor Distances: Surveys 9.18m, Gamma Ray 11.65m, Resistivity 14.01m, Pressure 16.54m, Density 22.91m, Porosity 26.97m

| FORMATION TOPS (Preliminary Field picks) |
| --- |
| FORMATION | ACTUAL TOP | High / Low to | High / Low to | PROGNOSED TOP |
|  | (MDmRT) | (TVDmSS) | Prognosis | East Reeve-1 | (MDmRT) | (TVDmSS) |
| Jemmy's Point | 5.9 | 2.7 | - | - | 6 | 3 |
| Tambo River (Coquina) | 143 | -134.4 | 30.6m High | 30.8m High | 180 | -165 |
| Gippsland Limestone | 235 | -225.9 | 5.9m Low | 0.2m High | 230 | -220 |
| Lakes Entrance Formation | 1880 | -956.4 | 3.6m High | 27.1m High | 1876 ** | -960 ** |
| Latrobe Coarse Clastics | 2124.5 | -1167 | 12m Low | 9.5m High | 2098 | -1155 |
| Latrobe N. Asperus (Coal) | 2196 | -1238 | 18m Low | 9.1m High | 2163 | -1220 |
| Total Depth |  |  |  |  | 2281 | -1338 |

** Revised Prognosis

HYDROCARBON SHOW SUMMARY

| INTERVAL | LITHOLOGY & HYDROCARBON FLUORESCENCE | GAS |
| --- | --- | --- |
|  | LATROBE COARSE CLASTICS 2124.5m (-1167mSS) |  |
| 2124.5-2139m ROP: 2.6-3.9 Ave: 3.6 Note: Control Drilled | SANDSTONE WITH THIN CLAYSTONE INTERBEDS SANDSTONE: Clear to translucent, light grey in part, dominantly medium to very coarse grained, occasional very fine to fine grained aggregates, trace moderately strong siliceous cement, minor off white argillaceous matrix, trace pyrite, trace glauconite grains, trace fossil fragments, common loose clear quartz grains, moderately hard to hard to occasional hard aggregates, poor visual porosity in aggregates, fair to generally good inferred porosity, fluorescence. 2129-2133m: Trace to 5%, dull brown yellow patchy fluorescence, trace pale yellow crush cut, thick ring residue. 2133-2139m: Trace to rare fluorescence as above. | 8 / 2 units 99/1 |

| GAS | MD (m) | Peak | Background | Chromatograph |
| --- | --- | --- | --- | --- |
| Trip Gas | - | - | - | - |
| Connection Gas | - | - | - | - |

| INTERVAL ROP (min/ft) | LITHOLOGY | GAS (Peak / BG) Composition |
| --- | --- | --- |

| 2080-2124.5m ROP:3.5-10.5 Ave: 4.0 | MASSIVE CALCAREOUS CLAYSTONE INTERBEDDED WITH CALCAREOUS SILTSTONE CALCAREOUS CLAYSTONE: Light to medium grey, green grey, light brown in part, minor medium to dark brown, common glauconite grains, trace fossil fragments, trace pyrite, soft to moderately hard, subblocky. CALCAREOUS SILTSTONE: Light to medium grey, occasional light green grey, trace lithic fragments, trace glauconite grains, trace pyrite, firm to moderately hard, subblocky. | 8 / 3 units 100/trace |
| --- | --- | --- |

| INTERVAL ROP (min/ft) | LITHOLOGY | GAS (Peak / BG) Composition |
| --- | --- | --- |

|  | LATROBE COARSE CLASTICS 2124.5m (-1167mSS) |  |
| --- | --- | --- |
| 2124.5-2139m ROP: 2.6-3.9 Ave: 3.6 Note: Control Drilled | SANDSTONE WITH THIN CLAYSTONE INTERBEDS SANDSTONE: Clear to translucent, light grey in part, dominantly medium to very coarse grained, occasional very fine to fine grained aggregates, trace moderately strong siliceous cement, minor off white argillaceous matrix, trace pyrite, trace glauconite grains, trace fossil fragments, common loose clear quartz grains, moderately hard to hard to occasional hard aggregates, poor visual porosity in aggregates, fair to generally good inferred porosity, fluorescence as below. 2129-2133m: Trace to 5%, dull brown yellow patchy fluorescence, trace pale yellow crush cut, thick ring residue. 2133-2139m: Trace to rare fluorescence as above. CLAYSTONE: Light to medium grey, brown grey, minor light to medium brown, trace pyrite, firm to moderately hard, occasional hard, subblocky. | 8 / 2 units 99/1 |
| 2139-2154m ROP:3.5-4.7 Ave: 4.0 Note: Control Drilled | SANDSTONE WITH THIN CLAYSTONE INTERBEDS SANDSTONE: Clear to translucent, light grey in part, medium to very coarse grained, moderately poorly sorted, subangular, trace pyrite, trace glauconite grains, common loose clear quartz grains, generally loose and clean, minor moderately hard aggregates, fair to generally good inferred porosity, trace fluorescence as below. 2148-2151m: Trace dull yellow patchy fluorescence, trace pale yellow crush cut, thick film residue. CLAYSTONE: Light to medium grey, brown grey, minor light to medium brown, trace pyrite, firm to moderately hard, occasional hard, subblocky. | 6 / 2 units 99/1 |
| 2154-2173m ROP:3.7-4.0 Ave: 3.9 Note: Control Drilled | SANDSTONE WITH THIN CLAYSTONE INTERBEDS SANDSTONE: Clear to translucent, opaque, light grey in part, fine to very coarse grained, poorly sorted, subrounded to dominantly subangular, common angular, trace glauconite grains, common loose clear quartz grains, generally loose and clean, generally good inferred porosity, no hydrocarbon fluorescence. CLAYSTONE: Light to medium grey, brown grey, minor light brown, trace carbonaceous specks, trace pyrite, firm to moderately hard, occasional hard, subblocky. | 5 / 2 units 100% C1 to 99/1 |
| 2173-2196m ROP:3.6-13.0 Ave:6.0 | SANDSTONE INTERBEDDED WITH CLAYSTONE SANDSTONE: Clear to translucent, off white, light grey, minor brown, fine to coarse grained, poorly sorted, subangular to subrounded in part, trace to locally common dolomitic cement, trace pyrite, generally loose, common hard aggregates, poor visual porosity, good inferred porosity, no hydrocarbon fluorescence, common mineral fluorescence. CLAYSTONE: Light grey, medium grey, trace micro-carbonaceous specks, trace off white lithic fragments, firm, subblocky. | 4 / 2 units 100% C1 to 99/1 |

| INTERVAL ROP (min/ft) | LITHOLOGY | GAS (Peak / BG) Composition |
| --- | --- | --- |

|  | LATROBE N. ASPERUS 2196m (-1238m) |  |
| --- | --- | --- |
| 2196-2242m ROP:3.5-10.4 Ave:4.4 | SANDSTONE INTERBEDDED WITH COAL, SILTSTONE AND CLAYSTONE SANDSTONE: Clear to translucent, light grey, opaque, fine to coarse grained, minor very coarse grained, poorly sorted, subangular to subrounded, occasional angular, occasional moderately strong siliceous cement, trace moderately strong calcareous cement, trace light grey argillaceous matrix, dominantly loose, minor moderately hard to hard aggregates, poor visual porosity, fair to good inferred porosity, no hydrocarbon fluorescence. COAL: Very dark brown to brown black, dull, minor sub-vitreous, silty, argillaceous in part, grading to Carbonaceous Siltstone in part, subblocky to subfissile, uneven fracture. SILTSTONE: Brown, brown grey, argillaceous, minor arenaceous, common off white lithic fragments, calcareous, trace carbonaceous specks, slightly micro-micaceous, subblocky. CLAYSTONE: Light to medium green grey, light to medium brown grey, trace glauconite, trace off white lithic fragments, firm to hard in part, subblocky to subfissile. | 130 / 18 units 96/4 % Gas from Coals & Carbonaceous Siltstones & Claystones |