PETRO TECH PTY. LTD. A.C.N. (009 116 429) HAZELWOOD No.1 PEP 166

DAILY GEOLOGICAL REPORT No. 35 Date: 27-04-2007

Depth: 2081m Progress: 29m Days from Spud: 35

Rig: CENTURY RIG No.11 GL(AHD): 100.0m Drilling Rep: Lou DeVattimo RT: (datum) 105.2m Geologist: David Horner Last Casing: 9⅝" at 1298m

0600 hrs Update: POOH to log.

Comments: Drill ahead with 7⅝" to 2081m (T.D.), circulate hole clean, survey, wiper trip prior to POOH to log. Reached Total Depth (2081m) at 2100 hrs, 27th April, 2007. Deviation at 2069m = 48° at 110° Az.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2052-2081 | Crayfish Equivalent - No Show NOTE: The Crayfish Equivalent (1830-2081+m), is a massive thick extremely carbonaceous rich sequence. At the correct level of maturity this unit would have excellent oil source potential. | TG 0.3-0.6u C1 98% C2 2% C3+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hill Formation | 5.2 | 5.2 | +100 | 0 |
| LaTrobe Group | 10 | - | - | - |
| Strzelecki Formation | 530 | 545 | -435 | 15 Low |
| Rintouls Creek Sand (Tyers Conglomerate) | 2430 | n/p | n/p | - |
| Crayfish Equivalent | n/p | 1830 | -1620 | - |
| Basement | 2730 | - | - | - |
| Total Depth | 2750 | 2081 | -1806 | 669 Low |

*Provisional, based on mudlog

**Subsea depths are corrected for hole deviation

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2052-2081 | CRAYFISH EQUIVALENT Shale (100%) with minor laminated Sandstone (Trace) and Coal (trace). SHALE: very dark grey to black, moderately to dominantly very carbonaceous - grades to argillaceous coal, non to rarely very silty, common micromica, common calcite and trace quartz lined fractures, hard, fissile. SANDSTONE: off white to medium grey, silty to very fine, subrounded, moderately sorted, very strong silica and weak calcareous cements, abundant white to dark grey siliceous matrix, abundant altered feldspar grains, trace very fine black carbonaceous flecks, trace calcite and quartz lined fractures, very hard, no visual porosity, no oil fluorescence. COAL: black to very dark grey, dominantly very argillaceous, slickensided to conchoidal fracture, earthy lustre where argillaceous, vitreous lustre where clean, very slickensided, common calcite lined fractures, hard, brittle, no fluorescence or cut. |