LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 1 Date: 05-03-2006

Depth: 220m Progress: 0m Days from Spud: 1

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: Nipple up BOP's.

Comments: Loy Yang No.2 was drilled to 27.5m with a cable tool rig, 9.625" (244mm) casing was set at 27.5m and the cable tool rig released. A small rotary rig was then used to drill 8.5" (216mm) hole to 220m, 7" (178mm) casing was run and cemented at 220m. The small rotary rig was released and Hunt Rig No.2 was rigged up, and began nippling up BOP's at 1800hrs, 5th March, 2006 prior to drilling ahead with 6.125" (156mm) hole.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 1

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |