LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 12 Date: 16-03-2006

Depth: 1443m Progress: 115m Days from Spud: 12

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: Run Precision Logs: Run No.1 Resistivity-Sonic-SP-GR-Cal, Run No.2 Neutron Density - tool failed, RIH with backup tool.

Comments: Drill ahead with 156mm hole to 1443m, Total Depth - Reached at 1415 hrs 16th March, 2006. Circulate hole clean, wiper trip, Rig up to run Precision Logs, Run No.1 Resistivity/Sonic/GR/SP/Cal. DST#2 Sample Chamber water Rw = 3.98 at 25 degrees C.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1328-1383 | Strzelecki Formation OIL SHOW: (1328-1350m) A series of small fractures between 1328 and 1350m appear to have live oil saturation. The fracture infill material (calcite and minor stilbite) (<1% of samples) has 10% dull to bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. This corresponded to a background gas ranging from 1 to 3 units. Best assessment would be for these fractures to be too limited in interconnected volume for conventional production. Note: The fractures are hosted by claystone and sandstone, the surrounding sandstones have no intergranular fluorescence. OIL SHOW: (1356-1362m, 1365-1374m, 1377-1383m) A series of small fractures appear to have live oil saturation. The fracture infill material (calcite and minor stilbite) (<1% of samples) has trace dull to bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. This corresponded to a background gas ranging from 1 to 5.5 units. Best assessment would be for these fractures to be too limited in interconnected volume for conventional production. Note: The fractures are hosted by claystone and sandstone, the surrounding sandstones have no intergranular fluorescence. | TG 1-5.5u C1 100% C2+ 0 |
| 1383-1395 | Strzelecki Formation No Fluorescence | TG 1-2u C1 100% C2+ 0 |
| 1395-1416 | Strzelecki Formation OIL SHOW: (1395-1416m) A series of small fractures between 1398 and 1416m appear to have live oil saturation. The fracture infill material (calcite and minor stilbite) (<1% of samples) has trace to 10% dull to bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. This corresponded to a background gas ranging from 0.5 to 1 unit. Best assessment would be for these fractures to be too limited in interconnected volume for conventional production. Note: The fractures are hosted by claystone and sandstone, the surrounding sandstones have no intergranular fluorescence. | TG 0.5-1u C1 100% C2+ 0 |
| 1416-1431 | Strzelecki Formation OIL SHOW: (1419-1431m) A series of small fractures between 1419 and 1431m appear to have live oil saturation. The fracture infill material (calcite = <1% of samples) has trace dull to bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. This corresponded to a background gas ranging from 0.5 to 1 unit. Best assessment would be for these fractures to be too limited in interconnected volume for production. Note: The fractures are hosted by claystone and sandstone, with the surrounding sandstones have no intergranular fluorescence. | TG 0.5u C1 100% C2+ 0 |
| 1431-1443 T.D. | Strzelecki Formation No Fluorescence | TG 0.5u C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 12

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1328-1383 | STRZELECKI FORMATION Sandstone (30%) interbedded and laminated with Claystone (70%). SANDSTONE: off white to medium green grey, very fine to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, trace black coal detritus, trace calcite and red orange mineral veining, hard, no visual porosity. CLAYSTONE: medium grey to medium brown grey, occasionally dark grey, often very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains - grades to very fine sandstone, slightly carbonaceous, trace black coal detritus, trace micromica, trace calcite and orange red mineral veining, moderately hard, subfissile. FLUORESCENCE: (1328-1350m) The calcite fracture infill material (<1% of sample) has 10% dull to moderately bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. FLUORESCENCE: (1356-1362m, 1365-1374m, 1377-1383m) The calcite fracture infill material (<1% of sample) has trace dull to moderately bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. |
| 1383-1416 | STRZELECKI FORMATION Sandstone (20%) interbedded and laminated with Claystone (80%). SANDSTONE: off white to medium green grey, very fine to rarely medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, trace black coal detritus, common calcite and red orange mineral veining, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium brown grey, often very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains - grades to very fine sandstone, slightly to moderately carbonaceous, trace black coal detritus, trace micromica, common calcite and orange red mineral veining, hard, subfissile. FLUORESCENCE: 1395-1416m, The fracture infill material (<1% of sample) has trace to 10% dull to moderately bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. |
| 1416-1431 | STRZELECKI FORMATION Sandstone (100%) laminated with minor Claystone (trace). SANDSTONE: off white to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, trace black coal detritus, common calcite veining, hard, no visual porosity. CLAYSTONE: medium to dark grey to medium brown grey, often very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains - grades to very fine sandstone, slightly to moderately carbonaceous, trace black coal detritus, trace micromica, common calcite veining, hard, subfissile. FLUORESCENCE: (1419-1431m) The fracture infill material (<1% of sample) has trace dull to moderately bright patchy very pale yellow white fluorescence giving a weak white crush cut, trace residue. |
| 1431-1443 T.D. | STRZELECKI FORMATION Claystone (100%) laminated with minor Sandstone (trace). CLAYSTONE: medium to dark grey to medium brown grey, often very silty - grades to siltstone, often very finely arenaceous with altered feldspars grains - grades to very fine sandstone, moderately carbonaceous, trace black coal detritus, trace micromica, common calcite veining, hard, subfissile. SANDSTONE: off white to medium green grey, very fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant light green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, trace black coal detritus, common calcite veining, hard, no visual porosity, no oil fluorescence. |