LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 7 Date: 11-03-2006

Depth: 882m Progress: 192m Days from Spud: 7

Rig: HUNT RIG No.2 GL(AHD): 104.00m Drilling Rep: Lou DeVattimo RT: (datum) 107.65m Geologist: David Horner Last Casing: 178mm at 220m

0600 hrs Update: Perform DST No.2 872.45-882.0m

Comments: Drill ahead with 156mm hole to 853m, 10 stand wiper trip, drill ahead to 863m, survey 8.5 degrees, pull back surveying (8.5 deg at 842m, 8.5+ deg at 750m, 8 deg at 700m, 4.5 deg at 630m), RIH, wiper trip gas 3 units (C1 100%), drill ahead with 156mm hole to 882m, circulate geological sample, POOH for DST No.2 (872.45-882.0m).

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 690-750 | Strzelecki Formation - OIL SHOWS 699-705m, 735-741m. The sandstone host rock has no fluorescence or cut, however the calcite fracture lining present in the sample (trace sample) has 5% patchy moderately bright pale yellow fluorescence giving a moderately bright milky white crush cut with a thin ring residue. No associated gas increase was observed across this interval. Best assessment is for there to be fractures present at around these depths with some open volume containing live oil. Due to the limited nature of the fracturing observed in the cutting samples, open hole testing would not be warranted at this stage, however to validate this assessment careful analysis over these zones with E-Logs is recommended. The detrital coal has no fluorescence but give a very weak dull milky white crush cut. Maximum gas reading of 12 units was from coaly material. | TG 1-12u C1 100% C2+ 0 |
| 750-874 | Strzelecki Formation The detrital coal has no fluorescence but give a very weak dull milky white crush cut. Maximum gas reading of 25 units was from coaly material. | TG 1-25u C1 100% C2+ 0 |
| 874-882 | Strzelecki Formation - OIL SHOW 874 - 877m The caprock interval 856-874m overlying the show interval consists of a claystone with minor tight sandstone laminae. From 874-822m the interval consists of a massive sandstone with minor fracturing around 879m. The oil fluoresence is at the top of the sand across the interval 874-877m (3m net). The sandstone has 5% patchy light brown oil staining with 70% dull to occasionally moderately bright patchy medium yellow fluorescence giving a dull pale yellow crush to occasionally slow streaming cut, thin ring residue. No gas increase was observed indicating a low GOR oil. Best assessment would indicate the interval 874-877m to be oil saturated with a medium gravity oil, intergranular porosity is estimated as poor. | TG 0.6-4.2u C1 100% C2+ 0 |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Haunted Hills Gravels LaTrobe Group Carrajung Volcanics | 3.7 23.45 130.45 | 3.7 n/p n/p | 3.7 n/p n/p | 0 - - |
| Strzelecki Formation | 148.45 | n/p | n/p | - |
| T.D. | 1000 |  |  |  |

*Provisional, based on mudlog

LAKES OIL N.L. A.C.N. (004 247 214) LOY YANG No.2 PEP 166

DAILY GEOLOGICAL REPORT No. 7

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 690-750 | STRZELECKI FORMATION Sandstone (50%) occasionally thinly interbedded and laminated with Claystone (50%). SANDSTONE: off white to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant off white to medium green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, trace black carbonaceous detritus, trace calcite veining, hard, no visual porosity. CLAYSTONE: medium to dark grey to medium green grey to medium brown grey, often very silty - grades in part to siltstone, very finely arenaceous with altered feldspars grains in part, slightly to occasionally moderately carbonaceous, trace black coal detritus, rare micromica, trace calcite veining, moderately hard, subfissile. CUT: The detrital coal has no fluorescence but give a very weak dull milky white crush cut. FLUORESCENCE: 699-705m, 735-741m. The sandstone has no fluorescence or cut, but the calcite fracture lining material (trace of sample) has 5% patchy moderately bright pale yellow fluorescence giving a moderately bright milky white crush cut, thin ring residue. |
| 750-774 | STRZELECKI FORMATION Sandstone (40%) occasionally thinly interbedded and laminated with Claystone (60%). SANDSTONE: off white to medium green grey, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica and weak calcareous cements, abundant off white to medium green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, trace quartz grains, trace orange brown and black lithics, common black coal detritus, trace calcite veining, hard, no visual porosity, no oil fluorescence. CLAYSTONE: medium to dark grey to medium green grey to medium brown grey, often very silty - grades in part to siltstone, very finely arenaceous with altered feldspars grains in part, slightly to moderately carbonaceous, common black coal detritus, rare micromica, trace calcite veining, moderately hard, subfissile. CUT: The detrital coal has no fluorescence but give a very weak dull milky white crush cut. |
| 774-882 | STRZELECKI FORMATION Massive Sandstone (100%). SANDSTONE: off white to medium green grey, very fine to medium, dominantly medium, subangular to subrounded, moderately sorted, strong silica and weak to moderate calcareous cements, common to abundant off white to medium green grey argillaceous matrix, abundant altered feldspar grains, common grey green lithics, common quartz grains, trace orange brown and black lithics, common black coal detritus, trace calcite veining, hard, very poor visual intergranular porosity. FLUORESCENCE: (874-877m) The sandstone has 5% patchy light brown oil staining with 70% dull to occasionally moderately bright patchy medium yellow fluorescence giving a dull pale yellow crush to occasionally slow streaming cut, thin ring residue. |