|  | LAKES OIL N.L. (A.C.N. 004 247 214) | Registered Office: Level 11, 500 Collins Street, Melbourne, Vic. 3000 | P.O. Box 300, Collins St. West Melbourne, Vic. 8007 Phone: (03) 9629 1566 Fax: (03) 9629 1624 |
| --- | --- | --- | --- |

# Loy Yang-2 Wellsite

# via Traralgon

March 15th 2006

# Loy Yang-2 Daily Report # 10 – March 15th 2006

24 Hour Progress

At 6am this morning the contractor was drilling ahead in 156mm (6-1/8”) hole at a depth of 1185m having progressed 110m in the past 24hrs. Bit #2 was pulled out of the hole due to decreasing ROP (4m/hr) and the 156mm (6-1/8”) PDC bit #1 was rerun into the hole. The ROP was increased to approximately 15m/hr with the PDC. Gas shows of up to 84 units have been recorded from coaly material around 1177m and fluorescence has been noted in the sandstones from 1152m with a dull patchy orange possibly residual oil fluorescence. Due to the deviation of the hole the formation is coming in approximately 8m low compared to Loy Yang-1A.

Next 24 Hours

Continue to drill ahead in 156mm (6-1/8”) hole towards TD.

Tim O’Brien

Lakes Oil