LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loy Yang-2 | REPORT No. : | 12 | DFS: | 11.25 | DATE : | 16-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1443m | LAST DEPTH : | 1328m | 24 HR PROGRESS: | 115m | PTD : | 1443m |
| TOTAL FUEL : | 3,700 | FUEL USAGE : | 2,000 | DAYCOST : $ | 31,401 | CUM. COST : $ | 1,064,722 |
| 0600 OPS : | Wellsite logging by Precision Resistivity Sonic |
| Next 24 Hrs Op | Log-Wiper trip-DST |
| Site Personnel: | Lakes 4 Higgins 2 Hunt Energy 15 Hunt Camp 4 Aust DST 2 Baroid 1 Total 28 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Run Number | 6 Re-run # 1 |  |  | Drilling | 14.00 |  | Density | 8.75 | PPG |
| Size (mm) | 156 |  |  | Tripping | 5.50 |  | Viscosity | 35 | Sec |
| Make | Reed |  |  | Surveys |  |  | Water Loss | 6.5 | Cc |
| Type | DSX416S-A1 |  |  | Rig repairs |  |  | pH | 9.00 | Strip |
| IADC Code | S-222 |  |  | Testing/tools |  |  | Filter Cake | 1.0 | 32 nd |
| Serial Number | 211343 |  |  | Circulate Sample |  |  | PV / YP | 6 / 13 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12-12 |  |  | Light reaming |  |  | Gels | 3 / 4 / 5 | S/m |
| Depth in (m) | 1164 |  |  | Cementing |  |  | Sand | 0.15 | % Vol |
| Depth out (m) | 1443 |  |  | Slip and Cut line |  |  | Solids | 2.7 | % Vol |
| Total Metres |  |  |  | Circulate & Condition | 1.00 |  | Oil |  | % Vol |
| Hours |  |  |  | Rig service | 0.50 |  | K+ |  | Mg/l |
| WOB (kg) | 4000 |  |  | Rig up BOP |  |  | Chlorides | 5,500 | Mg/l |
| RPM | 100 |  |  | Logging | 3.00 |  | PHPA |  |  |
| Condition | 10% worn |  |  | DST |  |  | KCL | 1.10 | % by vol |
| Impact Force | 206. |  |  | Wait On Cement |  |  | Daily Cost $ | 2,443 |
| Jet Velocity | 183ft/sec |  |  | Test BOPs |  |  | Cum Cost $ | 35,759 |
| BHA: | Bit –bit sub-2 drill collars-stab- 10 drill collars-jars- 2 drill collars |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From |  | Operation |  | 8 + | ° at | 1157 | m |  | Type | Amount |
| 00:00 | 10:00 | Drilled 156mm hole from 1328m to 1414m |  |  | ° at |  | m |  | Barazan-D plus | 2 |
| 10:00 | 10:30 | Serviced the rig |  |  | ° at |  | m |  | Dextrid LTE |  |
| 10:30 | 14:30 | Drilled 156mm hole from 1414m to 1443m TD |  |  | ° at |  | m |  | Baracide / Pac-L |  |
| 14;30 | 15:00 | Circulated |  |  | ° at |  | m |  | N-VIS Plus | 11 |
| 15:00 | 16:00 | Wiper tripped to 1057m no hole problems |  |  | ° at |  | m |  | KCL Tech |  |
| 16:00 | 17:00 | Tripped back to bottom |  |  | ° at |  | m |  | Baracor 129 | 3 |
| 17:00 | 17;30 | Circulated |  |  | ° at |  | m |  | Potassium Hydrox | 2 |
| 17:30 | 21:00 | Tripped out for logging |  |  |  |  |
| 21:00 | 21:30 | Held safety meeting then rigged up loggers |  | PUMP 1 |  | PUMP 2 |
| 21:30 | 24;00 | Ran log #1 Lateral log |  | Liner | 140 | mm |  | Liner |  | mm |
|  |  |  |  | Pressure | 7,700 | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC | 100.4 | f/in |  | A.V. DC |  | m/min |
|  |  |  |  | SPM | 45 |  | SPM |  |
|  |  |  |  | GPM | 252 |  | GPM |  |
|  |  | String wt up 70 k |  |  |  |  |
|  |  | Rot 61k |  | CEMENT DATA |  | LAST CASING |
|  |  | Down 56k |  | Sacks Halliburton | 198 |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA Circulating out trip gas |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA Mousehole connections |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 566 |  | Halliburton cost | $ 31,212 |  | Shoe | 220m from RKB | m |

,66