LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Loyang-2 | REPORT No. : | 2 | DFS: | 1.25 | DATE : | 6-03-2006 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 231m | LAST DEPTH : | 220m | 24 HR PROGRESS: | 11 | PTD : | 1250m |
| TOTAL FUEL : | 11,800 | FUEL USAGE : | 500 | DAYCOST : $ | 39,188 | CUM. COST : $ | 580,771 |
| 0600 OPS : | Drilling156mm hole with Bit # 1 at 307m |
| Next 24 Hrs Op | Drill to Core depth |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 |  |  | Drilling | 2.00 |  | Density | 8.40 | S.G. |
| Size (mm) | 156 |  |  | Tripping | 5.50 |  | Viscosity | 55 | Sec |
| Make | Reed |  |  | Surveys |  |  | Water Loss | 9.0 | Cc |
| Type | DSX 206AIF+GW |  |  | Rigged up |  |  | pH | 9.7 | Strip |
| IADC Code | S-222 |  |  | Testing/tools |  |  | Filter Cake |  | 32 nd |
| Serial Number | 211343 |  |  | Circulate Sample |  |  | PV / YP | 11 / 16 | Cp/lb/100’ |
| Nozzles (32) | 12-12-12-12 |  |  | Casing |  |  | Gels | 5 / 7 / 8 | S/m |
| Depth in (m) | 220 |  |  | Cementing |  |  | Sand | 0.20 | % Vol |
| Depth out (m) |  |  |  | Surveys |  |  | Solids | 0.40 | % Vol |
| Total Metres | 11 |  |  | Circulate & Condition | 0.50 |  | Oil |  | % Vol |
| Hours | 0.5 |  |  | Rig Service/slip & cut |  |  | K+ |  | Mg/l |
| WOB (kg) | 2000kg |  |  | Rig up BOP | 10.50 |  | Chlorides | 7,500 | Mg/l |
| RPM | 90 |  |  | Drill out Cmt | 1.50 |  | PHPA |  |  |
| Condition |  |  |  | F.I.T | 0.50 |  | KCL | 1.50 % |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 3,920 |
| Jet Velocity |  |  |  | Test BOPs | 3.50 |  | Cum Cost $ | 9,684 |
| B.H.A.: | Bit-Bit sub with totco ring and float valve- 2 drill collars –stabilizer-10 drill collars 112.97m |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 10:30 | Completed BOP installation |  |  | ° at |  | m |  | Barazan-D Plus | 4 |
| 10:30 |  | Pressure tested Blind rams-Kill and Choke valves |  |  | ° at |  | m |  | Dextrid LTE | 4 |
|  | 13:30 | Choke manifold to 10,500kpa |  |  | ° at |  | m |  | PAC-L | 4 |
| 13:30 |  | Made up Bit # 1 pick drilling assembly and run in hole |  |  | ° at |  | m |  | N-VIS Plus | 4 |
|  | 18:00 | to 120m |  |  | ° at |  | m |  | KCL Tech | 8 |
| 18:00 |  | Pressure tested Pipe rams to 10,500kpa and annular to |  |  | ° at |  | m |  | Baracor 129 | 7 |
|  | 18;30 | 7000kpa |  |  | ° at |  | m |  |  |  |
| 18:30 | 19:00 | Continued to pick up drill pipe and run in hole |  |  |  |  |
| 19:00 | 19:30 | Tagged cement at 210m then picked up kelly |  | PUMP 1 |  | PUMP 2 |
| 19:30 | 21:00 | Drilled out cement –plugs and shoe at 220m |  | Liner | 140 | mm |  | Liner |  | mm |
| 21:00 | 21:30 | Drilled 156mm hole from 220m to 223m |  | Pressure | 2,800 | kPa |  | Pressure |  | KPa |
| 21:30 | 22:00 | Circulated hole clean |  | A.V. DP | 64.8 | f/min |  | A.V. DP |  | m/min |
| 22:00 | 22:30 | F.I.T with 8.4ppg mud 200psi EMW of 14.00ppg |  | A.V. DC | 117 | f/in |  | A.V. DC |  | m/min |
| 22:30 | 24:00 | Drilled 156mm hole from 223m to 234m |  | SPM | 42 |  | SPM |  |
|  |  |  |  | GPM | 236 |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 177.80 | mm |
|  |  |  |  | Class Bulk |  |  | Weight | 38.69 | Kg/m |
|  |  |  |  | % |  |  |  | Grade | N-80 |  |
|  |  | JSA BOP installation procedures |  | % |  |  |  | Connection | Buttress |  |
|  |  | JSA Making up the drilling assembly |  | % |  |  |  | Joints | 18 |  |
|  |  |  |  | % |  |  |  | Length | 216.00 | m |
| Days since | LTA | 556 |  | Av. Wt |  |  | Shoe | 220m from RKB | m |

,66