ESSO Australia Pty Ltd

| Date: | 12th December 2008 | Last Casing: | 10 ¾” ” @ 5482.87MDRT |
| --- | --- | --- | --- |
| Report Number: | 03 | PIT @ 10 ¾” shoe: | 14.0 ppg EMW |
| Report Period: | 11/12/08 05:00 hrs to 12/12/08 05:00 hrs. | Current hole size: | 9 ½” |
| Depth @ 0500 Hrs: | 6456 mMDRT TD | Mud Weight: | 10.8 ppg (circ. density) |
| Last Depth: | 6197 mMDRT | ECD @ Bit: | 12.5 ppg |
| Progress: | 259 m | Mud Type: | WellSet NAF |
| TD Lithology: | Sandstone and Siltstone | Mud Chlorides: | 44743 ppm |
| Water Depth: | 55.0m | Mud Fluid Loss: | 4.0 |
| RT Elevation: | 41.7m aMSL | Bit Type: | Reed Hycalog RSR616M-B4 |

OPERATIONS SUMMARY

| 24 HOUR SUMMARY 11/12/08 05:00 hrs to 12/12/08 05:00 hrs | Drill 9-1/2" production hole from 6197m to 6456m TD with Schlumberger RSS drilling assembly, circulate 3x BU until shakers clean, pump out of hole with 9-1/2" RSS drilling assembly from 374m to 6053m, work through tight spots at 6053m and 6044m, pump out of hole with 9-1/2" RSS drilling assembly from 6023m to 5935m. |
| --- | --- |
| NEXT 24 HOURS: | Circulate and condition hole inside 10-3/4" csg shoe. RIH on elevators to 6446m. |

GEOLOGICAL SUMMARY

LITHOLOGIC DESCRIPTION

| INTERVAL m MDRT (m TVDRT) | LITHOLOGY |
| --- | --- |
| 6139 – 6170 (2090.3 – 2117.8) ROP: 21 – 63 m/hr (avg 41 m/hr) | SANDSTONE with minor SILTSTONE SILTSTONE: (20 – 30%) medium brown to pale brown, medium greyish brown, common micromicaceous, minor to common carbonaceous fragments, rare lithics, firm to moderately hard, sub blocky. SANDSTONE: (30-70%) clear to translucent, opaque, very pale grey, very fine to fine aggregates, medium to rare coarse loose grains, sub-angular to sub-rounded, common very pale grey argillaceous matrix, weak to moderately siliceous cement, minor lithics, locally common feldspar, friable to firm aggregates, loose medium to coarse grains, poor visible porosity, poor to fair inferred porosity, no fluorescence. |
| 6170 – 6359 (2117.8 – 2285.5) ROP: 15 – 63 m/hr (avg 34 m/hr) | Interbedded SANDSTONE and SILTSTONE and rare COAL SILTSTONE: (10-100%) medium brown to dark brown, greyish brown to dark greyish brown, arenaceous grading to very fine Sandstone, abundant carbonaceous material and laminations grading to Carbonaceous Siltstone, common to locally abundant micromicaeous, minor nodular and disseminated pyrite, minor lithics, minor medium quartz grains, firm to rare moderately hard, sub-blocky. SANDSTONE: (90-Trace%) translucent to opaque, minor clear, fine to rare medium aggregates. medium to rare coarse loose grains, moderately sorted, sub-angular to sub-rounded, trace pale grey argillaceous matrix, trace moderately pyrite, friable aggregates, loose in part, poor visible porosity, poor to fair inferred porosity, no fluorescence. COAL: (Trace-5%)black to very dark grey, sub-vitreous to earthy in part, hackly fracture, firm to brittle, sub-blocky. |
| 6359 – 6456 (2285.5 – 2371.9) ROP: 5 – 47 m/hr (avg 24 m/hr) | Interbedded SANDSTONE and SILTSTONE SILTSTONE: medium brown to dark brown, dark greyish brown to greyish brown, arenaceous grading to grading to very fine Sandstone, common to abundant micromicaeous, common carbonaceous material grading to Carbonaceous Siltstone, common nodular pyrite, minor lithics, minor medium quartz grains, firm to moderately hard, sub-blocky. SANDSTONE: opaque to very pale grey, translucent to rare transparent, very fine to fine, rare medium, moderately well sorted, sub-angular to sub-rounded, minor very pale argillaceous matrix, weak to moderately siliceous cement, minor lithics, minor nodular pyrite, rare feldspar, trace carbonaceous specks, friable to firm aggregates, loose in part, poor visible and inferred porosity, no fluorescence. |

HYDROCARBON FLUORESCENCE:

| INTERVAL m MDRT (m TVDRT) | FLUORESCENCE DESCRIPTION |
| --- | --- |
|  | No hydrocarbon fluorescence encountered |

GAS SUMMARY:

| INTERVAL (m MDRT) | GAS TYPE | Total Gas Units min - max (average) | C1 ppm min - max (average) | C2 ppm min - max (average) | C3 ppm min - max (average) | iC4 ppm min - max (average) | nC4 ppm min - max (average) | C5 ppm min - max (average) | H2S ppm min - max (average) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 6139 –6170 | BG | 73 – 223 (147) | 11176 – 35862 (23267) | 700 - 1871 (1201) | 208 – 569 (363) | 36 – 95 (60) | 47 – 103 (70) | 12 – 28 (70) | - |
| 6154 | DGP | 222 | 35668 | 1869 | 569 | 95 | 103 | 25 | - |
| 6170 – 6359 | BG | 44 – 334 (101) | 6102 – 55006 (15231) | 413 - 1642 (799) | 150 – 478 (257) | 29 – 75 (41) | 37 – 91 (56) | 11 – 23 (15) | - |
| 6183 | DGP | 121 | 18557 | 1030 | 332 | 54 | 68 | 18 | - |
| 6202 | DGP | 109 | 16311 | 877 | 283 | 47 | 59 | 15 | - |
| 6210 | DGP | 190 | 29697 | 1491 | 478 | 75 | 95 | 22 | - |
| 6265 | DGP | 87 | 12968 | 729 | 247 | 44 | 55 | 14 | - |
| 6297 | DGP | 333 | 55006 | 1642 | 441 | 53 | 172 | 15 | - |
| 6305 | DGP | 163 | 26343 | 943 | 273 | 39 | 58 | 15 | - |
| 6348.5 | DGP | 194 | 31526 | 1066 | 296 | 42 | 57 | 15 | - |
| 6359 – 6456 | BG | 43 – 641 (176) | 5804 – 105699 (26850) | 421 – 2295 (1095) | 150 – 663 (314) | 28 – 82 (40) | 35 – 123 (66) | 10 – 61 (27) | - |
| 6361 | DGP | 640 | 105699 | 2295 | 545 | 66 | 51 | 18 | - |
| 6395 | DGP | 509 | 83291 | 2040 | 493 | 50 | 80 | 28 | - |
| 6402 | DGP | 316 | 48657 | 2046 | 663 | 81 | 123 | 40 | - |
| 6411 | DGP | 212 | 32500 | 1340 | 394 | 50 | 77 | 31 | - |
| 6415 | DGP | 222 | 35180 | 1197 | 331 | 43 | 64 | 27 | - |
| Gas types as follows:- BG = Background Gas, DGP = Drilling Gas Peak, TG = Trip Gas, CG = Connection Gas (Note: DGP, TG & CG will only be reported as Maximum figures only) |

LATEST SURVEY:

| m MDRT | Inclination | Azimuth | m TVDRT | m TVDSS |
| --- | --- | --- | --- | --- |
| 6434.27 | 27.52 | 356.48 | 2352.5 | -2337.8 |

Deviation from the Proposed Well Path:

- 0.08 m Above

- 4.01 m Left

PRELIMINARY WELLSITE FORMATION TOPS:

| FORMATIONS | PROGNOSED DEPTHS (m) | ACTUAL DEPTHS (m) |
| --- | --- | --- |
|  | MDRT | TVDRT | TVDSS | MDRT | TVDRT | TVDSS | HIGH/LOW to prognosis |
| Lakes Entrance Fm. | 5052.0 | 1378.0 | -1336.3 | 5040.0 | 1377.1 | -1335.4 | 0.9 H |
| Top of Latrobe Group | 5479.0 | 1519.0 | -1477.3 | 5470.0 | 1520.6 | -1478.9 | 1.6 L |
| Top Coarse Clastics | 5518.0 | 1545.0 | -1503.3 | 5491.5 | 1534.5 | -1492.8 | 10.5 H |
| N-1.4 Coal | 5576.0 | 1592.0 | -1550.3 | 5562.5 | 1588.0 | -1546.3 | 4.0 H |
| N-1.9 Coal | 5682.0 | 1682.0 | -1640.3 | 5670.5 | 1678.3 | -1636.6 | 3.7 H |
| N-1.9 Reservoir | 5690.0 | 1693.0 | -1651.3 | 5684.3 | 1690.2 | -1648.5 | 2.8 H |
| M-2 Upper Reservoir | 5755.0 | 1745.0 | -1703.3 | 5744.8 | 1741.5 | -1699.8 | 3.5 H |
| M-2 Lower Reservoir | 5776.0 | 1764.0 | -1722.3 | 5771.9 | 1765.0 | -1723.3 | 1.0 L |
| L-5 Reservoir | 5925.0 | 1896.0 | -1854.3 | 5906.7 | 1884.5 | -1842.8 | 11.5 H |
| L-8 Reservoir | 5985.0 | 1951.0 | -1909.3 |  |  |  |  |
| Top Volcanics | 6069.0 | 2024.0 | -1982.3 | 6043.7 | 2006.0 | -1964.3 | 18.0 H |
| Base Volcanics | 6088.0 | 2039.0 | -1997.3 | 6060.2 | 2021.0 | -1979.3 | 18.0 H |
| Sub Volcanic Reservoir | 6100.0 | 2057.0 | -2015.3 | 6100.2 | 2033.0 | -1991.3 | 24.0 H |
| Top F-1 Sands | 6215.0 | 2154.0 | -2112.3 |  |  |  |  |
| Top T-1 Sands | 6380.0 | 2300.0 | -2258.3 | 6359.0 | 2285.5 | -2243.8 | -14.5 H |
| Base T-1 Sands | 6402.0 | 2320.0 | -2278.3 |  |  |  |  |
| Total Depth | 6463.0 | 2373.0 | -2331.3 | 6456.0 | 2371.9 | -2330.2 | 1.1 H |

COMMENTS:

- LWD sensor offsets

Tool              Sensor                To Bit (m)

CRS :            D&I                        4.17

EcoScope:     GR                         9.76

EcoScope:     Res                      12.80

EcoScope :    Neutron                13.11

EcoScope :    Density                 13.11

EcoScope :    PWD                      9.92

ARC5 :          GR                        27.60

ARC5 :          Res                       27.55

WELLSITE GEOLOGISTS:

- Daniel van der Aa	(0600 – 1800 hrs)

- Marcus Payne		(1800 – 0600 hrs)