Geology Operations

| NETHERBY 1DW1 PM REPORT DATE: 04/08/08 (15:30 Hours EST) | DEPTH: 1944m MDRT 1681.7m TVDRT (-1660.9m SS MSL) PROGRESS: 0m (Since 06:00 hrs EST) | GEOLOGIST: J. Pitman PHONE: (08) 6103 1104 RIG: OCEAN PATRIOT |
| --- | --- | --- |

CURRENT OPERATION: Back reaming out of the hole at 1570m having reached total depth for the 311mm (12¼") hole section.

OPERATIONS SINCE 06:00 to 15:30 hrs EST: Pull out of hole, working and back reaming tight hole as required. ANTICIPATED OPERATIONS: Continue to pull out of the hole, back reaming as required. Run in hole to total depth. Circulate bottoms up. Pull out of hole and run 244mm (9 5/8") / 273mm (10¾") casing

| Surveys | Type | MD (m) | Inclination | Azimuth (T) | TVD (m) | Offset (m) | Direction (T) |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | LWD | 1919.6 | 80 | 123 | 1677.6 | 585 | 118 |
|  | LWD | 1944.5 | 81 | 123 | 1681.8 | 609 | 118 |

|  | FORMATION TOPS |
| --- | --- |
| FORMATION | ACTUAL TOP | High / Low | High / Low | PROGNOSED TOP |
|  | (mMDRT) | (mSS MSL) | Prognosis (m) | Netherby 1 | (MDmRT) | (mSS MSL) |
| SEA LEVEL | 20.8 | 0.0 |  |  | 20.8 | 0.0 |
| HEYTSBURY GP | 86.9 | -66.1 |  | - | 87.0 | -65.0 |
| MEPUNGA FM | 674.0 | -653.2 | 9.8 High | - | 685.0 | -663.0 |
| DILWYN FM / WANGERRIP GP | 778.0 | -757.2 | 6.2 Low | - | 773.0 | -751.0 |
| PEMBER MUDSTONE | 1004.5 | -979.6 | 22.4 High | - | 1027.0 | -1002.0 |
| PEBBLE POINT FM | 1069.0 | -1042.2 | 17.2 Low | - | 1051.0 | -1025.0 |
| MASSACRE SHALE | 1139.0 | -1110.4 | 17.4 Low | - | 1123.0 | -1093.0 |
| TIMBOON FM | 1155.0 | -1125.4 | 21.4 Low | - | 1135.0 | -1104.0 |
| PAARATTE FM | 1346.0 | -1293.6 | 9.6 Low | - | 1337.0 | -1284.0 |
| SKULL CREEK MDST | 1561.0 | -1469.5 | 15.5 Low | 0.2 High | 1555.0 | -1454.0 |
| K85 UNCONFORMITY | 1898.0 | -1652.7 | - | 0.1 Low | NP | NP |
| WAARRE "A" | 1929.0 | -1658.5 | 0.5 High | 3.6 High | 1939.0 | -1659.0 |
| EUMERALLA FM |  |  |  |  | NP | NP |
| TOTAL DEPTH |  |  |  |  | 2504 | -1622.0 |

| INTERVAL | LITHOLOGY & HYDROCARBON FLUORESCENCE | GAS |
| --- | --- | --- |

COMMENTS: