| Date: | 1st August 2008 – 06:00 EST | Licence / State: | VIC/P44 |
| --- | --- | --- | --- |
| Report Period: | 06:00 – 06:00 Hours EST | Rig: | OCEAN PATRIOT |
| Days From Spud: | 17 | RT - SEAFLOOR: | 86.9m |
| Current Hole Size: | 311mm (12 ¼") | WATER DEPTH | 66.1m MSL |
|  |  | RT: | 20.8m MSL |
| Depth @ 06:00 Hrs EST: | 1875m MDRT | PTD: | 1822m MDRT |
|  | -1727.5m SS MSL | Spud Date: | 07:30 hrs on 15th July,08 |
| 24 Hr Progress: 06:00 – 06:00 EST | 0m |  |  |
| Current Operation: | Running in hole with cementing muleshoe prior to plugging back Netherby 1. |
| Nope Cost (Drill)$ | (C&S)$ |  | Cost To Date: |
|  | (P&A)$ 19.3 million |  |  |

| Casing Data | Hole Size | Depth | Casing Size | Wt: | Type | Shoe Depth | LOT |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | 914 mm (36") | 130.9m | 762mm (30") | 461 kg/m (310 lb/ft) | Conductor | 130.9m |  |
|  | 445mm (17.5") | 647.5m | 340mm (13.375") | 101 kg/m (68 lb/ft) | L80 | 642.2m | 2.12sg (17.7ppg) |
|  | 311mm (12.25") | 1875m |  |  |  |  |  |

| Mud Data | Type: | Wt: | Visc: | WL: | PH: | KCl: | Cl -: | PV/YP: | Rmf: |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | KCl/GLY | 11.0 | 47 | 4.0 | 8.5 | 8.3 | 45k | 21/38 | - |

| Bit Data | No. | Make | Type | Size | Hours | Meters | Condition |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Current |  |  |  |  |  |  |  |  |
| Previous | 5RR | Hughes | Mill | MXL-1X | 311mm (12¼") | 1.1 | 5.0 | 1-1-NO-A-E-1-NO-LOG |

| Surveys | Type | MD (m) | Inclination | Azimuth (T) | TVD (m) | Offset (m) | Direction (T) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Projection | MWD | 1875.0 | 35 | 119 | 1748.3 | 470 | 119 |

OPERATIONS SUMMARY

Previous 24 hrs Operations Summary at 06:00 hrs EST

Continue LWD Stethoscope pressure survey, trouble shooting tool problems as required. Total 17 tests attempted, 4 good tests, 5 tight, 1 no seal, 7 no test (unsure of probe extension). Condition hole, work tight spot at 1831m. Wash, rotate to bottom. Circulate hole clean and pull out of hole laying down LWD tools. Make up cementing muleshoe and run in hole. Slip and cut drill line at the casing shoe. Continue running in hole.

Anticipated Operations:

Plug back Netherby 1. Pick up 311mm (12¼") directional assembly and sidetrack to Netherby 1DW1.

|  | FORMATION TOPS |
| --- | --- |
| FORMATION | ACTUAL TOP | High / Low | High / Low | PROGNOSED TOP |
|  | (mMDRT) | (mSS MSL) | Prognosis (m) | Henry 1 | (MDmRT) | (mSS MSL) |
| SEA LEVEL | 20.8 | 0.0 |  |  | 20.8 | 0.0 |
| HEYTSBURY GP | 86.9 | -66.1 |  |  | 87.0 | -65.0 |
| MEPUNGA FM | 674.0 | -653.2 | 9.8 High | 102.1 High | 685.0 | -663.0 |
| DILWYN FM / WANGERRIP GP | 778.0 | -757.2 | 6.2 Low | 94.3 High | 773.0 | -751.0 |
| PEMBER MUDSTONE | 1004.5 | -979.6 | 22.4 High | 117.9 High | 1027.0 | -1002.0 |
| PEBBLE POINT FM | 1069.0 | -1042.2 | 17.2 Low | 80.7 High | 1051.0 | -1025.0 |
| MASSACRE SHALE | 1139.0 | -1110.4 | 17.4 Low | 76.5 High | 1123.0 | -1093.0 |
| TIMBOON FM | 1155.0 | -1125.4 | 21.4 Low | 73.2 High | 1135.0 | -1104.0 |
| PAARATTE FM | 1346.0 | -1293.6 | 9.6 Low | 104.9 High | 1337.0 | -1284.0 |
| SKULL CREEK MDST | 1560.0 | -1469.7 | 15.7 Low | 171.3 High | 1544.0 | -1454.0 |
| K85 UNCONFORMITY WAARRE 'B" | 1783.0 | -1652.6 | NP | 144.4 High | 1739.0 | -1614.0 |
| WAARRE "A" | 1792.5 | -1662.1 | 48.1 Low | 139.5 High | 1739.0 | -1614.0 |
| EUMERALLA FM | 1820.0 | -1684.2 | 43.2 Low | 147.3 High | 1772.0 | -1641.0 |
| TOTAL DEPTH | 1875.0 | -1727.5 |  |  | 1822.0 | -1682.0 |

HYDROCARBON SHOW SUMMARY

| INTERVAL | LITHOLOGY & HYDROCARBON FLUORESCENCE | GAS |
| --- | --- | --- |

| GAS | MD (m) | Peak | Background | Chromatograph |
| --- | --- | --- | --- | --- |

GEOLOGICAL SUMMARY

| INTERVAL ROP (m/hr) | LITHOLOGY | GAS (Peak / BG) Composition |
| --- | --- | --- |

REMARKS: