NETHERBY 1DW1:  CUTTINGS SAMPLE DESCRIPTIONS

| Depth From (m) | Depth To (m) | % | Lithology and Shows |
| --- | --- | --- | --- |
| NETHERBY 1DW1 was sidetracked from the Netherby 1 wellbore from 1505m at 21:00 hours on 2nd August 2008. |
|  |  |  | Directional assembly run into the hole tagging soft cement at 1421m. Soft cement drilled, washed and reamed from 1421m to firm cement at 1455m. Time drill attempting to sidetrack from the Netherby 1 wellbore. |
|  |  |  | 2nd August 2008 |
| 1455 | 1455.5 | 70 30 | Cement Siltstone |
| 1455.5 | 1456 | 70 30 | Cement Siltstone |
| 1456 | 1456.5 | 80 20 | Cement Siltstone |
| 1456.5 | 1457 | 80 20 | Cement Siltstone |
| 1457 | 1457.5 | 80 20 | Cement Siltstone |
| 1457.5 | 1458 | 75 25 | Cement Siltstone |
| 1458 | 1458.5 | 70 30 | Cement Siltstone / Sandstone |
| 1458.5 | 1459 | 60 40 | Cement Siltstone / Sandstone |
| 1459 | 1459.5 | 60 40 | Cement Siltstone / Sandstone |
| 1459.5 | 1460 | 60 40 | Cement Siltstone / Sandstone |
| 1455 | 1460 | 60-100 trace-10 | Directional drill 311mm (12¼") hole attempting to sidetrack the well. SILTSTONE: medium dark grey to dark grey, occasionally brownish grey, locally very finely arenaceous, trace fine carbonaceous specks, trace forams, minor fine grained glauconite, trace fine grained lithics, firm to predominately moderately hard, blocky to sub blocky. SANDSTONE: clear, translucent, trace with orange Fe stain, very fine to fine grained, minor medium grained, rare loose coarse quartz grains, fair sorting, weak siliceous cement, minor light grey argillaceous matrix, trace nodular pyrite, friable to moderately hard aggregates, poor inferred porosity, no fluorescence. Note: 100 decreasing to 60% cement in samples. |
| 1460 | 1460.5 | 70 30 | Cement Siltstone |
| 1460.5 | 1461 | 40 50 10 | Cement Siltstone Sandstone: very fine to fine grained. |
| 1461 | 1461.5 | 60 30 10 | Cement Siltstone Sandstone: very fine to fine grained. |
| 1461.5 | 1462 | 60 30 10 | Cement Siltstone Sandstone: very fine to fine grained. |
| 1462 | 1462.5 | 30 40 30 | Cement Siltstone Sandstone: very fine to fine grained. |
| 1462.5 | 1463 | 40 40 20 | Cement Siltstone Sandstone: very fine to fine grained, trace medium to coarse. |
| 1463 | 1463.5 | 50 40 10 | Cement Siltstone Sandstone: very fine to fine grained. |
| 1463.5 | 1465 | 100 | Cement |
| 1465 | 1469 | 95 5 | Cement Siltstone / trace loose medium quartz grains. |
| 1469 | 1470 | 90 10 | Cement Siltstone / Sandstone |
| 1470 | 1475 | 80 10 10 | Cement SILTSTONE: medium dark grey to dark grey, dark greenish grey, very finely arenaceous, rare to minor fine grained glauconite, trace fine carbonaceous specks, trace fine grained lithics, firm to predominately moderately hard, blocky to sub blocky. SANDSTONE: clear, translucent, very fine to fine grained, minor medium to coarse grained, fair sorting, weak siliceous cement in very fine to fine grained aggregates, minor light grey argillaceous matrix, trace very fine glauconite, friable very fine to fine grained aggregates, poor inferred porosity, no fluorescence. |
| 1475 | 1480 | 100 | Cement |
| 1480 | 1485 | 100 | Cement |
| 1485 | 1490 | 100 | Cement |
| 1490 | 1495 | 90 10 | Cement Siltstone. |
| 1495 | 1497 | 75 25 | Cement Siltstone: dark grey, minor – common glauconite. |
| 1497 | 1500 | 75 25 | Cement SILTSTONE: dark grey, dark brownish grey, argillaceous, minor glauconite, soft to dispersive, amorphous, blocky. |
| 1500 | 1502 | 70 20 10 | Cement Siltstone. Sandstone: very fine to fine grained. |
| 1502 | 1505 | 30 40 30 | Cement SILTSTONE: medium dark brownish grey, dark grey, very finely arenaceous, argillaceous in part, minor fine grained glauconite, trace very fine lithics, soft, dispersive with argillaceous content easily washed from samples, locally moderately hard, blocky. SANDSTONE: translucent, clear, very fine to fine grained, sub angular to predominately sub rounded, well sorted, common grey silty / argillaceous matrix, minor very fine glauconite, trace fine grained lithics, predominately loose quartz grains, poor inferred porosity, no fluorescence. |
|  |  |  | NETHERBY 1DW1 sidetracked from the Netherby 1 wellbore from 1505m at 21:00hours on 02/08/08 |
| 1505 | 1510 | 50 50 | SILTSTONE: medium dark brownish grey, dark grey, very finely arenaceous, argillaceous in part, minor fine grained glauconite, trace very fine lithics, soft, dispersive with argillaceous content easily washed from samples, locally moderately hard, blocky. SANDSTONE: translucent, clear, very fine to fine grained, sub angular to predominately sub rounded, well sorted, common grey silty / argillaceous matrix, minor very fine glauconite, trace fine grained lithics, predominately loose quartz grains, poor inferred porosity, no fluorescence |
| 1510 | 1520 | 50 50 | SILTSTONE: medium brownish grey, dark grey, very finely arenaceous, argillaceous in part, rare fine grained glauconite, trace very fine lithics, trace forams, soft, dispersive with argillaceous content easily washed from samples, locally moderately hard, blocky. SANDSTONE: translucent, clear, very fine to fine grained, trace medium loose quartz grains, sub angular to predominately sub rounded, moderately well sorted, common grey silty / argillaceous matrix, rare very fine glauconite, trace fine grained lithics, friable to loose quartz grains, poor inferred porosity, no fluorescence |
| 1520 | 1530 | 70 30 | SILTSTONE: medium brownish grey, dark grey, very finely arenaceous, argillaceous in part with clay content washing from samples, rare fine grained glauconite, trace very fine lithics, firm, locally moderately hard, blocky. SANDSTONE: translucent, clear, very fine to fine grained, trace medium – coarse loose quartz grains, sub angular to predominately sub rounded, moderately well sorted, common light grey argillaceous / silty matrix, rare very fine glauconite, trace fine grained lithics, friable to loose quartz grains, poor inferred porosity, no fluorescence |
| 1530 | 1540 | 90 10 | SILTSTONE: pale to medium grey brown, medium grey, generally argillaceous, minor carbonaceous specks and quartz grains, very soft to dispersive, occasionally firm, amorphous, sub-blocky in part. SANDSTONE: clear to translucent, off white, dominantly fine, occasionally medium to coarse, moderately sorted, sub-round to occasionally sub-angular, moderately calcareous cement, occasional off white argillaceous matrix, minor lithics, friable to moderately hard, loose in part, very poor visual porosity, poor inferred porosity, no fluorescence. |
| 1540 | 1550 | 50 50 | SILTSTONE: pale to medium grey brown, medium grey, generally argillaceous, minor carbonaceous specks and quartz grains, very soft to dispersive, occasionally firm, amorphous, sub-blocky in part. SANDSTONE: clear to translucent, off white, dominantly fine, rare medium to coarse, moderately sorted, sub-round to occasionally sub-angular, moderately calcareous cement, occasional off white argillaceous matrix, minor glauconite grains and lithics, friable to moderately hard, loose in part, very poor visual porosity, poor inferred porosity, no fluorescence. |
| 1550 | 1560 | 30 70 | SILTSTONE: pale to medium grey brown, medium grey, generally argillaceous, minor carbonaceous specks and quartz grains, very soft to dispersive, occasionally firm, amorphous, sub-blocky in part. SANDSTONE: clear to translucent, off white, dominantly fine to medium, minor coarse, moderately sorted, sub-round to occasionally sub-angular, moderately calcareous cement, occasional off white argillaceous matrix, locally common glauconite grains, minor lithics, friable to moderately hard, loose in part, very poor visual porosity, poor inferred porosity, no fluorescence. |
| 1560 | 1570 | 90 10 | SILTSTONE: pale to medium brown, medium to dark grey in part, argillaceous to minor arenaceous, occasional carbonaceous specks, soft to firm, sub-blocky, amorphous. SANDSTONE: clear to translucent, off white, generally medium, minor coarse, moderately sorted, sub-round to occasionally round, moderately calcareous cement, occasional off white argillaceous matrix, occasional glauconite grains, friable to moderately hard, loose, poor to very poor visual & inferred porosity, no fluorescence. |
| 1570 | 1580 | 90 10 | SILTSTONE: pale to medium brown, medium to dark grey in part, argillaceous to minor arenaceous, occasional carbonaceous specks, minor pyrite nodules, soft to firm, sub-blocky, amorphous. SANDSTONE: clear to translucent, off white, generally medium, minor coarse, moderately sorted, sub-round to occasionally round, moderately calcareous cement, occasional off white argillaceous matrix, occasional glauconite grains, friable to moderately hard, loose, poor to very poor visual & inferred porosity, no fluorescence. |
| 1580 | 1590 | 90 10 | SILTSTONE: pale to medium brown, medium to dark grey in part, argillaceous to minor arenaceous, occasional carbonaceous specks, minor pyrite nodules, soft to firm, sub-blocky, amorphous. SANDSTONE: clear to translucent, off white, generally medium, minor coarse, moderately sorted, sub-round to occasionally round, moderately calcareous cement, occasional off white argillaceous matrix, occasional glauconite grains, friable to moderately hard, loose, poor to very poor visual & inferred porosity, no fluorescence. |
| 1590 | 1600 | 100 trace | SILTSTONE: pale to medium brown, medium to dark grey in part, argillaceous to minor arenaceous, occasional carbonaceous specks, soft to firm, occasionally hard, sub-blocky, amorphous. SANDSTONE: clear to translucent, off white, generally medium, minor coarse, moderately sorted, sub-round to occasionally round, moderately calcareous cement, occasional off white argillaceous matrix, occasional glauconite grains, friable to moderately hard, loose, poor to very poor visual & inferred porosity, no fluorescence. |
| 1600 | 1610 | 100 trace | SILTSTONE: medium to occasionally dark grey brown, minor argillaceous to arenaceous, occasional carbonaceous specks, firm to moderately hard, occasionally soft, sub-blocky. SANDSTONE: clear to translucent, off white, generally medium, minor coarse, moderately sorted, sub-round to occasionally round, moderately calcareous cement, occasional off white argillaceous matrix, occasional glauconite grains, friable to moderately hard, loose, poor to very poor visual & inferred porosity, no fluorescence. |
| 1610 | 1620 | 100 | SILTSTONE: medium to dark grey brown, arenaceous in part, minor carbonaceous specks, locally micro mica, firm to moderately hard, occasionally hard, blocky to sub-blocky. |
| 1620 | 1630 | 100 | SILTSTONE: medium to predominately dark brown, minor brown grey, argillaceous to minor arenaceous, rare carbonaceous specks and micro mica, firm to moderately hard, occasionally soft, sub-blocky to blocky, amorphous. |
| 1630 | 1640 | 100 | SILTSTONE: medium to predominately dark brown, minor brown grey, argillaceous to minor arenaceous, rare carbonaceous specks and micro mica, firm to moderately hard, occasionally soft, sub-blocky to blocky, amorphous. |
| 1640 | 1650 | 80 20 | SILTSTONE: medium to predominately dark brown, minor brown grey, argillaceous to minor arenaceous, rare carbonaceous specks and micro mica, firm to moderately hard, occasionally soft, sub-blocky to blocky, amorphous. SANDSTONE: clear to translucent, off white, occasionally pale brown, fine to occasionally medium, moderately well sorted, sub-angular to sub-round, weak calcareous cement, occasional off white argillaceous matrix, rare lithics, loose, minor friable, poor to very poor visual and inferred porosity, no fluorescence. |
| 1650 | 1660 | 50 50 | SILTSTONE: medium to predominately dark brown, minor brown grey, argillaceous to minor arenaceous, rare carbonaceous specks and micro mica, firm to moderately hard, occasionally soft, sub-blocky to blocky, amorphous. SANDSTONE: clear to translucent, off white, occasionally pale brown, fine to dominantly medium, occasionally coarse, moderately well sorted, sub-angular to sub-round, weak calcareous cement, occasional off white argillaceous matrix, rare lithics, loose, minor friable, poor to visual and inferred porosity, no fluorescence. |
| 1660 | 1670 | 70 30 | SILTSTONE: medium to predominately dark brown, minor brown grey, argillaceous to minor arenaceous, rare carbonaceous specks and micro mica, minor glauconite grains, firm to moderately hard, occasionally soft, sub-blocky to blocky, amorphous. SANDSTONE: clear to translucent, off white, occasionally pale brown, fine to dominantly medium, occasionally coarse, moderately well sorted, sub-angular to sub-round, weak calcareous cement, occasional off white argillaceous matrix, rare lithics, loose, minor friable, poor to visual and inferred porosity, no fluorescence. |
| 1670 | 1680 | 90 10 | SILTSTONE: medium to predominately dark brown, minor brown grey, argillaceous to minor arenaceous, rare carbonaceous specks and micro mica, minor glauconite grains, occasional inclusions, firm to moderately hard, occasionally soft, sub-blocky to blocky, amorphous. SANDSTONE: clear to translucent, off white, occasionally pale brown, fine to dominantly medium, occasionally coarse, moderately well sorted, sub-angular to sub-round, weak calcareous cement, occasional off white argillaceous matrix, rare lithics, loose, minor friable, poor visual and inferred porosity, no fluorescence. |
| 1680 | 1690 | 100 | SILTSTONE: medium to dark grey, grey brown, rare arenaceous, occasional glauconite grains, minor carbonaceous specks, rare pyrite nodules, soft to firm, occasionally moderately hard, dispersive, blocky to sub-blocky. |
| 1690 | 1700 | 100 | SILTSTONE: medium to dark brown, grey brown, rare arenaceous, occasional glauconite grains, minor carbonaceous specks, minor calcareous inclusions, soft to firm, occasionally moderately hard, dispersive, blocky to sub-blocky. |
| 1700 | 1710 | 100 | SILTSTONE: medium to dark brown, grey brown, rare arenaceous, occasional glauconite grains, minor carbonaceous specks, minor calcareous inclusions, soft to firm, occasionally moderately hard, dispersive, blocky to sub-blocky. |
| 1710 | 1720 | 100 | SILTSTONE: medium to dark brown, grey brown, rare arenaceous, occasional glauconite grains, minor carbonaceous specks, minor glauconite grains and calcareous inclusions, soft to firm, occasionally moderately hard, dispersive, blocky to sub-blocky. |
| 1720 | 1730 | 100 | SILTSTONE: medium to dark brown, locally arenaceous, occasional glauconite grains, minor carbonaceous specks, minor glauconite grains and calcareous inclusions, soft to firm, occasionally moderately hard, dispersive, blocky to sub-blocky. |
| 1730 | 1740 | 100 | SILTSTONE: medium grey brown, occasionally pale to medium brown, siliceous in part, minor arenaceous, minor carbonaceous specks, rare glauconite grains, moderately hard to hard, minor very hard, blocky to sub-blocky. |
| 1740 | 1750 | 100 | SILTSTONE: medium grey brown, occasionally pale to medium brown, siliceous in part, minor arenaceous, minor carbonaceous specks, occasional calcareous inclusions, rare glauconite grains, moderately hard to hard, minor very hard, blocky to sub-blocky. |
| 1750 | 1760 | 100 | SILTSTONE: medium grey brown, occasionally pale to medium brown, siliceous in part, minor arenaceous, minor carbonaceous specks, occasional calcareous inclusions, rare glauconite grains, soft to dispersive, amorphous, moderately hard, blocky to sub-blocky. |
| 1760 | 1770 | 100 | SILTSTONE: medium grey brown, occasionally pale to medium brown, siliceous in part, minor arenaceous, minor carbonaceous specks, occasional calcareous inclusions, rare glauconite grains, soft to dispersive, amorphous, moderately hard, blocky to sub-blocky. |
| 1770 | 1780 | 100 | SILTSTONE: medium brownish grey, grey brown, locally arenaceous, minor fine carbonaceous specks, rare calcareous fragments, rare fine grained glauconite, soft to firm, moderately hard in part, blocky to sub blocky. |
| 1780 | 1790 | 100 trace | SILTSTONE: medium brownish grey, grey brown, locally arenaceous, minor fine carbonaceous specks, rare calcareous fragments, rare fine grained glauconite, soft to firm, moderately hard in part, blocky to sub blocky. SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, minor off white argillaceous matrix, trace very fine lithics, friable, poor visual porosity, no fluorescence. |
| 1790 | 1800 | 95 5 | SILTSTONE: medium brownish grey, grey brown, locally arenaceous, minor fine carbonaceous specks, rare cal fragments, rare fine grained glauconite, soft to firm, moderately hard in part, blocky to sub blocky. SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, minor off white argillaceous matrix, trace very fine lithics, trace nodular pyrite, trace fine grained glauconite, friable, poor visual porosity, no fluorescence. |
| 1800 | 1810 | 100 trace | SILTSTONE: medium brownish grey, grey brown, locally arenaceous, minor fine carbonaceous specks, rare fine grained glauconite, trace LIMESTONE fragments, soft to firm, moderately hard in part, blocky to sub blocky. SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, trace loose medium sub rounded quartz grains, sub angular to sub rounded, well sorted, weak calcareous cement, minor off white argillaceous matrix, trace very fine lithics, trace nodular pyrite, trace fine grained glauconite, friable, poor visual porosity, no fluorescence. |
| 1810 | 1820 | 100 | SILTSTONE: medium dark grey, occasionally medium to dark greenish grey, brownish grey, locally arenaceous, minor fine carbonaceous specks, common fine grained glauconite, trace LIMESTONE fragments, soft to firm, moderately hard in part, blocky to sub blocky. |
| 1820 | 1830 | 95 5 | SILTSTONE: medium to dark greenish grey, medium to dark brownish grey, locally arenaceous, minor fine carbonaceous specks, abundant fine grained glauconite, trace LIMESTONE fragments, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, common off white argillaceous matrix, trace very fine lithics, trace nodular pyrite, common fine grained glauconite, friable, poor visual porosity, no fluorescence. |
| 1830 | 1840 | 95 5 | SILTSTONE: medium to dark greenish grey, medium to dark brownish grey, locally arenaceous, minor fine carbonaceous specks, abundant fine grained glauconite, trace LIMESTONE fragments, trace forams, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, common off white argillaceous matrix, trace very fine lithics, trace nodular pyrite, common fine grained glauconite, friable, poor visual porosity, no fluorescence. |
| 1840 | 1850 | 95 5 | SILTSTONE: medium to dark greenish grey, medium to dark brownish grey, locally arenaceous, minor fine carbonaceous specks, abundant fine grained glauconite, trace LIMESTONE fragments, trace forams, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, common off white argillaceous matrix, trace very fine lithics, trace nodular pyrite, common fine grained glauconite, friable, poor visual porosity, no fluorescence. |
| 1850 | 1860 | 95 5 | SILTSTONE: medium to dark greenish grey, medium to dark brownish grey, locally arenaceous, minor fine carbonaceous specks, abundant fine grained glauconite, trace LIMESTONE fragments, trace forams, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, very light brown, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, common off white argillaceous matrix, trace very fine lithics, trace nodular pyrite, common fine grained glauconite, friable, poor visual porosity, no fluorescence. |
| 1860 | 1870 | 100 | SILTSTONE: medium to dark greenish grey, medium to dark grey, locally arenaceous, minor fine carbonaceous specks, common fine grained glauconite, trace LIMESTONE fragments, trace forams, firm to moderately hard, blocky to sub blocky |
| 1870 | 1875 | 100 | SILTSTONE: medium dark grey, medium to dark greenish grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, common fine grained glauconite, firm to moderately hard, blocky to sub blocky |
| 1875 | 1880 | 100 trace | SILTSTONE: medium dark grey, medium to dark greenish grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, common fine grained glauconite, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, clear, very fine to fine grained, sub angular to sub rounded, well sorted, weak calcareous cement, common off white argillaceous matrix, trace very fine lithics, friable to loose, poor visual porosity, no fluorescence. |
| 1880 | 1885 | 95 5 | SILTSTONE: medium to dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, clear, trace yellow Fe stain, very fine to fine grained, trace loose sub rounded medium quartz grains, sub angular to predominately sub rounded, moderately well sorted, rare weak calcareous cement, common very light grey argillaceous matrix, common fine grained glauconite, trace very fine lithics, friable to loose, poor visual porosity, no fluorescence. |
| 1885 | 1890 | 100 | SILTSTONE: medium to dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky. |
| 1890 | 1895 | 95 5 | SILTSTONE: medium to dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, clear, very fine to fine grained, sub angular to predominately sub rounded, moderately well sorted, rare weak calcareous cement, common very light grey argillaceous matrix, common fine grained glauconite, trace very fine lithics, friable to loose, poor inferred porosity, no fluorescence. |
| 1895 | 1900 | 100 | SILTSTONE: medium to dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky. |
| 1900 | 1905 | 95 5 | SILTSTONE: dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, light grey, clear, very fine to fine grained, sub angular to predominately sub rounded, moderately well sorted, rare weak calcareous cement, common very light grey argillaceous matrix, common fine grained glauconite, trace very fine lithics, friable to loose, poor inferred porosity, no fluorescence. |
| 1905 | 1910 | 95 5 | SILTSTONE: dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky SANDSTONE: translucent, clear, very fine to fine grained, trace medium, sub angular to predominately sub rounded, moderately well sorted, trace very light grey argillaceous matrix, common fine grained glauconite, rare nodular pyrite, predominately loose, poor to fair inferred porosity, no fluorescence. |
| 1910 | 1915 | 100 | SILTSTONE: dark greenish grey, medium dark grey, medium to dark brownish grey, locally arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm to moderately hard, blocky to sub blocky. |
| 1915 | 1920 | 100 | SILTSTONE: dark greenish grey, medium dark grey, medium to dark brownish grey, very finely arenaceous, rare fine carbonaceous specks, abundant fine grained glauconite, firm, blocky to sub blocky. |
| 1920 | 1925 | 100 | SILTSTONE: medium to dark brownish grey, medium to dark greenish grey, argillaceous, locally very finely arenaceous, rare fine carbonaceous specks, minor to common fine grained glauconite, firm, blocky to sub blocky, Note argillaceous content easily washing from samples. |
| 1925 | 1927 | 100 | SILTSTONE: as above. Spot sample. |
| 1925 | 1930 | 100 trace | SILTSTONE: medium to dark brownish grey, medium to dark greenish grey, argillaceous, locally very finely arenaceous, rare fine carbonaceous specks, minor to common fine grained glauconite, firm, blocky to sub blocky, Note argillaceous content easily washing from samples. SANDSTONE. |
| 1930 | 1932 | 85 15 | SILTSTONE: as above. SANDSTONE: very light, off white, translucent, clear, very fine to fine grained, moderately well sorted, sub rounded, abundant off white argillaceous matrix, minor to common fine grained glauconite, rare carbonaceous specks, trace nodular pyrite, soft to friable aggregates, very poor visual porosity, no fluorescence. |
| 1932 | 1935 | 30 70 | SILTSTONE: as above. SANDSTONE: off white, clear to translucent, very fine to fine, moderately well sorted, sub-round, weak siliceous cement, common to abundant off white argillaceous matrix, occasional carbonaceous specks and minor fragments, firm to friable, minor loose, common rock flour, very poor visual porosity, poor inferred porosity, no fluorescence. |
| 1935 | 1937 | 40 60 | SILTSTONE: as above. SANDSTONE: off white, clear to translucent, very fine to fine, moderately well sorted, sub-round, weak siliceous cement, common to abundant off white argillaceous matrix, occasional carbonaceous specks and minor fragments, firm to friable, minor loose, trace fine glauconite grains, common rock flour, very poor visual porosity, poor inferred porosity, no fluorescence. |
| 1937 | 1940 | 40 60 | SILTSTONE: pale brown, medium brown grey in part, argillaceous to minor arenaceous, occasionally glauconite grains and carbonaceous specks, very soft to dispersive, occasionally firm to moderately hard, amorphous, sub-blocky. SANDSTONE: off white, clear to translucent, very fine to fine, moderately well sorted, sub-round, weak siliceous cement, common to abundant off white argillaceous matrix, occasional carbonaceous specks and minor micro laminations, firm to friable, minor loose, trace fine glauconite grains, common rock flour, very poor visual porosity, poor inferred porosity, no fluorescence. |
| 1940 | 1944 | 20 80 | SILTSTONE: pale brown, medium brown grey in part, argillaceous to minor arenaceous, occasionally glauconite grains and carbonaceous specks, very soft to dispersive, occasionally firm to moderately hard, amorphous, sub-blocky. SANDSTONE: off white, clear to translucent, very fine to fine, moderately well sorted, sub-round, weak siliceous cement, common off white argillaceous matrix, occasional carbonaceous specks and minor micro laminations, firm to friable, loose, trace fine glauconite grains, occasional rock flour, poor visual and inferred porosity, no fluorescence. |
| 1944 | 1950 | 100 | SANDSTONE: pale grey, clear to translucent, medium to minor fine, moderately well sorted, sub-angular to sub-round, moderately siliceous cement, occasional off white argillaceous matrix, common to abundant carbonaceous fragments and specks, rare pyrite nodules, minor lithics, generally loose clean grains, occasionally friable, poor to fair visual porosity, fair inferred porosity, no fluorescence. |
| 1950 | 1955 | 90 10 | SANDSTONE: pale grey, clear to translucent, medium to minor fine to coarse, moderately well sorted, sub-angular to sub-round, moderately siliceous cement, occasional off white argillaceous matrix, common to abundant carbonaceous fragments and specks, rare pyrite nodules, minor lithics, generally loose clean grains, occasionally friable, poor to fair visual porosity, fair inferred porosity, no fluoresce. SILTSTONE: pale grey, arenaceous, occasional carbonaceous specks and minor fragments, locally micro mica, firm to occasionally moderately hard, blocky to sub-blocky. |
| 1955 | 1960 | 100 trace | SANDSTONE: pale grey, clear to translucent, medium to minor fine to coarse, moderately well sorted, sub-angular to sub-round, moderately siliceous cement, occasional off white argillaceous matrix, common to abundant carbonaceous fragments and specks, rare pyrite nodules, minor lithics, generally loose clean grains, occasionally friable, poor to fair visual porosity, fair inferred porosity, no fluoresce. SILTSTONE: pale grey, arenaceous, occasional carbonaceous specks and minor fragments, locally micro mica, firm to occasionally moderately hard, blocky to sub-blocky. |
| 1960 | 1965 | 100 | SANDSTONE: pale grey, clear to translucent, fine to medium, occasionally coarse to very coarse, moderately sorted, sub-angular to sub-round, moderately siliceous cement, occasional off white argillaceous matrix, common to abundant carbonaceous fragments and specks, rare pyrite nodules, minor lithics, generally loose clean grains, occasionally friable, poor to fair visual porosity, fair inferred porosity, no fluorescence. |
| 1965 | 1970 | 100 trace | SANDSTONE: off white to pale grey, clear to translucent, medium to coarse, rare fine to very coarse, angular to occasionally sub-round, weak siliceous cement, occasional off white argillaceous matrix, occasional to common carbonaceous specks, minor lithics, rare pyrite nodules, generally loose clean grains, minor friable, fair visual & inferred porosity, no fluorescence. SILTSTONE: pale grey, arenaceous, occasional carbonaceous specks and minor fragments, locally micro mica, firm to occasionally moderately hard, blocky to sub-blocky. |
| 1970 | 1975 | 100 | SANDSTONE: clear to translucent, off white to pale grey, fine to dominantly medium, well sorted, sub-angular to sub-round, weak siliceous cement, minor off white argillaceous matrix, common carbonaceous fragments and specks, minor lithics, generally loose clean grains, rare friable, fair visual & inferred porosity, no fluorescence. |
| 1975 | 1980 | 100 | SANDSTONE: clear to translucent, minor pale grey, medium to occasionally fine, well sorted, angular to sub-angular, minor sub-round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks and lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 1980 | 1985 | 100 | SANDSTONE: clear to translucent, minor pale grey, medium to occasionally fine, well sorted, angular to sub-angular, minor sub-round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks and fragments, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 1985 | 1990 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to medium, well sorted, angular to sub-angular, minor sub-round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks and fragments, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 1990 | 1995 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to medium, well sorted, angular to sub-angular, minor sub-round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks and fragments, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 1995 | 2000 | 100 | SANDSTONE: clear to translucent, minor pale grey, medium to dominantly fine, well sorted, sub-angular to sub-round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks and fragments, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2000 | 2005 | 100 | SANDSTONE: clear to translucent, minor pale grey, medium to dominantly fine, well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white argillaceous matrix, occasional carbonaceous specks and fragments, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2005 | 2010 | 100 | SANDSTONE: clear to translucent, fine, minor medium, well sorted, sub-angular to sub-round, weak siliceous cement, rare pale grey to off white argillaceous matrix, minor carbonaceous specks, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2010 | 2015 | 100 | SANDSTONE: clear to translucent, fine, minor medium, well sorted, sub-angular to sub-round, weak siliceous cement, rare pale grey to off white argillaceous matrix, minor carbonaceous specks, rare pyrite nodules, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2015 | 2020 | 100 | SANDSTONE: clear to translucent, minor off white to pale grey, fine to medium, rare coarse, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, rare off white argillaceous matrix, minor carbonaceous specks, generally loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2020 | 2025 | 100 | SANDSTONE: clear to translucent, minor off white to pale grey, fine to medium, rare coarse, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, rare off white argillaceous matrix, minor carbonaceous specks, rare pyrite nodules, generally loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2025 | 2030 | 100 | SANDSTONE: clear to translucent, fine to occasionally medium, well sorted, sub-angular to sub-round, weak siliceous cement, minor pale grey to off white argillaceous matrix, rare carbonaceous specks, generally loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2030 | 2035 | 100 | SANDSTONE: clear to translucent, fine to occasionally medium, well sorted, sub-angular to sub-round, weak siliceous cement, minor pale grey to off white argillaceous matrix, rare carbonaceous specks occasional lithics, generally loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2035 | 2040 | 100 | SANDSTONE: clear to translucent, fine to occasionally medium, well sorted, sub-angular to sub-round, weak siliceous cement, minor pale grey to off white argillaceous matrix, rare carbonaceous specks occasional lithics, generally loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2040 | 2045 | 100 | SANDSTONE: clear to translucent, off white, fine to medium, moderately sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, minor lithics and carbonaceous specks, loose, friable, poor visual porosity, poor to fair inferred porosity, no fluorescence. |
| 2045 | 2050 | 100 | SANDSTONE: clear to translucent, off white, fine to medium, moderately sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, minor lithics and carbonaceous specks, loose, friable, poor visual porosity, poor to fair inferred porosity, no fluorescence. |
| 2050 | 2055 | 100 | SANDSTONE: clear to translucent, off white, fine to occasionally medium, moderately sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, minor lithics and carbonaceous specks, loose, friable, poor visual porosity, poor to fair inferred porosity, no fluorescence. |
| 2055 | 2060 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine to medium in part, moderately well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, minor carbonaceous specks & lithics, loose, friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2060 | 2065 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine to medium in part, moderately well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, minor carbonaceous specks & lithics, loose, friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2065 | 2070 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine to medium in part, moderately well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, minor carbonaceous specks & lithics, loose, friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2070 | 2075 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine, occasionally medium in part, well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, minor carbonaceous specks & lithics, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2075 | 2080 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine, occasionally medium to rare very fine, well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, minor carbonaceous specks & lithics, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2080 | 2085 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine, occasionally medium to rare very fine, well sorted, sub-angular to sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, minor carbonaceous specks & lithics, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2085 | 2090 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to very fine, occasionally medium, well sorted, sub-angular to sub-round, weak siliceous cement, minor pale grey argillaceous matrix, minor lithics and carbonaceous specks, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2090 | 2095 | 100 | SANDSTONE: clear to translucent, minor pale grey, very fine to medium, dominantly fine, well sorted, dominantly sub-angular to sub-round, weak siliceous cement, minor pale grey argillaceous matrix, minor lithics and carbonaceous specks, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2095 | 2100 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to medium, well sorted, dominantly sub-angular to sub-round, weak siliceous cement, minor pale grey argillaceous matrix, minor lithics and carbonaceous specks, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2100 | 2105 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to medium, well sorted, dominantly sub-angular to sub-round, weak siliceous cement, minor pale grey argillaceous matrix, minor lithics and carbonaceous specks, rare pale orange grains, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2105 | 2110 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to medium, well sorted, dominantly sub-angular to sub-round, weak siliceous cement, minor pale grey argillaceous matrix, minor lithics and carbonaceous specks, rare pale orange grains, loose, minor friable, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2110 | 2115 | 100 | SANDSTONE: clear to translucent, off white, fine, occasionally medium, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional off white argillaceous matrix, minor lithics, occasional carbonaceous specks, rare pyrite nodules, generally loose grains, friable to rare moderately hard, poor visual porosity, fair inferred porosity, no fluorescence. |
| 2115 | 2120 | 100 | SANDSTONE: translucent, clear, light grey, fine to occasionally medium grained, well sorted, sub angular to predominately sub rounded, weak siliceous cement, trace calcareous cement, minor light grey argillaceous matrix, rare fine grained lithics, minor carbonaceous flecks, predominately loose to friable, minor moderately hard aggregates, fair inferred porosity, no fluorescence. |
| 2120 | 2125 | 90 10 | SANDSTONE: white, light grey, translucent, clear in part, fine to predominately medium grained, sub angular to sub rounded, moderately sorted, abundant white calcareous cement, minor light grey argillaceous matrix, trace fine pyrite nodules, trace orange and light green lithics, minor carbonaceous flecks, friable to occasionally moderately hard aggregates, poor visual porosity, 90% dull orange mineral fluorescence. SILTSTONE: medium to dark brownish grey, dark grey, common carbonaceous flecks, trace micro mica, moderately hard, sub blocky to sub fissile. |
| 2125 | 2130 | 100 | SANDSTONE: white, light grey, translucent, clear in part, fine to predominately medium grained, trace loose sub rounded coarse quartz grains, sub angular to sub rounded, moderately sorted, abundant white calcareous cement, minor light grey argillaceous matrix, trace red/orange and light green lithics, minor carbonaceous flecks, friable to occasionally moderately hard aggregates, poor visual porosity, 80% dull orange mineral fluorescence. |
| 2130 | 2135 | 100 | SANDSTONE: white, light grey, translucent, clear, fine to predominately medium grained, trace loose sub rounded coarse quartz grains, sub angular to sub rounded, moderately sorted, common white calcareous cement, minor light grey argillaceous matrix, trace red/orange and light green lithics, minor carbonaceous flecks, friable to moderately hard aggregates, poor visual porosity, 60% dull orange mineral fluorescence. |
| 2135 | 2140 | 100 | SANDSTONE: white, light grey, translucent, clear, fine to predominately medium grained, sub angular to sub rounded, moderately well sorted, common white calcareous cement, minor light grey / white argillaceous matrix, trace lithics, minor carbonaceous flecks, friable to moderately hard aggregates, loose in part, poor to fair visual porosity, 30% dull orange mineral fluorescence. |
| 2140 | 2145 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, moderately well sorted, sub angular to sub rounded, weak siliceous cement, minor light grey / off white argillaceous matrix, trace fine pyrite nodules, trace lithics, minor carbonaceous flecks, predominately loose quartz grains, friable to moderately hard aggregates in part, fair inferred porosity, trace mineral fluorescence. |
| 2145 | 2150 | 100 | SANDSTONE: translucent, light grey, clear, fine to predominately medium grained, moderately well sorted, sub angular to predominately sub rounded, rare weak siliceous cement, trace light grey argillaceous matrix, trace lithics, rare carbonaceous flecks, predominately loose clean quartz grains, trace friable aggregates, good inferred porosity, no fluorescence. |
| 2150 | 2155 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, rare weak siliceous cement, trace light grey argillaceous matrix, trace lithics, common carbonaceous flecks, predominately loose clean quartz grains, trace friable aggregates, good inferred porosity, no fluorescence. |
| 2155 | 2160 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, rare weak siliceous cement, rare to minor light grey argillaceous matrix, trace red lithics, minor carbonaceous flecks, predominately loose clean quartz grains, minor friable aggregates, good inferred porosity, no fluorescence. |
| 2160 | 2165 | 100 | SANDSTONE: light grey, translucent, clear, fine to predominately medium occasionally coarse, poor to fair sorting, sub angular to predominately sub rounded, rare weak siliceous cement, minor light grey argillaceous matrix, trace red lithics, common carbonaceous flecks, loose to friable aggregates, fair inferred porosity, no fluorescence. |
| 2165 | 2170 | 100 | SANDSTONE: light grey, translucent, clear, fine to predominately medium occasionally coarse, poor to fair sorting, sub angular to predominately sub rounded, rare weak siliceous cement, minor light grey argillaceous matrix, trace red lithics, common carbonaceous flecks, loose to friable aggregates, fair inferred porosity, no fluorescence. |
| 2170 | 2175 | 100 | SANDSTONE: light grey, translucent, clear, fine to predominately medium, rare coarse, fair sorting, sub angular to predominately sub rounded, rare weak siliceous cement, minor light grey argillaceous matrix, trace red lithics, minor carbonaceous flecks, loose to friable aggregates, fair inferred porosity, no fluorescence. |
| 2175 | 2180 | 100 | SANDSTONE: light grey, translucent, clear, fine to predominately medium, rare coarse, poor to fair sorting, sub angular to predominately sub rounded, rare weak siliceous cement, minor to common light grey argillaceous matrix, trace red lithics, minor carbonaceous flecks, loose to friable aggregates, fair inferred porosity, no fluorescence. |
| 2180 | 2185 | 100 | SANDSTONE: translucent, light grey, clear, fine to predominately medium grained, minor coarse, sub angular to sub rounded, moderately sorted, rare weak siliceous cement, minor to common calcareous cement, minor light grey argillaceous matrix, common carbonaceous flecks, trace light green and red lithics, rare biotite flecks, loose to friable aggregates, minor moderately hard, fair visual & fair to good inferred porosity, 30% dull orange mineral fluorescence. |
| 2185 | 2190 | 100 | SANDSTONE: light grey, translucent, clear, fine to medium grained, sub angular to sub rounded, well sorted, rare weak siliceous cement, common calcareous cement, minor light grey argillaceous matrix, common carbonaceous fragments, trace nodular pyrite, trace light green and red lithics, rare biotite flecks, loose to friable aggregates, minor moderately hard, fair visual and fair to good inferred porosity, 30% dull orange mineral fluorescence. |
| 2190 | 2195 | 95 5 | SANDSTONE: light grey, white, translucent, clear, fine to medium grained, sub angular to sub rounded, moderately sorted, common white calcareous cement, minor light grey argillaceous matrix, trace red & light green lithics, common carbonaceous flecks / fragments, friable to occasionally moderately hard aggregates, poor to fair visual porosity, 50% dull orange mineral fluorescence. SILTSTONE: medium to dark brownish grey, dark grey, common carbonaceous flecks, moderately hard, sub blocky to sub fissile. |
| 2195 | 2199 | 95 5 | SANDSTONE: light grey, white, translucent, clear, fine to medium grained, trace coarse, sub angular to sub rounded, moderately sorted, common white calcareous cement, minor light grey argillaceous matrix, trace red & light green lithics, common carbonaceous fragments, friable to occasionally moderately hard aggregates, poor to fair visual & inferred porosity, 20% dull orange mineral fluorescence. SILTSTONE: medium to dark brownish grey, carbonaceous in part, dark grey, common carbonaceous flecks, trace disseminated pyrite, moderately hard, sub blocky to sub fissile. |
| 2199 | 2202 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, moderately well sorted, sub angular to sub rounded, rare weak siliceous cement, trace light grey argillaceous matrix, trace red & light green lithics, common carbonaceous flecks, trace biotite, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2202 | 2205 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, moderately well sorted, sub angular to sub rounded, rare weak siliceous cement, trace light grey argillaceous matrix, trace red & light green lithics, common carbonaceous flecks, trace biotite, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2205 | 2210 | 100 | SANDSTONE: clear to dominantly translucent, occasionally pale grey, medium grains, minor coarse, well sorted, angular to occasionally sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional to common carbonaceous specks, minor orange grains, generally loose clean grains, friable to occasionally moderately hard, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2210 | 2215 | 100 | SANDSTONE: clear to translucent, occasionally pale grey, medium grains, minor coarse, well sorted, angular to occasionally sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional to common carbonaceous specks, minor lithics, generally loose clean grains, friable to occasionally moderately hard, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2215 | 2220 | 100 | SANDSTONE: clear to translucent, occasionally pale grey, medium grains, minor coarse, well sorted, angular to occasionally sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional to common carbonaceous specks and fragments, minor lithics, generally loose clean grains, friable, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2220 | 2225 | 100 | SANDSTONE: clear to translucent, occasionally pale grey, medium grains, very well sorted, angular to occasionally sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional to common carbonaceous specks and fragments, minor orange lithics, generally loose clean grains, friable, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2225 | 2230 | 100 | SANDSTONE: clear to translucent, off white, fine to medium grains, well sorted, sub-angular to sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional carbonaceous specks and fragments, minor lithics, generally loose clean grains, rare friable aggregates, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2230 | 2235 | 90 10 | SANDSTONE: clear to translucent, off white, fine to medium grains, occasionally very fine, well sorted, sub-angular to sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional carbonaceous specks and fragments, minor orange lithics, generally loose clean grains, rare friable aggregates, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. SILTSTONE: pale grey, argillaceous, minor carbonaceous specks, dispersive to firm, amorphous, occasionally sub-blocky. |
| 2235 | 2240 | 100 | SANDSTONE: clear to translucent, off white, fine to medium grains, occasionally very fine, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional carbonaceous specks and fragments, minor orange lithics, generally loose clean grains, rare friable aggregates, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2240 | 2245 | 100 | SANDSTONE: clear to translucent, off white, very fine to medium grains, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional carbonaceous specks and fragments, minor orange lithics, generally loose clean grains, rare friable aggregates, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2245 | 2250 | 90 10 | SANDSTONE: clear to translucent, off white, fine to medium grains, occasionally very fine, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional carbonaceous specks and fragments, rare orange lithics, generally loose clean grains, rare friable aggregates, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. SILTSTONE: pale grey, argillaceous, minor carbonaceous specks, dispersive to minor firm, amorphous, occasionally sub-blocky. |
| 2250 | 2255 | 100 | SANDSTONE: clear to translucent, off white, fine, very fine to medium in part, moderately sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional to common off white argillaceous matrix, occasional carbonaceous specks, rare orange lithics, generally loose clean grains, rare friable aggregates, poor to fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2255 | 2260 | 100 | SANDSTONE: clear to dominantly translucent, off white, medium, occasionally fine, well sorted, angular to sub-round, weak siliceous cement, occasional off white argillaceous matrix, minor lithics, occasional carbonaceous specks, occasional orange grains, loose clean grains, minor friable, fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2260 | 2265 | 100 | SANDSTONE: clear to dominantly translucent, off white, medium, occasionally fine, well sorted, angular to sub-round, dominantly angular to sub-angular, weak siliceous cement, occasional off white argillaceous matrix, minor lithics, occasional carbonaceous specks, occasional orange grains, loose clean grains, minor friable, fair visual porosity, fair to good inferred porosity, no fluorescence. |
| 2265 | 2270 | 100 | SANDSTONE: clear to translucent, occasionally pale orange, fine to coarse, occasionally very fine to very coarse, poor sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional off white argillaceous matrix, minor lithics, occasional carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2270 | 2275 | 100 | SANDSTONE: clear to translucent, occasionally pale orange, fine to medium, occasionally very fine to rare very coarse, poor sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional off white argillaceous matrix, minor lithics, occasional carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2275 | 2280 | 100 | SANDSTONE: clear to translucent, occasionally pale orange, fine to medium, occasionally very fine, poor sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional off white argillaceous matrix, minor lithics, occasional carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2280 | 2283 | 100 | SANDSTONE: clear to translucent, minor pale grey, generally medium, minor fine, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, occasional carbonaceous specks and minor fragments, minor orange grains, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2283 | 2286 | 100 | SANDSTONE: clear to translucent, minor pale grey, fine to medium, well sorted, sub-angular to dominantly sub-round, weak siliceous cement, occasional off white to pale grey argillaceous matrix, occasional carbonaceous specks and minor fragments, rare orange grains, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2286 | 2289 | 100 | SANDSTONE: clear to translucent, fine to dominantly medium, minor coarse to very coarse, moderately well sorted, sub-angular to dominantly sub-round, minor round, weak siliceous cement, minor off white argillaceous matrix, minor carbonaceous specks and fragments, loose, good inferred porosity, no fluorescence. |
| 2289 | 2292 | 100 | SANDSTONE: clear to translucent, pale orange in part, fine to dominantly medium, minor coarse, moderately well sorted, sub-angular to dominantly sub-round, minor round, weak siliceous cement, minor off white argillaceous matrix, minor carbonaceous specks and fragments, loose, good inferred porosity, no fluorescence. |
| 2292 | 2295 | 100 | SANDSTONE: clear to translucent, pale orange in part, fine to dominantly medium, trace coarse, moderately well sorted, sub-angular to dominantly sub-round, minor round, weak siliceous cement, minor off white argillaceous matrix, minor carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2295 | 2298 | 100 | SANDSTONE: clear to translucent, pale orange in part, fine to dominantly medium, moderately well sorted, sub-angular to dominantly sub-round, minor round, weak siliceous cement, occasional off white argillaceous matrix, minor carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2298 | 2301 | 100 | SANDSTONE: clear to translucent, pale orange in part, fine to dominantly medium, moderately well sorted, angular to sub-round, weak siliceous cement, rare off white argillaceous matrix, minor carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2301 | 2304 | 100 | SANDSTONE: clear to minor translucent, fine to dominantly medium, moderately well sorted, angular to sub-round, weak siliceous cement, rare off white argillaceous matrix, minor carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2304 | 2307 | 100 | SANDSTONE: clear to minor translucent, dominantly medium, occasional fine grains, moderately well sorted, angular to sub-round, weak siliceous cement, rare off white argillaceous matrix, minor carbonaceous specks, loose, good inferred porosity, no fluorescence. |
| 2307 | 2316 | 100 | SANDSTONE: clear to translucent, fine to medium, well sorted, sub-angular to dominantly sub-round, occasionally round, weak siliceous cement, minor off white argillaceous matrix, minor lithics and carbonaceous specks, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2316 | 2319 | 100 | SANDSTONE: clear to translucent, fine to medium, well sorted, sub-angular to dominantly sub-round, occasionally round, weak siliceous cement, minor off white argillaceous matrix, occasional carbonaceous specks, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2319 | 2322 | 100 | SANDSTONE: clear to translucent, fine to medium, rare very fine, well sorted, sub-angular to dominantly sub-round, occasionally round, weak siliceous cement, minor off white argillaceous matrix, occasional carbonaceous specks, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2322 | 2325 | 100 | SANDSTONE: clear to translucent, fine to occasionally very fine, minor medium, moderately well sorted, sub-angular to dominantly sub-round, occasionally round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks, minor lithics, loose clean grains, fair to good inferred porosity, no fluorescence. |
| 2325 | 2328 | 100 | SANDSTONE: clear to translucent, fine to occasionally very fine, minor medium, moderately well sorted, sub-angular to dominantly sub-round, occasionally round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks, minor lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2328 | 2331 | 100 | SANDSTONE: clear to translucent, pale grey, fine to occasionally very fine, minor medium, moderately well sorted, sub-angular to dominantly sub-round, occasionally round, weak siliceous cement, rare off white argillaceous matrix, occasional carbonaceous specks and rare laminations, minor lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2331 | 2334 | 100 | SANDSTONE: translucent, clear, light grey, very fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, weak siliceous cement, trace off white argillaceous matrix, rare carbonaceous specks / flecks, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2334 | 2337 | 100 | SANDSTONE: translucent, clear, light grey, very fine to medium grained, rare coarse to very coarse round quartz grains, moderately sorted, sub angular to predominately sub rounded, weak siliceous cement, trace off white argillaceous matrix, minor carbonaceous fragments, rare light red and green lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2337 | 2340 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, rare coarse, moderately well sorted, sub angular to predominately sub rounded, rare weak siliceous cement, trace off white argillaceous matrix, common carbonaceous fragments, rare red and light green lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2340 | 2343 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, rare coarse, moderately well sorted, sub angular to predominately sub rounded, rare weak siliceous cement, trace off white argillaceous matrix, common carbonaceous fragments, rare red and light green lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2343 | 2346 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, minor coarse, moderately sorted, sub angular to predominately sub rounded, rare weak siliceous cement, minor off white argillaceous matrix, minor carbonaceous fragments, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2346 | 2349 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, rare coarse, moderately sorted, sub angular to predominately sub rounded, rare weak siliceous cement, minor to common light grey argillaceous matrix, rare carbonaceous fragments, trace lithics, predominately loose clean quartz grains, friable aggregates in part, moderately good inferred porosity, trace dull orange mineral fluorescence. |
| 2349 | 2352 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, common carbonaceous flecks / fragments, rare lithics, trace nodular pyrite, trace mica flecks, predominately loose clean quartz grains, trace friable aggregates in part, good inferred porosity, no fluorescence. |
| 2352 | 2355 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, common carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates in part, good inferred porosity, no fluorescence. |
| 2355 | 2358 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, trace coarse, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, common carbonaceous flecks, rare lithics, trace mica, predominately loose clean quartz grains, trace friable aggregates in part, good inferred porosity, no fluorescence. Note: slight increase of metal in cuttings. |
| 2358 | 2361 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, common carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, good inferred porosity, no fluorescence. |
| 2361 | 2364 | 100 | SANDSTONE: translucent, light grey, clear, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, common carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, good inferred porosity, no fluorescence. |
| 2364 | 2367 | 100 | SANDSTONE: light grey, translucent, clear, fine to medium grained, rare coarse, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, common light grey argillaceous matrix, minor carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2367 | 2370 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, rare light grey argillaceous matrix, common carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, good inferred porosity, no fluorescence. |
| 2370 | 2373 | 100 | SANDSTONE: light grey, translucent, clear, fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, common light grey argillaceous matrix, minor carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2373 | 2376 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, rare light grey argillaceous matrix, common carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, good inferred porosity, no fluorescence. |
| 2376 | 2379 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2379 | 2382 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2382 | 2385 | 100 | SANDSTONE: light grey, translucent, clear, fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, common light grey argillaceous matrix, minor carbonaceous flecks, rare lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2385 | 2388 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2388 | 2391 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, trace friable aggregates, fair to good inferred porosity, no fluorescence. |
| 2391 | 2394 | 100 | SANDSTONE: translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2394 | 2397 | 100 | SANDSTONE: translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, moderate to good inferred porosity, no fluorescence. |
| 2397 | 2400 | 100 | SANDSTONE: translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, rare carbonaceous flecks, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2400 | 2403 | 100 | SANDSTONE: translucent, clear, light grey, fine to predominately medium grained, trace coarse, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous flecks, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2403 | 2406 | 100 | SANDSTONE: translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous flecks, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2406 | 2409 | 100 | SANDSTONE: as above, translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous flecks, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2409 | 2412 | 100 | SANDSTONE: as above, translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor to common carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2412 | 2415 | 100 | SANDSTONE: generally as above, translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2415 | 2418 | 100 | SANDSTONE: generally as above, translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2418 | 2421 | 100 | SANDSTONE: generally as above, translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2421 | 2424 | 100 | SANDSTONE: as above, translucent, clear, light grey, fine to predominately medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2424 | 2427 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2427 | 2430 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2430 | 2433 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2433 | 2436 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2436 | 2439 | 100 | SANDSTONE: generally as above, translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2439 | 2442 | 100 | SANDSTONE: generally as above, translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, trace light grey argillaceous matrix, rare carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2442 | 2445 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, rare light grey argillaceous matrix, trace carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2445 | 2448 | 100 | SANDSTONE: translucent, clear, light grey, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, rare light grey argillaceous matrix, trace carbonaceous flecks, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2448 | 2451 | 100 | SANDSTONE: light grey, off white, translucent, clear, fine to medium grained, well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor to common light grey argillaceous matrix, rare carbonaceous flecks / fragments, trace lithics, predominately loose clean quartz grains, friable aggregates in part, fair to good inferred porosity, no fluorescence. |
| 2451 | 2454 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous fragments, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2454 | 2457 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately well sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous fragments, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2457 | 2460 | 100 | SANDSTONE: generally as above, translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous fragments, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2460 | 2463 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous fragments, trace lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2463 | 2466 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous fragments, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2466 | 2469 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, minor carbonaceous fragments, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2469 | 2472 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, rare light grey argillaceous matrix, common carbonaceous fragments, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2472 | 2475 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, rare light grey argillaceous matrix, common carbonaceous fragments, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2475 | 2478 | 100 | SANDSTONE: translucent, light grey, clear, very fine to medium grained, moderately sorted, sub angular to predominately sub rounded, trace weak siliceous cement, minor light grey argillaceous matrix, common carbonaceous fragments, rare lithics, predominately loose clean quartz grains, good inferred porosity, no fluorescence. |
| 2478 | 2481 | 100 | SANDSTONE: clear to dominantly translucent, pale grey to off white, medium to occasionally fine, moderately well sorted, sub-angular to sub-round, occasionally angular, weak siliceous cement, minor off white to pale grey argillaceous matrix, occasional to common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2481 | 2484 | 100 | SANDSTONE: clear to dominantly translucent, pale grey to off white, medium, minor fine to very fine, moderately well sorted, sub-angular to sub-round, occasionally angular, weak siliceous cement, minor off white to pale grey argillaceous matrix, occasional to common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2484 | 2487 | 100 | SANDSTONE: clear to translucent, pale grey to off white, medium, minor fine to rare very fine, moderately well sorted, sub-angular to sub-round, occasionally round, weak siliceous cement, minor off white to pale grey argillaceous matrix, occasional to common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2487 | 2490 | 100 | SANDSTONE: clear to translucent, pale grey to off white, medium, minor fine, well sorted, sub-angular to sub-round, occasionally round, weak siliceous cement, minor off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2490 | 2493 | 100 | SANDSTONE: clear to translucent, pale grey to off white, medium, minor fine, well sorted, sub-angular to sub-round, occasionally round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2493 | 2496 | 100 | SANDSTONE: clear to translucent, pale grey to off white, medium, minor fine to coarse, moderately well sorted, sub-angular to sub-round, occasionally round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2496 | 2499 | 100 | SANDSTONE: clear to translucent, pale grey to off white, medium, minor fine to rare coarse, moderately well sorted, sub-angular to sub-round, occasionally round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, rare lithics, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2499 | 2502 | 100 | SANDSTONE: clear to translucent, pale grey to off white, medium, minor fine to rare coarse, moderately well sorted, sub-angular to sub-round, occasionally round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, rare pyrite nodules, rare lithics, occasional orange grains, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2502 | 2505 | 100 | SANDSTONE: clear to translucent, pale grey to off white, fine too occasionally medium, well sorted, sub-round to round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, rare pyrite nodules, rare lithics, occasional orange grains, generally loose clean grains, good inferred porosity, no fluorescence. |
| 2505 | 2508 | 90 10 | SANDSTONE: clear to translucent, pale grey, fine to occasionally medium, well sorted, sub-round to round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, occasional pyrite nodules, rare lithics, occasional orange grains, generally loose clean grains, good inferred porosity, no fluorescence. SILTSTONE: pale grey, minor medium to dark grey, argillaceous, rare arenaceous, occasional to common carbonaceous specks and fragments, soft to minor firm, dispersive, amorphous, sub-blocky. |
| 2508 | 2511 | 95 5 | SANDSTONE: clear to translucent, pale grey, fine to occasionally medium, rare coarse to very coarse, moderately sorted, sub-angular to sub-round, weak siliceous cement, rare off white to pale grey argillaceous matrix, common carbonaceous specks and fragments, occasional pyrite nodules, rare lithics, occasional orange grains, generally loose clean grains, good inferred porosity, no fluorescence. SILTSTONE: pale grey, minor medium to dark grey, argillaceous, rare arenaceous, occasional to common carbonaceous specks and fragments, minor pyrite nodules, soft to minor firm, dispersive, amorphous, sub-blocky. Note: dispersive silts washing out of samples. |
| 2511 | 2514 | 95 5 | SANDSTONE: clear to translucent, pale grey, fine to occasionally medium, moderately well sorted, sub-angular to sub-round, weak siliceous cement, rare pale grey argillaceous matrix, common carbonaceous specks and fragments, rare pyrite nodules, rare lithics, occasional orange grains, generally loose clean grains, good inferred porosity, no fluorescence. SILTSTONE: pale grey, minor medium grey, argillaceous, rare arenaceous, occasional to common carbonaceous specks and fragments, soft to dispersive, amorphous, rare sub-blocky. Note: dispersive silts washing out of samples. |
| 2514 | 2517 Total Depth | 95 5 | SANDSTONE: clear to translucent, pale grey, fine to occasionally medium, rare coarse, moderately well sorted, sub-angular to sub-round, weak siliceous cement, rare pale grey argillaceous matrix, common carbonaceous specks and fragments, rare pyrite nodules, rare lithics, rare orange grains, loose clean grains, good inferred porosity, no fluorescence. SILTSTONE: pale grey, minor medium grey, argillaceous, rare arenaceous, occasional carbonaceous specks and fragments, soft to dispersive, amorphous, rare sub-blocky. Note: dispersive silts washing out of samples. |