LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 44 | DFS: | 44 | DATE : | 29-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : |  |
| TOTAL FUEL : | 1,800 | FUEL USAGE : | 1,300 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Rigged down cementing head –Backed out landing joint -Rigging down the BOP at 06.00hrs |
| Next 24 Hrs Op | Lay out BOP –Wellhead spools-Install 10K Tree |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| j Bit Number |  |  |  | Drilling |  |  | Density | 1.146 | S.G. |
| Size (mm) |  |  |  | Tripping |  |  | Viscosity | 38 | Sec |
| Make |  |  |  | Standy | 3.30 |  | Water Loss | 34 | Cc |
| Type |  |  |  | Wireline logging |  |  | pH | 8.5 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 8 / 12 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing | 17.50 |  | Gels | 1 / 2 | S/m |
| Depth in (m) |  |  |  | Cementing | 3.00 |  | Sand | 0.40 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing |  |  | Solids | 7.8 | % Vol |
| Total Metres |  |  |  | Circulate & Condition |  |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 7,875 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 14,500 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | K+ | 10,500 |  |
| Condition |  |  |  | Reaming |  |  | KCL | 2.0 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 465 |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 94,834 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 03.30 | Rig on standby wait on new Float equipment for csg |  |  | ° at |  | m |  | Widcat-420 | 2 |
| 03.30 | 06.00 | Made up new Shoe and Float collar |  |  | ° at |  | m |  |  |  |
| 06.00 | 21.00 | Ran 4½" Casing 210 Joints plus landing jnt |  |  | ° at |  | m |  |  |  |
| 21.00 | 22.00 | Rigged up Halliburton circulated hole volume |  |  | ° at |  | m |  |  |  |
| 22.00 | 24.00 | Tested surface lines-held meeting –cemented casing |  |  | ° at |  | m |  |  |  |
|  |  |  |  |  | ° at |  | m |  |  |  |
|  |  | Full circulation when circulated with mud |  |  | ° at |  | m |  |  |  |
|  |  | Full returns during cementing |  |  |  |  |
|  |  | No returns to surface when pumping wiper plug |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
|  |  |  |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 4½" | inch |
|  |  | Hunt 15 camp 4 Schlumberger stby |  | Class Bulk |  |  | Weight | 41x15.1-169x13.5 | ppf |
|  |  | Lakes 3 |  | % |  |  |  | Grade | P110 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 210 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | 2474.32 | m |
| Days since | LTA | 470 |  | Av. Wt |  |  | Shoe | 2478.72 | m |

,66