LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 16 | DFS: | 16 | DATE : | 1-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1,478 | LAST DEPTH : | 1,448 | 24 HR PROGRESS: | 30 | PTD : |  |
| TOTAL FUEL : | 7,200 | FUEL USAGE : | 1,300 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Making up DST Manifold on the Rig floor |
| Next 24 Hrs Op | Perform DST # 1 with Packer in cased hole |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 5 |  |  | Drilling | 2.5 |  | Density | 1.176 | S.G. |
| Size (mm) | 156 |  |  | Tripping | 8.00 |  | Viscosity | 44 | Sec |
| Make | Smith |  |  | Surveys | 1.0 |  | Water Loss |  | Cc |
| Type | MDi613 |  |  | Wireline logging |  |  | pH | 9.5 | Strip |
| IADC Code |  |  |  | Testing/tools | 11.0 |  | Filter Cake | 2 | 32 nd |
| Serial Number | JD1042 |  |  | Circulate Sample |  |  | PV / YP | 15/ 25 | Cp/lb/100’ |
| Nozzles (32) | 3 x 12 |  |  | Casing |  |  | Gels | 4 / 6 | S/m |
| Depth in (m) | 1378 |  |  | Cementing |  |  | Sand | 0.40 | % Vol |
| Depth out (m) | 1478 |  |  | Surveys |  |  | Solids | 9.5 | % Vol |
| Total Metres | 100 |  |  | Circulate & Condition | 1.0 |  | Oil |  | % Vol |
| Hours | 7.5 |  |  | Rig Service/slip & cut | 0.5 |  | K+ |  | Mg/l |
| WOB (kg) | 2,000 |  |  | Rig up/ d own bop |  |  | Chlorides | 17,800 | Mg/l |
| RPM | 100 |  |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | AS NEW |  |  | Reaming |  |  | KCL | 2.0 | % |
| Impact Force | 257 |  |  | Wait On Cement |  |  | Daily Cost $ | 7,986 |
| Jet Velocity | 219 |  |  | Test BOPs |  |  | Cum Cost $ | 55,151 |
| B.H.A.: 5 | 156mm Bit-NBS with Float and Totco ring on top of NBS-NMDC-Stab-2 x 4¾" DC-STB-12 x 4¾" DC-Jars-2 x 4¾" DC |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 1½º N60E | ° at | 1354 | m |  | Type | Amount |
| 0000 | 02.30 | Drilled 156mm hole from 1448m to 1478m |  |  | ° at |  | m |  | AMC Biocide G | 2 |
| 02.30 | 03.00 | Circulated bottoms up |  |  | ° at |  | m |  | Sodium sulphite | 4 |
| 03.30 | 04.00 | Ran survey on wireline |  |  | ° at |  | m |  | Barytes | 48 |
| 04.00 | 09.30 | Tripped out for DST |  |  | ° at |  | m |  |  |  |
| 09.30 | 10.00 | Serviced the Rig |  |  | ° at |  | m |  |  |  |
| 10.00 | 12,00 | Wait on DST gauges to arrive on site ex Adelaide |  |  | ° at |  | m |  | Residrill | 88 |
| 12.00 | 19.00 | Made up DST tools –continued to wait for gauges |  |  | ° at |  | m |  |  |  |
| 19.00 | 21.00 | Made up remainder of test tools installed gauges |  |  |  |  |
| 21.00 | 23.30 | Tripped in hole to 713m |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 23.30 | 24.00 | Malfunction in DST tool fluid going into pipe |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure | 7,700 | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP | 220 | Ft/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC | 371 | Ft//mn |
|  |  |  |  | SPM |  |  | SPM | 100 |
|  |  |  |  | LPM |  |  | GPM | 227 |
|  |  | Held weekly safety meeting |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 18 Camp 4 |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 4 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 4 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA |  |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66