LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 40 | DFS: | 40 | DATE : | 25-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 4,500 | FUEL USAGE : | 800 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | RIH 1335-1526m-Circ 9.7in 9.5 out-RIH to1909m-Circ 9.6in 10.3 out-RIH to 2195m-Circ 9.6in 9.4 out-RIH to 2253m-PU Kelly |
| Next 24 Hrs Op | Continue wiper trip to bottom-wash and ream where required-circulate and condition mud –lay out drill string |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| j Bit Number | 7 RR# 6 |  |  | Drilling |  |  | Density | 1.152 | S.G. |
| Size (mm) | 156 |  |  | Tripping | 6.00 |  | Viscosity | 32 | Sec |
| Make | Reed |  |  | Downtime ( Float ) |  |  | Water Loss | 38 | Cc |
| Type | R22AP |  |  | Wireline logging |  |  | pH | 7.5 | Strip |
| IADC Code | 5-1-7 |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number | KD1019 |  |  | Circulate Sample |  |  | PV / YP | 6 / 4 | Cp/lb/100’ |
| Nozzles (32) | 14-14-14 |  |  | Casing |  |  | Gels | 1 / 2 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.25 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing | 17.00 |  | Solids | 9.3 | % Vol |
| Total Metres | Wiper trip |  |  | Circulate & Condition | 1.00 |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut |  |  | K+ | 7,875 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 14,000 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | K+ | 10,500 |  |
| Condition |  |  |  | Reaming |  |  | KCL | 2.0 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ |  |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 91,615 |
| B.H.A.: | 156mm Bit-Bit Sub-14 x 4¾" Drill Collars- |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 03.30 | Continued to trip in hole with DST tools to 1120m |  |  | ° at |  | m |  | AMC Pac L |  |
| 03.30 | 05.00 | Rigged up and tested surface equipment |  |  | ° at |  | m |  | AMC Pac R |  |
| 05.00 | 06.00 | Set packers to test perforated interval 1109 to 1112m |  |  | ° at |  | m |  | Lakes Pac R |  |
| 06.00 | 06.30 | Opened tool for 10min then closed in for 30 min |  |  | ° at |  | m |  | Xan Bore |  |
| 06.30 | 08.30 | Flowed well for second flow good bubbles in bucket |  |  | ° at |  | m |  | Bayrtes |  |
| 08.30 | 11.30 | Shut in well for second build up period |  |  | ° at |  | m |  | Potassium Chloride |  |
| 11.30 | 12.00 | Unseated packers |  |  | ° at |  | m |  | AMC Biocide G |  |
| 12.00 | 13.00 | Dropped bar-reverse circulated through poor boy degas |  |  |  |  |
| 13.00 | 13.30 | Pumped pill-rigged down surface equipment |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
| 13.30 | 17.00 | Tripped out hole -Retrieved recorders and sample |  | Liner | 140 | mm |  | Liner | 140 | mm |
| 17.00 | 19.00 | Layed out tools |  | Pressure |  | kPa |  | Pressure |  | KPa |
| 19.00 | 21.00 | Made up 156mm Bit tripped in hole to 650m |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
| 21.00 | 21.30 | Filled pipe and circulated |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
| 21.30 | 23.30 | Tripped in hole from 650m to 1335m |  | SPM |  |  | SPM |  |
| 23.30 | 24.00 | Circulated mud in balance |  | GPM |  |  | GPM |  |
|  | DST | 81m of formation fluid in drill string ( Water ) |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 19 camp 4 Schlumberger stby |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 3 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  | Farley Riggs 2 |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | 466 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66