LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 42 | DFS: | 42 | DATE : | 27-11-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 2,500 | LAST DEPTH : | 2,500 | 24 HR PROGRESS: |  | PTD : | Total Depth |
| TOTAL FUEL : | 1,800 | FUEL USAGE : | 1,300 | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Freed obstruction in Float equip -Circ Casing- mud-mix Barite pill to pump down Casing then pull and lay out Casing from 1856m |
| Next 24 Hrs Op | Lay out all 4½ " Casing-locate failure in Float equipment –replace the faulty Float equipment then Run Casing again |
| Site Personnel: | Lou DeVattimo - Supervisor |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES @ 22.30 |
| --- | --- | --- | --- | --- |
| j Bit Number |  |  |  | Drilling |  |  | Density | 1.152 | S.G. |
| Size (mm) |  |  |  | Tripping | 18.50 |  | Viscosity | 35 | Sec |
| Make |  |  |  | Downtime ( Float ) |  |  | Water Loss | 34 | Cc |
| Type |  |  |  | Wireline logging |  |  | pH | 8.5 | Strip |
| IADC Code |  |  |  | Testing/tools |  |  | Filter Cake | 3 | 32 nd |
| Serial Number |  |  |  | Circulate Sample |  |  | PV / YP | 7/ 8 | Cp/lb/100’ |
| Nozzles (32) |  |  |  | Casing |  |  | Gels | 1 / 2 | S/m |
| Depth in (m) |  |  |  | Cementing |  |  | Sand | 0.20 | % Vol |
| Depth out (m) |  |  |  | Drill stem testing |  |  | Solids | 7.8 | % Vol |
| Total Metres |  |  |  | Circulate & Condition | 5.00 |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut | 0.50 |  | K+ | 7,875 | Mg/l |
| WOB (kg) |  |  |  | Rig up/ d own bop |  |  | Chlorides | 14,500 | Mg/l |
| RPM |  |  |  | Drill out Cmt |  |  | K+ | 10,500 |  |
| Condition |  |  |  | Reaming |  |  | KCL | 2.0 | % |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ |  |
| Jet Velocity |  |  |  | Test BOPs |  |  | Cum Cost $ | 92,290 |
| B.H.A.: |  |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  |  | ° at |  | m |  | Type | Amount |
| 0000 | 00.30 | Slipped block line |  |  | ° at |  | m |  | AMC Pac L |  |
| 00.30 | 03.30 | Laid out Drill collars |  |  | ° at |  | m |  | AMC Pac R |  |
| 03.30 | 07.00 | Changed out Rams to 4½" Rigged up to run Casing |  |  | ° at |  | m |  | Caustic |  |
| 07.00 | 07.30 | Held safety meeting with Weatherford operator |  |  | ° at |  | m |  | Xan Bore |  |
| 07.30 | 08.00 | Replaced faulty hydraulic hose |  |  | ° at |  | m |  | Bayrtes |  |
| 08.00 | 17.30 | Ran Casing to 2035m filled casing as required |  |  | ° at |  | m |  | Potassium Chloride |  |
| 17.30 | 20.30 | Made various attempts to circulate thru Casing no-go |  |  | ° at |  | m |  | AMC Biocide G |  |
| 20.30 | 22.30 | Pulled and laid out Casing 2035m-1856m |  |  |  |  |
| 22.30 | 24.00 | Attempted to break circulation using Halliburton no-go |  | PUMP 1 Duplex |  | PUMP 2 Triplex |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | KPa |
|  |  |  |  | A.V. DP |  | f/min |  | A.V. DP |  | Ft/min |
|  |  |  |  | A.V. DC |  | f/min |  | A.V. DC |  | Ft//mn |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | GPM |  |  | GPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton |  |  | Size | 7" | inch |
|  |  | Hunt 17camp 4 Schlumberger stby |  | Class Bulk |  |  | Weight | 26 | ppf |
|  |  | Lakes 3 |  | % |  |  |  | Grade | K-55 |  |
|  |  | Mud logger 2 |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 117 |  |
|  |  | RMN 1 |  | % |  |  |  | Length | RT-Brd Hd 5.0 | m |
| Days since | LTA | 468 |  | Av. Wt |  |  | Shoe | 1376m from RKB | m |

,66