LAKES OIL N.L

DAILY DRILLING REPORT

| WELL : | Wombat-4 | REPORT No. : | 6 | DFS: | 6 | DATE : | 22-10-09 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 747m | LAST DEPTH : | 557m | 24 HR PROGRESS: | 190m | PTD : |  |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ |  | CUM. COST : $ |  |
| 0600 OPS : | Drilling 216mm hole at 778m |
| Next 24 Hrs Op | Drill ahead to top of Latrobe formation , continue drilling to 7" casing depth |
| Site Personnel: | Hunt Energy 22 Camp 4 Lakes Oil 4 RMN 1 Baker Mud Loggers 2 |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 1 Re-run | 2 |  | Drilling | 21.0 |  | Density | 1.086 | S.G. |
| Size (mm) | 311 | 216 |  | Tripping | 1.5 |  | Viscosity | 42 | Sec |
| Make | Reed | Reed |  | Slip Cut |  |  | Water Loss |  | Cc |
| Type | EPH41 HKPR | RO1APDH |  | BHA |  |  | pH | 9.5 | Strip |
| IADC Code | 4-1-7 | 4-1-7 |  | F.I.T |  |  | Filter Cake | 1.0 | 32 nd |
| Serial Number | NR 2008 | NDO593 |  | Circulate Sample |  |  | PV / YP | 9 / 21 | Cp/lb/100’ |
| Nozzles (32) | 18-18-18 | 14-14-14 |  | Casing |  |  | Gels | 3 / 5 | S/m |
| Depth in (m) | 16 | 302 |  | Cementing |  |  | Sand | Tr | % Vol |
| Depth out (m) | 302 |  |  | Surveys | 1.0 |  | Solids | 3.9 | % Vol |
| Total Metres | 285 / 846 | 445 |  | Circulate & Condition | 0.5 |  | Oil |  | % Vol |
| Hours | 18.5 / 63.5 | 36 |  | Rig Service |  |  | K+ | 12,075 | Mg/l |
| WOB (kg) | 2000 | 4000 / 5000 |  | Rig up/down bop |  |  | Chlorides | 19,000 | Mg/l |
| RPM | 100 | 100 |  | Drill out Cmt |  |  | PHPA |  |  |
| Condition | 2-2-NO-A-E-1-1-CT | S.I.H |  | Breakdown kelly |  |  | KCL | 2.3 | % |
| Impact Force |  | 329 |  | Wait On Cement |  |  | Daily Cost $ | 3,258 |
| Jet Velocity |  | 223 |  | Test BOPs |  |  | Cum Cost $ | 17,209 |
| B.H.A.: # 2 | 216mmBit-NBS-NMDC-Stab- 2 x 6¼" DC-Stab-6 x 6¼" DC-Supra Drilling Jar- 3 x 6¼" DC-4 x HWDP- X/O Sub Length 162.44m |
| HOURLY OPERATIONS SUMMARY (0000 – 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | ¾º | ° at | 32 | m |  | Type | Amount |
| 00.00 | 00.30 | Ran survey at 555m |  | ½º | ° at | 96 | m |  | AMC Pac R | 3 |
| 00.30 | 18.00 | Drilled 216mm hole from 557m to 699m |  | 1º | ° at | 239 | m |  |  |  |
| 18.00 | 18.30 | Ran survey at 687m |  | 1½º | ° at | 295 | m |  | KCL | 46 |
| 18.30 | 22.00 | Drilled 216mm hole from 699m to 747m |  | 2 | ° at | 458 | m |  | Xan Bore | 3 |
| 22.00 | 22.30 | Circulated bottoms up ,pumped 5 bbl pill |  | 2 | ° at | 687 | m |  | Barite | 32 |
| 22.30 | 24.00 | Wiper tripped back to 574m |  |  | ° at |  | m |  |  |  |
|  |  |  |  |  | ° at |  | m |  |  |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  | Held BOP Drills |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure | 5,000 | KPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP | 40 | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC | 70 | m/min |
|  |  |  |  | SPM |  |  | SPM | 140 |
|  |  |  |  | LPM |  |  | LPM / GPM | 1230 / 325 |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks Halliburton | 377 |  | Size | 9⅝" | inch |
|  |  |  |  | Class Bulk |  |  | Weight | 36 | ppf |
|  |  |  |  | % |  |  |  | Grade | K-55 |  |
|  |  |  |  | % |  |  |  | Thread | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 25 |  |
|  |  |  |  | % |  |  |  | Length |  | m |
| Days since | LTA |  |  | Av. Wt | 15.6 |  | Shoe | 299.00 | m |

,66