PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 12 Date: 28-10-09

Depth: 1378m Progress: 12m Days from Spud: 12

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 9⅝" at 299m

0600 hrs Update: Finish POOH, Install 7" casing rams prior to running 7" casing.

Comments: POOH, Rig up Schlumberger for wireline logging, Run#1 HALS-BHC-PEX (1361-299m), GR to surface, RIH, trip gas 1.4 units, drill ahead with 8½" hole to 1378m, POOH for 7" (178mm) casing.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1366-1376 | Strzelecki Group - No Show | TG 0.1-5u C1 90% C2 4% C3 3% C4 2% C5 1% |
| 1376-1378 | Strzelecki Group - Gas Show The interval from 1376-1378m appears to be gas saturated, however the sandstone in this interval still appears to be slightly damaged by weathering being the top of the first sand package beneath the unconformity. The penetrated interval of 2 meters is insufficient for any reliable estimate to be placed on flow potential. | TG 21u C1 74% C2 8% C3 7% C4 7% C5 4% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1366-1376 | STRZELECKI GROUP Claystone (90%) with minor laminated Sandstone (10%). CLAYSTONE: off white to medium green grey, light to medium grey to medium brown grey, moderately silty, trace very fine off white altered feldspar grains, trace brown to black carbonacous specks, trace micromica, soft to firm, very dispersive, slightly subfissile. SANDSTONE: light grey, silty to fine, dominantly fine, subangular to subrounded, moderately sorted, weak silica cement, abundant off white argillaceous and silt matrix - matrix supported, abundant altered feldspar grains, common red brown grey and green lithics, trace quartz grains, trace coarse brown mica flakes, trace very fine black carbonaceous detritus, trace pyrite, friable, no visual porosity, no oil fluorescence. |
| 1376-1378 | STRZELECKI GROUP Sandstone (100%). SANDSTONE: light grey, very fine to medium, dominantly fine to medium, subangular to subrounded, moderately sorted, weak silica cement, abundant off white argillaceous and silt matrix, abundant altered feldspar grains, common red brown grey and green lithics, trace quartz grains, trace coarse brown mica flakes, trace very fine black carbonaceous detritus, trace pyrite, friable, poor visual porosity, no oil fluorescence. |