PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 18 Date: 3-11-09

Depth: 1551m Progress: 73m Days from Spud: 18

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 1637m. The interval from 1551-1600m appears to be gas saturated. From visual cuttings examination most of this unit has very poor to poor visual porosity sands interbedded with Claystone (70%), however within this interval better quality sands with poor to fair visual porosity are located at 1560-1562m with TG = 122u, 1580-1581m with TG = 60u, 1584-1586m with TG = 155u (C1 95%, C2 3.2%, C3 1.3%, C4 0.5%, C5 0.2%). An assessment based on drill and gas analysis data would suggest further evaluation on these intervals may warranted to positively ascertain flow potential. Possible gas/water contact present at approximately 1600m.

Comments: Continue DST#1, (Gas analysis C1 91.2%, C2 4.7%, C3 2.4%, C4 1.2%, C5 0.5% - analysis indicates the gas comes from the deeper sands in the tested interval), Finish FSI (540 mins), unseat packers, reverse circulate contents of string - recovered 140m of gas cut rathole mud (no field identifiable water oil or condensate in the rathole mud), POOH with test tools, RIH with drilling assembly, drill ahead with 6¼" hole to 1551m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 1478-1551 | Strzelecki Formation - Gas Show The interval from 1478 to 1551m appears to be gas saturated. From visual cuttings examination most of this unit has nil to very poor visual porosity with no better quality sandstones observed in cuttings samples. | TG 25-55u C1 92.5% C2 5% C3 2% C4 1% C5 0.5% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 1478-1551 | STRZLECKI FORMATION Sandstone (30%) inerbedded with Claystone (70%). SANDSTONE: light green grey, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, moderate silica cement, weak calcareous cement in part, abundant off white argillaceous matrix - matrix supported, abundant altered feldspar grains and red brown grey and green lithics, common quartz grains, trace coarse brown mica flakes, trace very fine black carbonaceous detritus, friable, nil to very poor visual porosity, no oil fluorescence. CLAYSTONE: off white to medium brown grey to medium grey to occasionally medium green grey, moderately to very silty grading to argillaceous siltstone in part, very finely arenaceous in part, trace very fine off white altered feldspar grains, trace to common brown to black carbonaceous specks, trace micromica, firm, very dispersive, slightly subfissile. |