PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 22 Date: 7-11-09

Depth: 2278m Progress: 249m Days from Spud: 22

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: Drill ahead with 6¼" hole at 2315m. Current lithology Strzelecki Formation, Sandstone (80%) interbedded with Claystone (20%), background gas 10-15 units, no shows.

Comments: Drill ahead with 6¼" hole to 2149m, survey at 2237m = 18½° at N340E, drill ahead with 6¼" hole to 2278m.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
| 2144-2199 | Strzelecki Formation - No Show. The coal detritus in the sandstone and claystone has no natural fluorescence but gives a moderately bight slow streaming to crush milky white cut fluorescence. The minor gas peaks within this interval are associated with increased coal detritus in the cuttings samples. | TG 10-55u C1 93.7% C2 3.7% C3 1.6% C4 0.7% C5 0.3% |
| 2199-2200 | Strzelecki Formation - Gas Show. A gas peak of 100 units total gas was observed at 2200m, which from cutting samples appears to be associated with an increase in fracture infill material. No oil fluorescence was observed. | TG 100u C1 95.3% C2 3.7% C3 1.0% C4 trace C5 trace |
| 2200-2223 | Strzelecki Formation - No Show. | TG 10-45u C1 94.1% C2 3.6% C3 1.8% C4 0.4% C5 0.1% |
| 2223-2224 | Strzelecki Formation - Gas Show. A gas peak of 81 units total gas was observed at 2224m, which from cutting samples appears to be associated with an increase in fracture infill material, no oil fluorescence was observed. | TG 81u C1 95.8% C2 2.8% C3 1.1% C4 0.2% C5 0.1% |
| 2224-2278 | Strzelecki Formation - No Show. | TG 10-50u C1 94.1% C2 3.6% C3 1.9% C4 0.2% C5 0.2% |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | 1323 | 39 Low |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
| 2144-2278 | STRZLECKI FORMATION Sandstone (80%) interbedded with Claystone (20%) and minor detrital Coal (trace). SANDSTONE: off white to light green grey, light pinkish grey, very fine to occasionally medium, dominantly fine, subangular to subrounded, moderately sorted, strong silica cement, strong calcareous cement in part, abundant off white and trace pink argillaceous matrix, abundant white and pink feldspar grains, common green red brown grey and black lithics, common quartz grains, trace green brown mica flakes, common to abundant black coaly detritus, common calcite and red mineral veining, hard, no visual intergranular porosity, no oil fluorescence. CLAYSTONE: medium grey, occasionally medium green grey to medium brown grey, moderately to very silty, very finely arenaceous in part, trace to common very fine off white altered feldspar grains, common brown to black carbonaceous specks and coaly detritus, common micromica, trace to common calcite and red mineral infilled fractures, common slickensides, hard, very dispersive, subfissile. COAL: black, earthy to vitreous, platy fracture, slightly argillaceous, hard, brittle. The coal has no fluorescence but gives a moderately bight slow streaming to crush milky white cut fluorescence. |