PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 28 Date: 13-11-09

Depth: 2500m Progress: 0m Days from Spud: 28

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 7" at 1376m

0600 hrs Update: RIH for cleanout trip, circulate whilst increasing mud weight to 10.8ppg, prior to POOH to continue wireline logging.

Comments: POOH, Rig up Schlumberger for repeat of Run#2 Sonic-Scanner-FMI, unable to pass bridge at 1610m, attempt logging up, tool sticking, POOH with Sonic-Scanner-FMI, RIH with Sonic-Scanner, unable to pass bridge at 1612m, check hole caliper - hole oval in claystones (indicative of tectonic stress), POOH with Sonic-Scanner, rig down Schlumberger, RIH for cleanout trip.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 | 627 | -600 | 2 Low |
| LaTrobe Group | 786 | 820 | -793 | 34 Low |
| Strzelecki Formation | 1311 | 1350 | -1323 | 39 Low |
| Total Depth | 2004 | 2500 | -2473 | 496 Low |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |