PETRO TECH PTY. LTD. A.C.N. (009 116 429) Wombat No.4 PRL 2

DAILY GEOLOGICAL REPORT No. 3 Date: 19-10-09

Depth: 302m Progress: 0m Days from Spud: 3

Rig: Hunt Rig No.2 GL(AHD): 23.0m Drilling Rep: Lou DeVattimo RT: (datum) 26.65m Geologist: David Horner Last Casing: 244mm at 299m

0600 hrs Update: Continue to nipple up BOP's.

Comments: POOH, rig up and run 244mm (9.625") casing to 299m, cement casing, nipple up BOP's.

| Interval (mRT) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled. |  |

| Formation Tops: | Prognosed (mRT) | Actual* (mRT) | Actual* (mSS) | Difference* (High/Low) |
| --- | --- | --- | --- | --- |
| Quaternary Haunted Hills Gravels Jemmy's Point Formation Tambo River Formation | 3.65 14 33 126 | 3.65 14 35 125 | +23.65 +12.65 -8 -98 | 0 0 2 Low 1 High |
| Gippsland Limestone | 137 | 145 | -110 | 8 Low |
| Lakes Entrance Formation | 625 |  |  |  |
| LaTrobe Group | 786 |  |  |  |
| Strzelecki Formation | 1311 |  |  |  |
| Total Depth | 2004 |  |  |  |

*Provisional, based on mudlog

| Lithological and Fluorescence Description |
| --- |
| Interval (m) | Description |
|  | No new formation drilled. |