LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 17	Date: 09 Oct 05

Depth: 282.1m		Progress: 15.1m		Days from Spud: 33

Rig:			Drilltec		GL(ASL):		31.55m

Drilling Rep:	Tim O’Brien	RT (AGL):		0.80m

Geologist:		Ingrid Campbell	Last Casing:         115mm at 232m

Comments: Run electric logs Suite 1Run 1 (GR-CCL-PRES-TEMP)

Mix and pump cement plug No. 1.

| Interval (mGL) | Hydrocarbon Show Summary | Gas |
| --- | --- | --- |
|  | No new formation drilled |  |

| Formation Tops: | Prognosed (mGL) | Actual (mGL) | Actual (mSS) | Difference (High/Low) |
| --- | --- | --- | --- | --- |
| Pleistocene dune deposit | Absent | Surface | +31.55 | - |
| Haunted Hills Gravel | Surface | 34.45 | -2.9 | 34.45 Low |
| Jemmy’s Point Formation | 15 | 42 | -10.45 | 27 Low |
| Gippsland Limestone | 50 | 107 | -75.45 | 57 Low |
| Lakes Entrance Formation Seacombe Marl Member | 190 | 234 | -202.45 | 44 Low |
| Lakes Entrance Formation Giffard Sandstone Member | Absent | 262 | -230.45 | - |
| Colquhuon Gravels | 360 | 272.2 | -241.65 | 87.8 High |
| Palaeozoic Basement | 400 | 281.9 | -250.35 | 118.1 High |
| Total Depth | 600 | 282.1 | -250.55 | 317.9 High |

LAKES OIL N.L.

A.C.N. (004 247 214)

Patrobus No.1		PEP 155 (east)

DAILY GEOLOGICAL REPORT No. 17

Lithological and Fluorescence Description

| Interval (m) | Description |
| --- | --- |
|  | No new formation drilled. |