Report for : Dan Daniels / Mark Calicutt  / Andy Choy

Compiled by : Gareth Munro / Dan Dennis

| WELL | WKF W12A |
| --- | --- |
| DATE | 23-11-2009 |
| REPORT # | 6 |
| MIDNIGHT ACTIVITY | Drill ahead 9-7/8” production hole. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2259.00 mMDRT |  | MINIMUM | 21.93 | 1933.0 |
| TVD | 2241.94 mTVDRT |  | MAXIMUM | 124.3 | 1883.0 |
| PROGRESS LAST 24 hrs | 676.0 m |  | AVERAGE | 64.38 | - |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 1488.0 | 1474.0 | -1432.3 | 2.3L | 1483.5 | 1471.7 |
| Top of Lakes Entrance Formation | 1885.0 | 1867.4 | -1825.7 | -5.3H | 1888.7 | 1872.7 |
| Top of Latrobe Group | 2283.5 | 2265.7 | -2224.0 | 4.0L | 2278.0 | 2261.7 |
| Top Coarse Clastics (SBP2) | 2304.0 | 2286.2 | -2244.5 | 0.5L | 2302.0 | 2285.7 |
| Top Up. M diversus | 2304.0 | 2286.2 | -2244.5 | 0.5L | 2302.0 | 2285.7 |
| Top M12 (PSB3) | 2312.0 | 2294.2 | -2252.5 | 2.5L | 2308.0 | 2291.7 |
| Top M13 (PSB7) | 2318.8 | 2301.0 | -2259.3 | -0.7H | 2318.0 | 2301.7 |
| Top M14 (SB13) |  |  |  |  | 2348.0 | 2331.7 |
| Top M15 |  |  |  |  | 2368.0 | 2351.7 |
| OOWC |  |  |  |  | 2372.0 | 2353.7 |
| Total Depth |  |  |  |  | 2432.98 | 2415.70 |

| Current Formation | Lakes Entrance |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 1741.0 | 46.0 | 0.920 | 0.003 | 0.001 | 0.001 | 0.000 | - |
| MAX (GFF) | 1879.0 | 57.0 | 1.607 | 0.000 | 0.000 | 0.000 | 0.000 | - |
| BG (Reserval) | 1583.0 – 2259.0 | 15.3 | 0.293 | 0.002 | 0.001 | 0.001 | 0.000 | 0 |
| BG (GFF) | 1583.0 – 2259.0 | 9.0 | 0.186 | 0.000 | 0.000 | 0.001 | 0.000 | 0 |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR516M-B6 |  |
| JETS (/32 inch) | 7 x 18 |  |
| DEPTH IN (m) | 637.0 |  |
| DEPTH OUT (m) | - |  |
| METRES ON RUN (m) | 1622.0 |  |
| HRS ON BTM 24hrs/total | 10.5 / 27.3 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 89 – 161 |  |
| Pump Hrs 24 hrs / total | 21.1 / 50.6 |  |
| Krevs 24 hrs / total | 83.6 / 218.6 |  |

| 24 HOUR SUMMARY | Continue to control drill from 1583.0 mMDRT to 1671.0 mMDRT. Drill ahead 9 7/8” production hole from 1671.0 mMDRT to 1758.0 mMDRT. Circulate and work pipe until bottoms up at 1788.0 mMDRT adding calcium carbonate 500 m prior to entering Top of Latrobe Group. Continue to drill 9-7/8” hole as per Annadrill’s instruction from 1788.0 m to 2107.0 mMDRT. Work pipe whilst clearing blockage in mud dryer. |
| --- | --- |
| 24-11-2009 5 AM UPDATE | Continue to drill 9-7/8” hole as per Annadrill’s instruction from 2107.0 m to 2227.0 mMDRT. Commence control drilling at 50 m/hr. 2395.0 mMDRT (2377.03 mTVDRT) |