DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS October 6, 2006

| RIG 453 | 141 | 363 |
| --- | --- | --- |
| CAMERON | 1616 | 1616 |
| HALLIBURTON | 3404 | 3404 |
| SCHLUMBERGER | 2345 | 2345 |
| ISDL | 141 | 647 |
| ISS | 130 | 2346 |

Well: WKF_W23

Rig/Contractor: 	Rig 453	Report Date: October 6, 2006

Supervisor:	Campbell, Glenn R.

Davis, Brian

| AFE Number: | 40000460 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 3.0 | AFE Cost/Days: | $1,278,800 |
| Daily Cost: | $ 187,968 |  |  |
| Total Cost: | $ 554,528 | Planned MD/TVD: |  |
| Casing Size: |  | Actual MD/TVD: |  |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W23 |
| --- | --- |
| Management Summary: | Set DGLV & Test tubing to 800 psi. R/dn slickline & Totco BOP. Set BPV in tbg hanger. N/dn Xmas tree. Inspect tbg hanger threads. N/up HP riser & BOP. BCFT. Recover BPV. M/up landing joints & shell test BOP to 300/3000 psi. Attempt to unjay from tbg hanger without success. Review plans with Ops Supt. WOW. Unable to operate crane due to weather. Rig down slickline and clear pipe deck. |
| Current: | Rigging down Slickline |
| Planned: | R/up Schlumberger, Cut & L/out Tubing |