Report for : Greg Doty / Sam Falkner / Mark Calicutt

Compiled by : Alex Djukanovic / Mark Smith

| WELL | WKF W26A |
| --- | --- |
| DATE | 20-12-2009 |
| REPORT # | 5 |
| MIDNIGHT ACTIVITY | Drilling ahead. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 3680.12 mMDRT |  | MINIMUM | 18.5 | 3647 |
| TVD | 2298.16 mMDRT |  | MAXIMUM | 148.1 | 2775 |
| PROGRESS LAST 24 hrs | 934 m |  | AVERAGE | 38.9 |  |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2248.0 | 1481.5 | -1439.8 | 14.8 L | 2223.1 | 1466.7 |
| Top of Lakes Entrance Formation (Mid Miocene Marker) | 2940.0 | 1872.5 | -1830.8 | 4.2 H | 2942.0 | 1876.7 |
| Top of Latrobe Group | 3619.0 | 2262.2 | -2220.5 | 0.5 L | 3616.7 | 2261.7 |
| Top Coarse Clastics (SBP3) | - | - | - | - | 3651.8 | 2281.7 |
| Top M13L (PSB4) | - | - | - | - | 3665.8 | 2289.7 |
| Top M14 (SB13) | 3668.0 | 2290.2 | -2248.5 | 1.5 H | 3669.3 | 2291.7 |
| Top M15 | 3692.0 | 2303.7 | -2262.0 | 0 | 3690.4 | 2303.7 |
| OOWC | - | - | - | - | 3771.1 | 2349.7 |
| Total Depth | - | - | - | - | 3831.06 | 2383.90 |

| Current Formation | Latrobe Gp. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 3673.0 | 57.0 | 0.56 | 0.10 | 0.08 | 0.05 | 0.01 | - |
| MAX (GFF) | 3673.0 | 129.0 | 1.94 | 0.19 | 0.13 | 0.06 | 0.01 | - |
| BG (Reserval) | 2746 – 3680 | 11.6 | 0.21 | - | - | - | - | - |
| BG (GFF) | 2746 – 3680 | 36.2 | 0.68 | - | - | 0.01 | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 2 | 1 |
| SIZE (in) | 9.875 | 9.875 |
| MANUFACTURER/TYPE | REED Hycalog / RSX616S-A1 | REED Hycalog / RSX616M-A13 |
| JETS (/32 inch) | 8 x 16 | 8 x 16 |
| DEPTH IN (m) | 1762 | 733 |
| DEPTH OUT (m) | - | 1762 |
| METRES ON RUN (m) | 1918 | 1029 |
| HRS ON BTM 24 hrs/total | 12.3 / 23.7 | 13.7 |
| BIT CONDITION | - | 1-1-WT-A-X-IN-SD-DTF |
| RPM RANGE 24hrs | 106 – 183 | 80 – 159 |
| Pump Hrs 24 hrs / total | 20.5 / 39.1 | 29.1 |
| Krevs 24 hrs / total | 110 / 214 | 110.0 |

| 24 HOUR SUMMARY | Continue to drill with steerable assembly as per Anadrill instructions from 2746.0 mMDRT to 3125.0 mMDRT. Back ream and rack stands back after circulating 3 times bottoms up equivalent each stand from 3125.0 mMDRT to 3038.0 mMDRT prior to treating the mud system with calcium carbonate before drilling into sands. Run back in hole to resume drilling, washing the last stand to bottom to 3125.0 mMDRT. Continue to drill ahead adding calcium carbonate to active from 3125.0 mMDRT to 3484.0 mMDRT. Drill ahead at a controlled drill rate entering the Latrobe formation as per Anadrill instructions from 3494.0 mMDRT to 3680.0 mMDRT. |
| --- | --- |
| 21-12-2009 5 AM UPDATE | Continue to drill with steerable assembly as per Anadrill instructions from 3680.0 mMDRT to 3825 mMDRT. Current operation at 0500 hours; drilling ahead. 3825.00 mMDRT (2381.70 mTVDRT) |