Report for : Dan Daniels / Mark Calicutt  / Andy Choy

Compiled by : Mark Smith

| WELL | WKF W5A |
| --- | --- |
| DATE | 10-11-2009 |
| REPORT # | 4 |
| MIDNIGHT ACTIVITY | Circulating hole clean. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2658.0 mMDRT |  | MINIMUM | 40.2 | 2130.0 |
| TVD | 1987.3 mTVDRT |  | MAXIMUM | 141.6 | 2515.0 |
| PROGRESS LAST 24 hrs | 1027.0 m |  | AVERAGE | 93.4 | 1631.0 – 2658.0 |

| PRELIMINARY FIELD PICKS | ACTUAL TOP (mMDRT) | ACTUAL TOP (mTVDRT) | ACTUAL TOP (mTVDSS) RT to MSL (41.7m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of High Velocity Channel | 2158.0 | 1643.0 | -1601.3 | 1.3 L | 2153.9 | 1641.7 |
| Top of Lakes Entrance Formation | 2513.0 | 1886.9 | -1845.2 | 8.2 L | 2500.0 | 1878.7 |
| Top of Latrobe Group |  |  |  |  | 3147.3 | 2281.7 |
| Top P11 (FSP1) |  |  |  |  | 3203.2 | 2299.7 |
| Top Coarse Clastics (SBP3) / M12 |  |  |  |  | 3215.2 | 2305.7 |
| Top M13 (PSB7) |  |  |  |  | 3229.2 | 2312.7 |
| Top M14 (SB13) |  |  |  |  | 3297.2 | 2346.7 |
| Top M15 |  |  |  |  | 3337.2 | 2366.7 |
| OOWC |  |  |  |  | 3315.3 | 2355.7 |
| Total Depth |  |  |  |  | 3375.3 | 2385.7 |

| Current Formation | Lakes Entrance: Calcareous Claystone |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | C4 % | C5 % | H2S ppm |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (Reserval) | 2007.0 | 47.8 | 0.818 | 0.002 | - | - | - | - |
| MAX (GFF) | - | - | - | - | - | - | - | - |
| BG (Reserval) | 1631.0-2658.0 | 21 | 0.404 | 0.002 | - | - | - | - |
| BG (GFF) | - | - | - | - | - | - | - | - |
| TRIP GAS (Reserval) | - | - | - | - | - | - | - | - |
| TRIP GAS (GFF) | - | - | - | - | - | - | - | - |
| CONNECTION GAS | - | - | - | - | - | - | - | - |

| BIT DATA | PRESENT BIT | PREVIOUS BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 9-7/8 |  |
| MANUFACTURER/TYPE | Reed Hycalog RSR616S |  |
| JETS (/32 inch) | 8 x 16 |  |
| DEPTH IN (m) | 679.0 |  |
| DEPTH OUT (m) | - |  |
| METRES ON RUN (m) | 1979.0 |  |
| HRS ON BTM 24hrs/total | 11.0 / 27.8 |  |
| BIT CONDITION | - |  |
| RPM RANGE 24hrs | 134-163 |  |
| Pump Hrs 24 hrs / total | 19.9 / 61.1 |  |
| Krevs 24 hrs / total | 95.9 / 231.4 |  |

| 24 HOUR SUMMARY | Drill and survey 9-7/8” hole from 1631.0 mMDRT to 2103.0 mMDRT. Circulate while changing out mud pump #2 standpipe seal. Drill and survey 9-7/8” hole from 2103.0 mMDRT to 2658.0 mMDRT. Circulate hole while back reaming one stand per bottoms up to 2570.0 mMDRT. |
| --- | --- |
| 11-11-2009 5 AM UPDATE | Continue to back ream to 2570.0 mMDRT. Run in hole and wash last stand to bottom. Control drill at 50.0 m/hr while building mud volume and adding Baracarb to system. Drill and survey 9-7/8” hole from 2658.0 mMDRT to 2774.0 mMDRT. Monitor on trip while repairing mud pump stand pipe seal. 2774.0 mMDRT (2061.8 mTVDRT) |