LAKES OIL Ltd

DAILY DRILLING REPORT

| WELL : | WOMBAT-1 | REPORT No. : | 13 | DFS: | 13 | DATE : | 17 Dec 2003 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2400 DEPTH : | 1385m | LAST DEPTH : | 1385m | 24 HR PROGRESS : | 0m | PTD : | 1800m |
| TOTAL FUEL : |  | FUEL USAGE : |  | DAYCOST : $ | 38,597 | CUM. COST : $ | 774,626 |
| 0600 OPS : | Circulate casing prior to cementing. |
| Next 24 hr OPS: | Cement 244mm casing. Test BOP’s. |
| Site Personnel: | Peter Dwyer – Supervisor. |

| BIT INFORMATION |  | OPS BREAKDOWN |  | MUD PROPERTIES |
| --- | --- | --- | --- | --- |
| Bit Number | 2RR |  |  | Drilling |  |  | Density | 1.2112 | S.G. |
| Size (mm) | 311 |  |  | Tripping | 4.0 |  | Viscosity | 50 | sec |
| Make | Security |  |  | Surveys | 0.5 |  | Water Loss | 5.5 | cc |
| Type | XS1 |  |  | Reaming/work tight hole | 3.5 |  | pH | 9.0 | strip |
| IADC Code | 1.1.6 |  |  | Testing |  |  | Filter Cake | 1 | 32 nd |
| Serial Number | 10406660 |  |  | Circulate Sample |  |  | PV / YP | 15/29 | cp/lb/100’ |
| Nozzles (32) | 1x16, 3x18 |  |  | Casing | 12.5 |  | Gels | 3/7 | s/m |
| Depth in (m) | 1385 |  |  | Cementing |  |  | Sand | 1.25 | % Vol |
| Depth out (m) | Wiper trip |  |  | Wireline |  |  | Solids | 8.2 | % Vol |
| Total Metres |  |  |  | Circulate & Condition | 3.0 |  | Oil |  | % Vol |
| Hours |  |  |  | Rig Service/slip & cut | 0.5 |  | K+ | 20,265 | mg/l |
| WOB (kg) |  |  |  | Test BOP's |  |  | Chlorides | 22,000 | mg/l |
| RPM |  |  |  | Repairs |  |  | PHPA | 1.7 |  |
| Condition |  |  |  | Drill Out |  |  | ALC - 50 |  |  |
| Impact Force |  |  |  | Wait On Cement |  |  | Daily Cost $ | 592 |
| Jet Velocity |  |  |  | Nipple Up BOPs |  |  | Cum Cost $ | 61,237 |
| B.H.A.: | Bit, bit sub, 2x8” DC’s, stabilizer, XO, 18x6-1/2” DC’s, jars, 3x6-1/2” DC’s, 6x4-1/2” HWDP |
| HOURLY OPERATIONS SUMMARY (0000 - 2400) |  | SURVEYS |  | CHEMICALS USED |
| From | To | Operation |  | 0.75 | ° at | 1385 | m |  | Type | Amount |
| 0000 | 0330 | RIH. Ream bridges from 1283m to 1385m. |  |  | ° at |  | m |  | AMC PAC-R |  |
| 0330 | 0630 | Circulate and condition hole. Raise MW to 10.1ppg. |  |  | ° at |  | m |  | Sodium Sulphite |  |
| 0630 | 0700 | Drop survey and pump barite pill. |  |  | ° at |  | m |  | Barite | 74 |
| 0700 | 1100 | POH. Hole condition good. |  |  | ° at |  | m |  | Drillzan |  |
| 1100 | 1130 | Slip and cut 24’ drill line. |  |  | ° at |  | m |  | KCl Tech |  |
| 1130 | 1300 | Rig up to run 244mm casing. |  |  | ° at |  | m |  | PHPA |  |
| 1300 | 2400 | Run 88 jts 244mm casing to 988m. |  |  | ° at |  | m |  | Caustic Soda |  |
|  |  |  |  | PUMP 1 |  | PUMP 2 |
|  |  |  |  | Liner | 140 | mm |  | Liner | 140 | mm |
|  |  |  |  | Pressure |  | kPa |  | Pressure |  | kPa |
|  |  |  |  | A.V. DP |  | m/min |  | A.V. DP |  | m/min |
|  |  |  |  | A.V. DC |  | m/min |  | A.V. DC |  | m/min |
|  |  |  |  | SPM |  |  | SPM |  |
|  |  |  |  | LPM |  |  | LPM |  |
|  |  |  |  | CEMENT DATA |  | LAST CASING |
|  |  |  |  | Sacks | 800 |  | Size | 340 | mm |
|  |  |  |  | Class | A |  | Weight | 81 | kg/m |
|  |  |  |  | % |  |  |  | Grade | K55 |  |
|  |  |  |  | % |  |  |  | Connection | BTC |  |
|  |  |  |  | % |  |  |  | Joints | 26 |  |
|  |  |  |  | % |  |  |  | Length | 303.5 | m |
|  |  |  |  | Av. Wt | 12.5/15.8ppg |  | Shoe | 302.0 | m |

,66