# OPERATIONS

## Onboard Personnel

### Marine Crew

| Master: | Richard Dixon |
| --- | --- |
|  | Jonathon Jones |
| 1st Mate: | Victor Pinto |
|  | Glen Laurence |
| 2nd Mate: | Darren Webster |
|  | Tony Egito |
| Chief Engineer: | Robert Moore |
|  | John Maclean |
| 1st Engineer | C. Gonsalves |
|  | Robert Egan |
| 2nd Engineer | Russell Vik |
|  | Eamon Heggarty |

### Seismic Crew

| Party Chief | Rob Secker |
| --- | --- |
|  | Dave Coughlan |
|  | Paddy MacCurtain |
| HSE Advisor | Ian Robertson |
|  | Lyall Cowin |
| Co-ordinator | Wayne Buffham |
|  | Eric Gundersen |
|  | Russ Blohm |
| Assistant Co-ordinator: | Iain Smith |
|  | Alan Lewis |
|  | Rob Coe |
|  | Brent Spooner |

| Senior Observer: | Les Hayden |
| --- | --- |
|  | Rolando Jaberina |
|  | Andy Gibson |
|  | Gary Birkett |
| Observer | Adam Powell |
|  | Brad Feist |
|  | Justin Hall |
|  | Rob Coe |
|  | Clive Dugdale |
|  | Adam Norris |

| Technician: | Nick Skingle |
| --- | --- |
|  | Kevin Jones |
|  | Steve Parker |
|  | Julian Ramsey |
|  | Andy Craven |
|  | Larry Dusolt |
|  | Nolan Vaness |
| Cable Repair | Gairn McClelland |
|  | Nat Roach |

| Chief Gun Mechanic: | Andy Statham |
| --- | --- |
|  | Ted Currey |
| Gun Mechanic: | Ronnie Morales |
|  | Steve French |
|  | Greg Back |
|  | Marcus Egington |
|  | Jason Phillips |

| Senior Navigator: | Mike Ray |
| --- | --- |
|  | Andy Young |
| Navigator: | Richard Stirrup |
|  | Fred Aiken |
|  | Jason Liddell |
|  | Gary Nicholson |
|  | Kevin Cane |
|  | Chris Gibbons |
|  | Colin Sheppard |
|  | Karl Prinz |
|  | John Cole |
|  | Pete Huxford |

| Field QA: | Rhod Morrison |
| --- | --- |
|  | Mark Trickett |
|  | Martin Skirving |
|  | David Millard |

| Navigation QC & Processing: | Gary Nicholson |
| --- | --- |
|  | Luke Cannon |
|  | Peter Hayward |
|  | Mike Vink |
|  | Nick Martin |

| Seismic QC & Processing: | Geoff Garratt |
| --- | --- |
|  | Virgilio Carreon |
|  | Ocal Necmioglu |
|  | Mike Grimes |
|  | Giorgio Liberati |
|  | Abd El Aleem El Essawy |

## Production Figures

Start of Job	5th December 1999

End job 			5th April 2000

### Time Breakdown All

Figure 2-1 Time Breakdown

| Survey Total | 2874.83 | 100.000% |
| --- | --- | --- |
| Operational | 1019.83 | 35.500% |
| Standby | 1455.55 | 50.600% |
| Downtime | 395.20 | 13.700% |
| Maintenance | 4.25 | 0.001% |

### Operational Time

Figure 2-2 Operational Time Breakdown

| Operational Time | 1019.83 | 100.0% |
| --- | --- | --- |
| Shooting Prime | 470.05 | 46.1% |
| Line Change After Prime | 235.68 | 23.1% |
| Line Change After Infill | 107.83 | 10.6% |
| Shooting Infill | 192.63 | 18.9% |
| Resupply at Sea | 3.80 | 0.4% |
| Transit to/from Survey Area | 9.83 | 1.0% |

### Standby Time

Figure 2-3 Standby Time Breakdown

| Standby Time | 1455.55 | 100.0% |
| --- | --- | --- |
| Weather | 901.08 | 61.9% |
| Transit to/from Survey Area | 266.37 | 18.3% |
| Resupply - Port Call | 127.52 | 8.8% |
| Streamer - Deployment | 57.35 | 3.9% |
| Streamer - Recovery | 22.08 | 1.5% |
| Avoidance (Fishing Shipping Debris) | 22.07 | 1.5% |
| Damage (Fishing Shipping Debris) | 14.80 | 1.0% |
| In Port or at Anchor | 11.83 | 0.8% |
| Resupply at Sea | 9.50 | 0.7% |
| Source - Deployment | 5.80 | 0.4% |
| Source - Recovery | 5.18 | 0.4% |
| Streamer - Reconfiguration | 4.72 | 0.3% |
| Currents / Tides | 3.42 | 0.2% |
| Source - Reconfiguration | 2.83 | 0.2% |
| Deploying Vanes | 1.00 | 0.1% |

### Downtime

Figure 2-4 DownTime Breakdown

| DownTime | 371.53 | 100.0% |
| --- | --- | --- |
| Vane Tow Wire Failure | 132.73 | 35.7% |
| Vessel - Propulsion | 35.42 | 9.5% |
| Streamer - Bad Groups | 27.83 | 7.5% |
| Airgun - Mechanical | 24.48 | 6.6% |
| Source - Deployment | 22.63 | 6.1% |
| Vane Harness | 20.68 | 5.6% |
| Streamer - Mechanical Damage | 18.20 | 4.9% |
| Streamer - Optics | 14.75 | 4.0% |
| Bird/Acoustic Comms | 13.50 | 3.6% |
| Recording System - CRS | 10.00 | 2.7% |
| Streamer - Lead-in | 9.75 | 2.6% |
| Streamer - Deployment | 8.25 | 2.2% |
| Rec. System - Semi-Monthly Acceptance | 6.67 | 1.8% |
| Robotic Tape Library | 6.58 | 1.8% |
| Streamer - Balancing | 5.48 | 1.5% |
| Vessel - Electricity | 5.32 | 1.4% |
| Airgun - Timing Coil | 4.75 | 1.3% |
| Nav - Tailbuoy - rGPS | 4.50 | 1.2% |
| Rec. System - MSX Chassis | 4.45 | 1.2% |
| Streamer - Cable Spread Adjustment | 3.88 | 1.0% |
| Nav - Headbouy - rGPS | 3.73 | 1.0% |
| Rec. System - Tape drive | 3.47 | 0.9% |
| Operator Error | 2.53 | 0.7% |
| Source - Electrical Jumper | 1.63 | 0.4% |
| Nav - Streamer Compass | 1.15 | 0.3% |
| Source - Recovery | 1.22 | 0.3% |
| Airgun - Hose Fitting | 0.88 | 0.2% |
| Streamer - Streamer Module | 0.50 | 0.1% |
| Streamer - Head Stretch | 0.17 | 0.0% |

### Maintenance

Figure 2-5 Maintenance Time Breakdown

| Maintenance | 4.25 | 100.0% |
| --- | --- | --- |
| Deploying Vanes | 2.68 | 63.1% |
| Recovering Vanes | 1.57 | 36.9% |

## Operational Comments and Problems

### Weather

Throughout the survey, the weather conditions were marginal.  There were extensive periods of weather down time, and many lines were rejected after analysis of the seismic data identified unacceptable levels of swell noise.

Figure 2-6 Weather Summary

### Streamer Configuration Changes

The adverse weather conditions found on the prospect also forced a reduction in the number of cable deployed from eight to six.  This reduction made it possible to retrieve individual cables for cable maintenance while leaving the remainder of the cables deployed. This was important, as there were very few weather windows for the small boat operations normally used to effect repairs.  The number of deployed cables was reduced from eight to six following sequence 008.

### Recording System Parameter Changes

At the start of the survey, data was being acquired using a 5 second record length.  This was very close to the maximum record length achievable within a 12.5 metre shotpoint interval.  It was hoped that using the CRS multi-shot option would allow a shortened cycle time, but this proved technically difficult to implement.  After sequence 003 the record length was reduced to 4.5 seconds in order to allow an increase in vessel speed, which improved cable depth control in the rough conditions.

### Equipment Failures

Generally, with the exception of the comments below, the equipment performed to a high standard throughout the survey.

- The rough seas experienced throughout the survey put the towed equipment under severe strain.  This caused the wire to the port vane to part during particularly rough weather on two separate occasions.  In order to prevent further occurrence of this fault both vane wires were replaced with heavier duty wire.

- The main tow from the vanes to the streamers became unspliced, again due to heavy inclement weather, again on two separate occasions.

- The tailbuoys also had a higher than average failure rate during this survey due to damage caused by the high sea states.

- During the mobilisation and early stages of acquisition, the Continuous Recording System would not perform multishot acquisition satisfactorily.  Single shot acquisition was enabled instead.

- Data telemetry errors were seen on a number of occasions.  Cable 1 gave errors during the early 8 cable sequences.  This was probably due to an in-water collision with debris, as the depth of the cable head fluctuated wildly just before the cable failed.  Cables 4 and 6 also failed during the survey.  The cause in both these cases was a bad module.

### Seismic Noise

- There was no external seismic interference seen during the prospect.

- Due to the prevalent weather conditions, swell noise was extensive.  The majority of the lines acquired exhibited some degree of swell noise.  A bench mark line was established early on in the survey and all subsequent lines were compared to this bench mark using brute stack sections and RMS noise analysis.  The bench mark line was sequence 12, which was rejected by a small margin after extensive processing tests.

- Screw noise from passing shipping was seen on occasions but was never of sufficient magnitude to warrant reacquiring the data.

- An increase in strum noise was seen on heads of outer cables following the extension of the vane warps before acquiring sequence 30.  This was cured by installing new, faired vane warps before acquiring sequence 142.

### Fishing

The prospect was split into swathes and the local fishermen were informed of the location of each swathe the vessel was operating in, together with estimated completion times.  While this did not completely eliminate incidents, as a few lines were aborted due to fishing gear ahead, it reduced them and co-operation was generally good.

#### Perfect Lady Fishing Equipment Pick up Summary.

| Boat Name | Reg. | Owner Name | No. | Type | Status | Date | Lat.-Long. (in Deg-Min) | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Arctic Gull | X6K | Ian McEackeran | 4 | Pots | Pulled | 15/12/99 | 142-24.84 S 38-56.08 E |  |
| Aquamarine | XSY | Paul Armstrong | 8 | Pots | Pulled | 15/12/99 | 142-25.52 S 38-58.81 E |  |
| Dolphin Ii | XNL |  | 6 | Pots | Pulled | 01/03/00 | 143-02.98 S 38-54.44 E | Wife picked up Pt.Fairy 4th |
| Amayos | XCF | David Sharp | 2 | Pots | Pulled | 01/11/00 | 142-41.15 S 39-03.27 E |  |
| Arctic Gull | X6K | Ian McEackeran | 8 | Pots | Pulled | 21/01/00 | 142-59.82 S 39-17.84 E 142-59.?? S 39-17.09 E |  |
| Arctic Gull | X6K | Ian McEackeran | 7 | Pots | Pulled | 28/01/00 | 142-59.63 S 39-16.78 E 142-59.97 S 39-16.01 E | 1 x Pot Broke off |
| Arctic Gull | X6K | Ian McEackeran | 7 | Pots | Pulled | 29/01/00 | 142-54.76 S 39-18.10 E 142-54.51 S 39-17.69 E |  |
| Melina E | UPA | Gary Edwards | 1 | Pot | Pulled | 31/01/00 | 142-53.94 S 39-21.26 E | Picked up 9th Feb |
| Arctic Gull | X6K | Ian McEackeran | 4 | Pots | Pulled | 02/01/00 | 142-52.12 S 39-17.86 E 142-52.36 S 39-17.14 E 142-52.88 S 39-16.39 E |  |
| Georges Bay | TET | Shannon Churchill | 5 | Pots | Pulled | 02/04/00 | 142-54.11 S 39-23.67 E 142-54.89 S 39-23.76 E 142-54.39 S 39-23.89 E |  |
|  |  |  |  |  |  |  | 142-54.?? S 39-24.04 E 142-54.52 S 39-24.16 E |  |
| Gwen Kane | XSZ | Wayne Towers | 6 | Pots | Pulled | 03/10/00 | 142-57-49 S 39-11-16 E 142-57-63 S 39-11-88 E | Pots were inside our area |
| Putty's Pride | UHQ | Ross Ferrier | 1 | Pot | Pulled | 16/3/00 |  |  |
| Georges Bay | TET | Shannon Churchill | 7 | Pots | Pulled | 04/01/00 | 142-50-45 S 39-17-57 | Pots moved back after pasting |