# SURVEY VESSELS

## Figure 3.10-1 R/V Western Pride

## R/V Western Pride

### Introduction

The R/V WESTERN PRIDE is a purpose built seismic vessel, constructed at the Ulstein Hatlo Yard at Ulsteinvik in Norway. She was christened in 1991 and re–fitted in April 1998 in Aarhus, Denmark. She is equipped for 8 x 6000 metre streamers, and has 8 strings of low-pressure air guns. Propulsion and compressors are all mechanically driven, with all rotating machinery resiliently mounted to ensure hydroacoustic noise is kept to a minimum. The hull and propulsion system is designed specifically for extremely low noise level.

### Vessel Description

Vessel Name	Western Pride

Port of Registry	Panama

Flag	Republic of Panama.

Year Built	1991

Where Built	Ulsteinvik, Norway

Builders Name	Ulstein Verft AS

Built As	Seismic Survey Vessel

Vessel Upgrade	March - June 1998 Aarhus Denmark

Classification Society	Det Norske Veritas

Classification	DnV 1A1,ICE-C, EO, HELDK.

Registration number	19993-9.

Call sign	3EYQ8.

Owners	Western Sea Services

Operators	Western Geophysical a division of Baker Hughes

Dimensions

Length	71.5 metres.

Beam	17.0 metres.

Draft	5.9 metres.

Gross Tonnage	2,945

Net Tonnage	883

Accommodation capacity	56 + 1 Hospital.

Maximum Cruising speed	14 knots.

Cruising range	36 days + 4 days emergency fuel

11,000 nautical miles

Fuel capacity	1,000 cubic metres (900 service + 100 emergency)

Fuel Consumption cruising	Approx. 25 cubic metres / day

Fuel Consumption shooting	Approx. 28-30 cubic metres per day (30-32 days)

Main Engine Lube oil capacity	12 cubic metres ( 12,000 litres ).

Cable oil capacity	16 cubic metres (16,000 litres).

Freshwater capacity	110 cubic metres

Freshwater making capacity	1 x Serck COMO, RXT 12/8, 12 tons/day.

1 x Aqua Sep 9 tons/day reverse osmosis.

Freshwater endurance	Unlimited - water makers.

Incinerator	Teamtec/Golar Marine Incinerator - garbage & waste oil

Helideck	Rated up to & including AS 332 Super Puma, S76, Bell 212 helicopters,

Helideck Approval	CAA/DNV approved.

Lifeboats	2 x 48 person, enclosed, diesel driven.

Liferafts	8 x 16 person as per SOLAS requirements.

Fast Rescue Craft 	1 x Seabear 23 inboard diesel, davit deployed.

Work boat	1 x CMV ( Cable Maintenance Vessel)

Main Engines	2 x Bergen Diesel BD32M6, each of 3,600 bhp.

Propulsion	2 x 4 bladed Ulstien - Liaaen variable pitch.

Main generators	2 x Leroy Somer 1,665 kVA, 450V/60 Hz, 3 phase, shaft driven.

Aux. Generator	1 x Caterpillar 3512 900 KVA, 450V

Clean Power	2 x 75KVA, 208/120, 60 Hz

Bow thruster	Ulstien-Liaaen 150 TV 800 hp, variable pitch propeller

Seismic Hydraulic Equipment	Odim

Fixed Fire Fighting systems

Halon	Engine / Compressor spaces

Recording room / Tape store

Hydraulic room

Galley

Incinerator room.

Foam (AFFF)	Cable Reels

Helideck.

CO2	Paint locker.

Navigation	SAL Log 502-6 electromagnetic speed log.

Furuno FAR-2822, X band ARPA.

Decca Marine Bridgemaster 343/12E, S band ARPA.

Furuno FSN-50 transit satellite receiver.

Furuno GP-500 GPS receiver.

Furuno LC-90 Mk II Loran-C receiver.

Furuno FD-525 VHF direction finder.

Furuno FE-680 echo sounder, 0-2,100 metres.

Furuno DFax 208-A weather facsimile receiver.

Sait Navtex 2 - XH5123 receiver.

Robertson AP9 Mk II autopilot.

C Plath SR-180 Mk1 gyrocompass.

Taiyo TD-C318 emergency automatic direction finder.

Emergency Positioning	2 x Jotron Search and Rescue Transponders (SARTS)

Jotron X-94492 Sarsat Cospas 406 MHz EPIRB

Communications 	Vingtor shipboard communications system

(GMDSS STANDARDS)	Thrane & Thrane TT 3000 standard-C Inmarsat telex system.

Thrane & Thrane TT 3210A integrated radio telex system.

2 x Skanti DSC 3000 VHF DSC Controller Receiver

2 x Skanti TRP-3000 VHF radios ( to 5 slave handsets )

Sailor RT 2047 VHF radio/telephone.

Skanti DSC 9000 MF/HF DSC Contoller / Receiver.

Skanti Control Unit 8000 HF-SSB Transceiver.

Skanti WR 6000 Watch Receiver 2182 kHz.

2 x Navico GMDSS hand held VHF radios.

Sailor RT 2047 VHF radio / telephone, simplex & duplex.

Jotron TR-6102 AM/VHF aeronautical radio

Dittel FSG 7MPS UHF Transceiver aeronautical radio

Inmarsat	JRC Inmarsat A - JUE 45A Mk II - Voice, telex, fax, data

V-Sat 	Data Marine Systems C band - Voice, fax, data

### Vessel V-SAT contact

Tel: 	00 61 (0) 8 92682 663 (Party Chief)

Tel: 	00 61 (0) 8 92682 636 (Co-ordinator/Fax)

Tel: 	00 61 (0) 8 92682 649 (Client)

Tel: 	00 61 (0) 8 92682 664 (Crew)

### Vessel INMARSAT contact

Tel: 	00 873 1335433

Fax:	00 873 1335434