# GEODETIC & CARTOGRAPHIC PARAMETERS

## Local Datum

Local Datum Name		AGD84

Spheroid			Australian National Spheroid (ANS)

Semi-major axis		6378160.000

1/flattening 			298.2500000

## Satellite Datum

Satellite Datum Name		WGS 84

Spheroid			WGS 84

Semi-major axis		6378137.000

1/flattening 			298.257224

## Shift Parameters

From WGS 84 to Local Datum

Dx = +116.0 m

Dy = +50.47 m

Dz = -141.69 m

Rx = -0.23 arc sec*

Ry = -0.39 arc sec*

Rz = -0.344 arc sec*

Scale factor = -0.0983 ppm

*As entered in the Spectra INS, which uses the Bursa Wolf Rotation Convention, a 'left handed' rotation rule. For Co-ordinate Frame Rotation, which is a 'right handed' rotation rule, the signs of the rotations must be reversed.

## Mapping Projection

Mapping Projection Name	AMG ZONE 54 (UTM)

Origin of Latitude		000° 00' 00.00" N

Origin of Longitude		141° 00' 00.00" E

False Northing			10,000,000.0 m

False Easting			500,000.0 m

Central Meridian		141° 00' 00.00" E

Scale factor at CM		0.9996

Grid Units			Metres

## Geoidal/Spheroidal Mean Undulation

-2.624 m	Calculated using the OSU91A model at the nine boundary points of the survey grid

|  | Easting (local projection) | Northing (local projection) | Geoid/Spheroid Separation |
| --- | --- | --- | --- |
| P1 | 649973.0 | 5682748.5 | -2.768 |
| P2 | 652442.7 | 5698341.7 | -2.294 |
| P3 | 666764.2 | 5696073.4 | -1.947 |
| P4 | 672475.0 | 5692017.6 | -1.897 |
| P5 | 670691.7 | 5680757.9 | -2.237 |
| P6 | 675759.3 | 5676955.8 | -2.197 |
| P7 | 670890.3 | 5646214.0 | -3.331 |
| P8 | 649185.8 | 5649651.7 | -4.219 |
| P9 | 653982.5 | 5679936.7 | -2.730 |
|  |  | Average: | -2.624 |

## Magnetic declination

+11.103°	Calculated using the IGRF95 model for 25-Dec-1999 at the nine boundary points of the survey grid

|  | Easting (local projection) | Northing (local projection) | Magnetic Declination |
| --- | --- | --- | --- |
| P1 | 649973.0 | 5682748.5 | 11.021 |
| P2 | 652442.7 | 5698341.7 | 10.991 |
| P3 | 666764.2 | 5696073.4 | 11.076 |
| P4 | 672475.0 | 5692017.6 | 11.119 |
| P5 | 670691.7 | 5680757.9 | 11.141 |
| P6 | 675759.3 | 5676955.8 | 11.180 |
| P7 | 670890.3 | 5646214.0 | 11.242 |
| P8 | 649185.8 | 5649651.7 | 11.110 |
| P9 | 653982.5 | 5679936.7 | 11.051 |
|  |  | Average: | 11.103 |

## Binning Grid

The in-line cell size used for both real-time fold-of-coverage acquisition displays and for offline fold-of-coverage displays was 12.5 m.

The cross-line cell size, based on the CMP spacing, was 25.0 m.

The binning grid used was defined using Grid distances.

A shotpoint layback was used such that the first shotpoint of the line coincided with the first CMP hit in the full-fold area.

### Binning Grid Parameters

| Binning Grid |  |  |
| --- | --- | --- |
| Map Grid Origin Easting | 643880.97 | (bin centre) |
| Map Grid Origin Northing | 5647960.68 | (bin centre) |
| Map Grid Bearing (°) | 9.000 | (In-line axis) |
|  | In-line | X-line |
| Bin Grid Extent (m) | 53587.50 | 27475.00 |
| Bin Number at Origin | 801 | 978 |
| Bin Number Increment | 1 | 1 |
| Bin Dimensions (m) | 12.5 | 25.0 |
| Apply scale factor | No (using mapping grid distances) |  |
| Nominal Offset Distribution |  |  |
| Minimum Offset (m) | 150 |  |
| Maximum Offset (m) | 4750 |  |
| Offset Increment (m) | 50 |  |
| Coverage Groups | Near Offset (m) | Far Offset (m) |
| Nears | 150 | 1300 |
| Near Mids | 1300 | 2450 |
| Far Mids | 2450 | 3600 |
| Fars | 3600 | 4750 |