# DAILY LOG

Please note that all times are approximate and are for operational information.  They are not necessarily the final times used for charging.  The start and end of line times given refer to the first and last good shot whenever applicable.

## INVESTIGATOR 3D LINES SEQ 001-147

06-December-99 to 07-December-99

In transit

08-December-99

07:00	Anchor off Freemantle for refuelling and resupply

17:30	Anchor raised, continue transit

09-December-99 to 12-December-99

In transit

13-December-99

21:00	Begin deploying cables

14-December-99

Deploying cables

Partial crew change by helicopter

15-December-99

Deploying cables

Complete remaining crew change by helicopter

16-December-99

Deploying cables

Weather increasing to 30-40 kts, 3-4 m seas.  Unable to continue deploying.  Down for weather

22:45	Tag line between streamers 7 and 8 parted, but unable to retrieve d/t sea state

17-December-99

Down for weather

17:09	Tag line between streamers 1 and 2 parted, but unable to retrieve d/t sea state

18-December-99

Weather moderating

Inner cables recovered and untangled

Deploying cables

19-December-99

Deploying cables

20:30	Techno float on cable 6 tangled on leadin due to heavy swell

22:05	Techno float untangled

22:30	Techno float tangled again

23:30	Techno float untangled

20-December-99

Deploying cables

00:50	Unable to deploy cable 5 as swell is pushing tailbuoy over cable 6.  Deploying cable 4 after course adjustment

08:45	Tagline between cables 3 and 4 tangles on Techno float.  Cable heads retreived to untangle line.

13:05	Bunkering at sea commences

20:00	Bunkering at sea completed

22:30	All cables deployed.  Begin deploying guns

21-December-99

Deploying guns and running CRS test lines

17:00	All guns deployed.  Adjusting towing configuration

21:20	Retreiving guns to adjust offsets

22-December-99

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Adjusting towing configuration

04:50	Power failure due to fire in auxilliary generator.  Fire extinguished.  Propulsion and steering maintained throughout

05:25	Clean power restored

06:15	Recording room instrumentation powered up.

10:01	CMV launched to add birds to outer cables

10:45	CMV operation aborted due to swell

11:57	SOL	W00INV2048P1

Line aborted and sequence stratched due to CRS multishot configuration problems.  No seismic data recorded.

13:33	EOL	W00INV2048P1

Investigator 3D acquisition commences

16:11	SOL	W00INV1840P1	1880	6.5 Stbd (West)	9.3 µBar	SE 18 kts	3.0 m	001

Line rejected d/t separations.  Reshot as Seq# 28*

17:26	EOL	W00INV1840P1	188	930	0	0.7 Stbd (West)	N/A	SE 20 kts	3.0 m	001

22:55	SOL	W00INV2048P1	8	903	1001	6.5 Port (West)	6.3 µBar	SE 20 kts	2.5 m	002

SP 3396-3683: Early EOL d/t Gun Errors.  Reshot as Seq# 22

23-December-99

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

03:16	EOL	W00INV2048P1	8	3516	3395	9.3 Port (West)	5.0 µBar	SE 20 kts	2.5 m	002

03:45	Loss of optic data to cable 1 following apparent in water collision

08:56	SOL	W00INV1936P1	188	3714	3617	2.0 Port (East)	8.0 µBar	SSE 20 kts	3.0 m	003

SP 1913-1887: MSX Lock-up.  Reshot as Seq# 36

SP 2892-2876: Gun Errors (Even Shots Only).  No reshoot required

SP 3617-817: Cable 1 : CH 1-368 No Data Telemetry.  No reshoot required

13:54	EOL	W00INV1936P1	188	807	817	9.0 Stbd (West)	4.5 µBar	SSE 25 kts	3.0 m	003

Record length changed from 5.0 seconds to 4.5 seconds

19:26	SOL	W00INV1952P1	8	903	1001	3.5 Stbd (East)	3.7 µBar	SSE 15 kts	2.5 m	004

SP 1001-3784: Cable 1 : CH 1-368 No Data Telemetry.  No reshoot required

24-December-99

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:18	EOL	W00INV1952P1	8	3794	3784	4.7 Port (West)	4.4 µBar	SSE 15 kts	2.5 m	004

04:33	SOL	W00INV2032P1	188	3612	3515	12.5 Stbd (West	7.1 µBar	SSE 24 kts	2.5 m	005

SP 3515-817: Cable 1 : CH 1-368 No Data Telemetry.  No reshoot required

08:59	EOL	W00INV2032P1	188	807	817	2.0 Port (East)	9.5 µBar	SSE 14 ts	2.0 m	005

13:06	SOL	W00INV2016P1	80	3.8 Port (West)	7.3 µBar	SE 15 kts	2.0 m	006

Line rejected d/t acoustics/weather.  Reshot as Seq# 9*

17:58	EOL	W00INV2016P1	80	5.8 Port (West)	10.1 µBar	W 30 kts	3.0-3.5 m	006

23:51	SOL	W00INV1968P1	1880	8.5 Stbd (West)	13.8 µBar	E 30 kts	3.0 m	007

Line rejected d/t acoustics/weather.  Reshot as Seq# 10*

25-December-99

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

04:31	EOL	W00INV1968P1	1880	10.5 Stbd (West)	6.0 µBar	SE 27 kts	3.0 m	007

10:53	SOL	W00INV1888P1	80	7.0 Stbd (East)	6.7 µBar	ESE 27kts	3.0 m	008

Line rejected d/t acoustics/weather.  Reshot as Seq# 14*

15:56	EOL	W00INV1888P1	80	8.2 Port (West)	4.7 µBar	ENE 35 kts	3.0 m	008

Down for weather.  Retrieving guns

19:00	All guns onboard

Retrieving cables 4 and 5 in order to reduce the number of deployed cables from 8 to 6

22:00	Centre tag tangles with cable 5 due to rough seas. Loss of bird line on cable 5

26-December-99

00:00	Replacing damaged section from cable 5

01:30	Retrieving cables 4 and 5

04:40	Cables 4 and 5 onboard.  Retrieving head of cable 1

09:15	Replacing cable 1 lead-in.  Damaged sheathing and armour coinciding with optical break approx. 150 m from tail.

17:45	Replacement lead-in failing at head termination.  Changing out lead-in again.

19:30	Lead-in tests good.  Cable 1 being retrieved to fix failed rGPS on tailbuoy.

27-December-99

Deploying cable 1 and tagging starboard side

Unable to turn back to prospect due to rough sea conditions.  Waiting for weather to improve.

28-December-99

Tagging port side until rough weather prevents further work

29-December-99

Waiting for weather to improve

30-December-99

02:25	Weather lessening.  Retrieving cable 8

05:23	Port vane wire parts.  Retrieving all gear.

13:30	Spotter plane searching for lost vane

20:50	Unable to contiue retrieving cables due to rough weather conditions

21:00	Spotter plane leaves area without locating lost vane

31-December-99

Still unable to contiue retrieving cables due to rough weather conditions

06:25	Smit Lloyd (chase boat) commences search pattern for lost vane

09:30	Spotter plane searching for lost vane

10:45	Smit Lloyd (chase boat) locates vane

Waiting for weather to improve

01-January-00

01:30	Weather lessening.  Retrieving cables

04:05	Cables all onboard

12:27	Vane back onboard after retreival operation by CMV

13:05	Deploying cables

02-January-00

Deploying cables

09:56	Bunkering at sea commences

19:26	Bunkering at sea completed

03-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Deploying cables and guns

05:00	All gear deployed, adjusting offsets

09:29	SOL	W00INV2026P1	80	1.0 Port (East)	N/A	SW 15 kts	1.0 m	009

Line rejected d/t low source volume.  Reshot as Seq# 11

12:01	EOL	W00INV2026P1	80	6.0 Port (East)	N/A	SW 15 kts	1.5 m	009

13:18	Clean power failure following generator tripping out

15:01	Power restored and recording room instrumentation back online

17:02	SOL	W00INV1954P1	188	3696	3599	6.0 Port (East)	4.3 µBar	SW 10 kts	2.5 m	010

21:44	EOL	W00INV1954P1	188	807	817	6.2 Stbd (West)	3.3 µBar	SW 15 kts	3.0 m	010

04-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:40	SOL	W00INV2026P2	8	904	1001	6.0 Port (West)	3.6 µBar	SW 10 kts	2.5 m	011

05:05	EOL	W00INV2026P2	8	3716	3706	6.2 Stbd (East)	7.1 µBar	SW 15 kts	3.0 m	011

08:15W00INV2014P1

Line aborted and sequence stratched.  No seismic data recorded.

Guns retrieved.  Waiting for weather to improve

05-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Waiting for weather to improve

16:10	Deploying guns

21:17	SOL	W00INV1918P1	8	904	0	2.8 Stbd (East)	14.5 µBar	SW 25 kts	2.5 m	012

Line rejected d/t weather noise.  Reshot as Seq# 31

06-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:58	EOL	W00INV1918P1	8	3831	0	1.7 Stbd (East)	16.6 µBar	S 24 kts	3.0 m	012

05:56	SOL	W00INV1906P1	188	3748	0	3.9 Port (East)	12.7 µBar	SSE 15-20 kts	2-2.5 m	013

Line rejected d/t weather noise.  Reshot as Seq# 29

10:37	EOL	W00INV1906P1	188	807	0	2.1 Port (East)	7.9 µBar	SSE 20 kts	2.0 m	013

14:03	SOL	W00INV1894P1	8	904	1001	3.9 Port (West)	12.7 µBar	SSE 15-20 kts	2-2.5 m	014

18:45	EOL	W00INV1894P1	8	3858	3848	2.1 Port (West)	7.9 µBar	SSE 20 kts	2.0 m	014

17:24	Recording room powered down prior to generator change over.

23:19	SOL	W00INV2014P1	188	3634	3536	3.8 Stbd (West)	8.9 µBar	S 20 kts	2.5 m	015

07-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

03:50	EOL	W00INV2014P1	188	807	817	9.0 Stbd (West)	7.4 µBar	S 20  kts	2.5 m	015

07:14	SOL	W00INV1966P1	8	904	1001	1.0 Stbd (East)	6.5 µBar	SSE 15 kts	2.0 m	016

11:51	EOL	W00INV1966P1	8	3780	3770	2.0 Port (West)	6.8 µBar	SSE 15 kts	2.0 m	016

14:35	SOL	W00INV1894I1	188	3760	3663	8.0 Stbd (West)	7.3 µBar	SSE 18 kts	2-2.5 m	017

19:23	EOL	W00INV1894I1	188	807	817	1.5 Stbd (West)	9.6 µBar	SSE 13 kts	3.0 m	017

22:02	SOL	W00INV2002P1	8	903	1001	0.8 Port (West)	9.9 µBar	SE 12 kts	3.5 m	018

08-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

02:42	EOL	W00INV2002P1	8	3742	3732	7.3 Port (West)	8.4 µBar	NE 20 kts	2.5 m	018

05:32	SOL	W00INV1882P1	188	3773	3675	6.8 Stbd (West)	10.4 µBar	ESE 15 kts	3.5 m	019

10:17	EOL	W00INV1882P1	188	807	818	2.6 Port (East)	7.2 µBar	E 20 kts	3.0 m	019

Guns retreived to repair rGPS on string 1

17:33	SOL	W00INV1870P1	8	904	1001	6.8 Port (West)	10.4 µBar	E 22 kts	3.0 m	020

22:17	EOL	W00INV1870P1	8	3882	3872	2.6 Stbd (East)	7.2 µBar	E 25 kts	3.0 m	020

09-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:27	SOL	W00INV1990P1	188	3658	3561	3.7 Stbd (West)	5.8 µBar	E 15 kts       E	2.0 m	021

SP 2039-817: Early EOL d/t Fishing vessel in path.  Reshot as Seq# 27

03:57	EOL	W00INV1990P1	188	2028	2040	5.0 Stbd (West)	3.8 µBar	E 15 kts	2.5 m	021

07:55	SOL	W00INV2048R1	8	3288	3386	1.8 Port (West)	4.8 µBar	ENE 22 kts	3.5 m	022

08:24	EOL	W00INV2048R1	8	3693	3683	0.3 Port (West)	3.6 µBar	ENE 22 kts	3.5 m	022

12:28	SOL	W00INV1870I1	188	3785	3688	1.0 Stbd (West)	3.4 µBar	SE 15 kts	1.5 m	023

17:15	EOL	W00INV1870I1	188	809	817	0.4 Stbd (West)	2.1 µBar	Light air	1.5 m	023

21:10	SOL	W00INV1942I1	8	1028	1125	7.9 Stbd (East)	2.4 µBar	Calm	1.5 m	024

SP 2541-3119: Coverage not required.  No reshoot required

10-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:36	EOL	W00INV1942I1	8	3806	3796	1.7 Port (West)	2.0 µBar	Calm	1.5 m	024

04:22	SOL	W00INV1858P1	188	3799	3701	6.8 Stbd (West)	3.1 µBar	Calm	Calm	025

09:06	EOL	W00INV1858P1	188	807	817	0.7 Port (East)	1.9 µBar	Calm	Calm	025

Resupply at sea

16:24	SOL	W00INV1978P1	8	904	1001	3.6 Port (West)	2.5 µBar	Light airs	1.0 m	026

20:59	EOL	W00INV1978P1	8	3767	3757	0.6 Stbd (East)	2.3 µBar	SE 12 kts	1.5 m	026

11-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:14	SOL	W00INV1978I1	188	3671	3573	1.0 Stbd (West)	2.6 µBar	SE 10 kts	0.5 m	027

04:47	EOL	W00INV1978I1	188	807	817	5.0 Stbd (West)	1.6 µBar	SE 6 kts	0.3 m	027

08:53	SOL	W00INV1846P1	8	903	1001	2.0 Stbd (East)	2.7 µBar	SE 15 kts	1.5 m	028

13:35	EOL	W00INV1846P1	8	3908	3898	3.6 Stbd (East)	2.0 µBar	ENE 16kts	1.0 m	028

16:32	SOL	W00INV1906R1	1880	10.5 Port (East)	4.0 µBar	SE 18 kts	2.0 m	029

Line rejected d/t vane wire failure.  Reshot as Seq# 38

Port vane wire parted

16:33	EOL	W00INV1906R1	1880	11.5 Port (East)	N/A	SE 18 kts	2.0 m	029

16:50	Retreiving guns

18:53	All guns onboard.  Retrieving cables

12-January-00

00:30	Tailbuoys 2 and 6 tangle

12:45	Cable 2 onboard with tailbuoy 6 still attached.  Untangling buoys

13:40	Tailbuoy 6 released

15:30	Tailbuoy 6 towing correctly.  Retrieving cables.

13-January-00

11:49	All gear onboard.  Heading for lost vane.

16:10	CMV unable to grapple vane due to heavy seas.  Waiting for the weather to improve.

14-January-00

Waiting for weather to improve

18:45	Port vane retrieved following recovery operation by CMV.  400 metres of trailing wire cut and let go overboard.

22:50	Deploying cables

length of vane warp increased to further isolate cables from vanes.

15-January-00

Deploying cables.  Lead-in on cable 6 replaced (optics failed when vane parted)

16-January-00

Deploying cables

17-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Deploying cables

06:15	Cables all deployed, deploying guns

10:06	All gear deployed

11:02	SOL	W00INV2002I1	8	904	1001	0.6 Port (West)	5.2 µBar	SE 15 kts	1.5 m	030

12:59	EOL	W00INV2002I1	8	2182	2179	4.1 Stbd (East)	9.6 µBar	SSE 5-10 kts	1.5 m	030

13:05	Retrieving gear prior to heading to port

18-January-00

06:00	All gear retrieved.  Raising hull transducer.

09:00	Hull transducer raised.  Heading for Portland, Victoria.

13:56	Pilot onboard

14:30	Alongside Portland

Crew Change

19-January-00 to 21-January-00

Alongside Portland.  Sailing delayed due to poor weather on prospect.

22-January-00

05:40	Pilot onboard

06:18	Depart Portland

14:45	Weather still too poor to head straight to prospect, heading fair seas instead and waiting for weather to improve.

23-January-00

16:30	Deploying cables

24-January-00

Deploying cables

25-January-00

Deploying cables

08:30	All cables out waiting for weather to improve before deploying guns.

10:30	Cable 3 fails.  Picking up cable 3

21:00	Cable 3 fixed and being redeployed.

26-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

02:25	Deploying guns

04:30	Guns deployed.  Heading for line

05:30	Fishing vessel in path.  Moving offline to avoid

06:45	Cleared fishing boat and heading back for line

07:36	SOL	W00INV1918R1	8	902	0	10.4 Port (West)	N/A	E 35 kts	4.0 m	031

Line rejected d/t Fishing vessel.  Reshot as Seq# 32

07:47	EOL	W00INV1918R1	8	1113	0	N/A	N/A	E 35 kts	4.0 m	031

14:25	SOL	W00INV1918R2	8	903	0	2.8 Port (West)	7.8 µBar	NE 20 kts	3.0 m	032

Line rejected d/t weather.  Reshot as Seq# 34

14:53	EOL	W00INV1918R2	8	1283	0	4.1 Port (West)	N/A	NE 20 kts	3.0 m	032

Waiting for weather to improve, running CRS test line.

22:30	Cable 6 lost al data

27-January-00

01:25	All guns onboard

02:00	Cable 6 slipring bypassed and data good

21:00	Weather moderating.  Retrieving cable 2 to fix bird-line leakage

28-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:00	Cable 2 repaired and redeployed

09:30	CMV lauched to check cable 3 for fishing gear following failure of channels

10:50	Retrieving cable 3 and reattaching loose bird.

15:45	All cables deployed.  Deploying guns

17:20	All guns deployed.

21:45	SOL	W00INV2026I2	188	1371	1350	10.0 Stbd (West)	3.4 µBar	SSW 10 kts	1.5 m	033

22:39	EOL	W00INV2026I2	188	807	817	3.0 Stbd (West)	N/A	SSW 5 kts	2.0 m	033

29-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:47	SOL	W00INV1918R3	8	904	1001	2.6 Stbd (East)	4.4 µBar	SSE 10kts	2.5 m	034

06:22	EOL	W00INV1918R3	8	3831	3821	1.9 Port (West)	4.7 µBar	SSE 15kts	1.5 m	034

10:20	SOL	W00INV2038I1	188	3517	3420	8.2 Stbd (West)	8.9 µBar	SSW 20kts	2.0 m	035

SP 3420-3045: Cable 5 : CH 1-368 Cable Depth Control.  No reshoot required

10:58	EOL	W00INV2038I1	188	2951	3045	0.0 Stbd (West)	N/A	SSW 20kts	2.0 m	035

12:57	SOL	W00INV1930R1	188	2021	1923	0.6 Port (East)	10.0 µBar	SW 20 kts	3.0 m	036

13:01	EOL	W00INV1930R1	188	1867	1877	3.0 Stbd (West)	12.0 µBar	SW 20 kts	3.0 m	036

16:25	SOL	W00INV1846I1	8	1602	0	7.8 Stbd (East)	8.2 µBar	SW 20 kts	2-2.5 m	037

Line rejected d/t weather.  Reshot as Seq# 57

17:33	EOL	W00INV1846I1	8	2351	0	1.5 Stbd (East)	8.3 µBar	SW 20 kts	3.0 m	037

23:24	SOL	W00INV1906R2	188	3747	0	6.6 Stbd (West)	13.4 µBar	SSW 15kts	4.0 m	038

Line rejected d/t weather.  Reshot as Seq# 39

30-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:45	EOL	W00INV1906R2	188	2607	0	1.3 Port (East)	N/A	SSW 15kts	4.0 m	038

07:57	SOL	W00INV1906R3	80	N/A	12.7 µBar	SW 10 kts	3.0 m	039

Line rejected d/t weather.  Reshot as Seq# 40

08:17	EOL	W00INV1906R3	80	N/A	N/A	SW 10 kts	3.0 m	039

08:20	Retrieving guns

10:05	Guns onboard.  Waiting for the weather to improve.

31-January-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:00	Deploying guns

01:40	Guns deployed

06:06	SOL	W00INV1906R4	188	3748	3650	1.3 Port (East)	8.1 µBar	SW 10kts	4.0 m	040

10:46	EOL	W00INV1906R4	188	807	817	6.2 Stbd (West)	6.6 µBar	SW 2 kts	3.0 m	040

17:27	SOL	W00INV1918I1	8	803	1001	5.1 Stbd (East)	6.5 µBar	SW 5 kts	3.0 m	041

18:42	EOL	W00INV1918I1	8	3831	3821	2.0 Stbd (East)	3.3 µBar	SW 15 kts	3.0 m	041

23:26	SOL	W00INV1894I2	188	3861	3663	9.1 Stbd (West)	3.6 µBar	SW 15 kts	2.0 m	042

SP 1838-817: Early EOL d/t MIDAS Lock-up.  Reshot as Seq# 43

01-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

02:24	EOL	W00INV1894I2	188	1804	1839	0.5 Stbd (West)	N/A	SW 20 kts	3.0 m	042

08:59	SOL	W00INV1894I3	188	1946	1848	5.0 Stbd (West)	2.6 µBar	E 20kts	2.0 m	043

10:38	EOL	W00INV1894I3	188	807	817	2.5 Stbd (West)	N/A	E 25kts	2.0 m	043

13:32	SOL	W00INV1666P1	8	903	1001	1.0 Stbd (East)	5.8 µBar	East 25 kts	3.0 m	044

SP 2912-3242: Cable 1 : CH 1-368 Cable Depth Control.  No reshoot required

20:26	EOL	W00INV1666P1	8	4998	4988	5.1 Port (West)	2.1 µBar	East 20kts	1.5 m	044

22:52	SOL	W00INV1834P1	188	4734	4637	9.0 Stbd (West)	2.8 µBar	East 15 kts	2.0 m	045

02-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:08	EOL	W00INV1834P1	188	807	817	8.3 Port (East)	2.2 µBar	ENE 10Kts	1.5 m	045

07:18	SOL	W00INV1654P1	8	903	1001	2.0 Stbd (East)	2.1 µBar	Calm	0.0 m	046

14:00	EOL	W00INV1654P1	8	5010	5000	4.0 Port (West)	2.5 µBar	Calm	0.5 m	046

18:39	SOL	W00INV1834I1	188	4735	4637	0.8 Port (East)	1.8 µBar	E 10 kts	slight	047

03-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:01	EOL	W00INV1834I1	188	807	817	0.4 Port (East)	1.6 µBar	E  8 kts	0.5 m	047

03:17	SOL	W00INV1642P1	8	903	1001	0.0	1.5 µBar	E 10kts	0.5 m	048

09:56	EOL	W00INV1642P1	8	5022	5012	1.5 Port (West)	1.9 µBar	0 kts	0.5 m	048

11:54	SOL	W00INV1822P1	188	4746	4649	7.5 Stbd (West)	1.9 µBar	5 kts	1.0 m	049

SP 2664-817: Early EOL d/t Gun Errors.  Reshot as Seq# 50

15:13	EOL	W00INV1822P1	188	2624	2665	0.5 Stbd (West)	1.6 µBar	10 kts	2.0 m	049

Working on guns

19:35	SOL	W00INV1822P2	188	2772	2675	5.5 Port (East)	2.7 µBar	South 10 kts	1.5 m	050

22:43	EOL	W00INV1822P2	188	807	817	0.5 Stbd (West)	N/A	outh 10 kts	1.5 m	050

04-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:00	SOL	W00INV1630P1	8	904	1001	3.8 Port (West)	1.9 µBar	SWN 15kts	2.0 m	051

07:43	EOL	W00INV1630P1	8	5034	5024	3.0 Stbd (East)	3.6 µBar	NNE 15kts	SW 2.0 m	051

09:50	SOL	W00INV1810P1	188	4759	4661	1.6 Port (East)	2.8 µBar	NE 10 kts	2-3 m	052

16:12	EOL	W00INV1810P1	188	807	817	3.8 Port (West)	4.0 µBar	ENE15 kts	3-4 m	052

18:36	SOL	W00INV1618P1	8	903	1001	8.5 Stbd (East)	2.5 µBar	ENE 15 kts	SW 3-4 m	053

05-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:24	EOL	W00INV1618P1	8	5046	5036	1.9 Port (West)	5.0 µBar	NW 5 kts	SW 2 m	053

Port engine stut down to repair faulty injectors

04:44	SOL	W00INV1798P1	188	4770	4673	1.6 Port (East)	3.0 µBar	NE 10 kts	2.5 m	054

SP 1649-817: Early EOL d/t Cable Depth Control.  Reshot as Seq# 60

10:03	EOL	W00INV1798P1	188	1337	1650	2.2 Port (East)	11.2 µBar	WSW 25kts	4.0 m	054

Retrieving guns.  Waiting for the weather to improve.

06-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Waiting for the weather to improve.

16:20	Deploying guns

18:50	Guns deployed

23:29	SOL	W00INV1606P1	80	3.2 Stbd (East)	11.4 µBar	SE 15 kts	1.5 m	055

Line rejected d/t weather.  Reshot as Seq# 58

07-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

03:12	EOL	W00INV1606P1	80	1.1 Stbd (East)	N/A	SE 20 kts	1.5 m	055

03:59	SOL	W00INV1630I1	80	N/A	N/A	SE 20 kts	1.5 m	056

Line rejected d/t weather.  Reshot as Seq# 108 (1642I1)

04:01	EOL	W00INV1630I1	80	N/A	N/A	SE 20 kts	1.5 m	056

06:45	SOL	W00INV1846I2	188	2798	2700	2.2 Stbd (West)	5.2 µBar	ENE 5 kts	3.0 m	057

SP 972-928, 2080-2016, 2231-2191, 2625-2541: Cable 1 and 2 : CH 1-368 Poor Geometry.  No reshoot required

09:52	EOL	W00INV1846I2	188	807	817	5.3 Port (East)	5.2 µBar	SSE 10kts	3.0 m	057

12:19	SOL	W00INV1606P2	80	1.5 Stbd (East)	4.4 µBar	SSE 15 kts	2.0 m	058

Line rejected d/t timebreak problems/poor acoustics.  Reshot as Seq# 61

13:38	EOL	W00INV1606P2	80	1.0 Stbd (East)	N/A	SSE 15 KT	2.0 m	058

Gunstrings 1 and 2 found to be damaged by fishing gear.  Tming errors and acoustic loss due to cut electrical lines.

22:37	SOL	W00INV1786P1	188	5009	4685	1.0 Port (East)	4.9 µBar	SSE 5kts	2.0 m	059

SP 1873-817: Early EOL d/t CRS/MSX Errors.  Reshot as Seq# 68

08-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

03:34	EOL	W00INV1786P1	188	1868	1874	5.1 Stbd (West)	N/A	ESE 10kts	2.0 m	059

08:24	SOL	W00INV1798P2	188	1756	1659	2.6 Stbd (West)	N/A	E 10kts	2.0 m	060

09:52	EOL	W00INV1798P2	188	807	817	8.8 Port (East)	N/A	Calm	1.0 m	060

14:50	SOL	W00INV1606P3	8	403	1001	6.5 Stbd (East)	3.5 µBar	Sth 5kts	1.5 m	061

21:37	EOL	W00INV1606P3	8	5058	5048	3.3 Port (East)	5.4 µBar	Sth 5 kts	1.5 m	061

23:35	SOL	W00INV1774P1	188	4794	4697	6.0 Stbd (West)	4.4 µBar	Sth 5kts	2.0 m	062

09-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

06:03	EOL	W00INV1774P1	188	807	817	6.3 Stbd (West)	3.2 µBar	SE  5 kts	2.0 m	062

08:15	SOL	W00INV1594P1	8	903	1001	4.9 Stbd (East)	2.5 µBar	SW 10 kts	2.0 m	063

15:07	EOL	W00INV1594P1	8	5070	5060	7.8 Port (West)	3.1 µBar	East 15kts	2.0 m	063

17:06	SOL	W00INV1762P1	188	4806	4709	20 Stbd (West)	4.5 µBar	SE 15-20 kts	2.5 m	064

23:32	EOL	W00INV1762P1	188	807	818	7.0 Port	3.3 µBar	ESE15 kts	2.5 m	064

10-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

02:09	SOL	W00INV1594I1	8	904	1001	3.8 Stbd (East)	4.1 µBar	SSW 20kts	2.0 m	065

08:56	EOL	W00INV1594I1	8	5070	5060	0.8 Port (West)	2.4 µBar	N  15 kts	1.0 m	065

10:52	SOL	W00INV1750P1	188	4819	4721	3.5 Port (East)	2.7 µBar	SSW 15-20kts	2.0 m	066

17:35	EOL	W00INV1750P1	188	807	817	.5Stbd (West)	4.0 µBar	SW15-20kts	.0 m	066

Working on guns

22:16	SOL	W00INV1582P1	8	904	1001	0.0	5.8 µBar	SW 5 kts	2.0 m	067

SP 2501-5072: Early EOL d/t Gun Errors.  Reshot as Seq# 69

11-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:49	EOL	W00INV1582P1	8	2567	2500	6.6 Stbd (East)	2.5 µBar	SW 15 kts	1.0 m	067

04:23	SOL	W00INV1786P2	188	1981	1883	0.0	5.3 µBar	SW 4 kts	2.0 m	068

SP 1199-817: Early EOL d/t Cable Depth Control.  Reshot as Seq# 74

05:33	EOL	W00INV1786P2	188	1127	1200	8.0 Stbd (West)	10.8 µBar	SW 15kts	2.5 m	068

11:45	SOL	W00INV1582P2	8	2393	2491	4.0 Stbd (East)	6.7 µBar	SW 10-15 kts	2-3 m	069

16:03	EOL	W00INV1582P2	8	5082	5072	2.0 Port (West)	8.4 µBar	SW 10 kts	2.0 m	069

18:56	SOL	W00INV1750I1	188	4818	4721	10.0 Stbd (West)	7.1 µBar	SW 10 kts	3.0 m	070

SP 3249-817: Early EOL d/t Cable Depth Control.  Reshot as Seq# 72

21:22	EOL	W00INV1750I1	188	3147	3250	1.5 Stbd (West)	12.1 µBar	SW 10 kts	3.0 m	070

Aborted run-in to line due to excessive swell noise.  Waiting for the weather to improve.

12-February-00

Waiting for the weather to improve.

13-February-00

Waiting for the weather to improve.  Attempting to retrieve cable 2

14-February-00

Waiting for the weather to improve.  Attempting to retrieve cable 2

02:30	Cable 2 and 3 tangle

19:30	Retrieving cables 2 and 3 to untange tail end

15-February-00

03:35	Starboard vane retrieved.  Crack found in float bracket.

10:45	Commence preparation for refuelling at sea

11:42	Fuel line parted under strain.  No fuel being transferred at the time.  Refuelling operation aborted.

14:25	Smit Lloyd alongside (rather than ahead) to reattempt refuelling operation.

17:00	Port vane retrieved and also found to have a cracked float breacket.

17:15	Refuelling at sea completed.

18:40	Vanes repaired.  Deploying cables.

16-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Deploying cables

13:15	All cables deployed.  Deploying guns.

15:00	All guns deployed.

15:14	SOL	W00INV1570P1	8	1847	1850	9.5 Stbd (East)	N/A	SE 5 kts	1.0 m	071

SP 1001-1849: Late SOL d/t Deploying Guns.  Reshot as Seq# 73

20:34	EOL	W00INV1570P1	8	5083	5072	2.5 Port (West)	2.0 µBar	SE 5 kts	1.0 m	071

17-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:43	SOL	W00INV1750I2	188	3356	3259	5.x Stbd (West)	2.4 µBar	072

04:50	EOL	W00INV1750I2	188	807	817	5.3 Port (East)	3.1 µBar	E  5 kts	0.5 m	072

07:01	SOL	W00INV1570P2	8	903	1001	0.0	2.5 µBar	SE  8 kts	1.0 m	073

08:26	EOL	W00INV1570P2	8	1869	1859	4.2 Stbd (East)	2.6 µBar	SE  5 kts	2.0 m	073

11:06	SOL	W00INV1786P3	188	1998	1900	9.5 Stbd (West)	2.0 µBar	Light airs	1.0 m	074

12:52	EOL	W00INV1786P3	188	807	817	1.8 Stbd (West)	1.8 µBar	SW 5 kts	1.0 m	074

15:07	SOL	W00INV1570I1	8	903	1001	5.8 Stbd (West)	2.1 µBar	SE 5 kts	1.0 m	075

21:55	EOL	W00INV1570I1	8	5083	5073	6.3 Port (East)	3.7 µBar	SW 5 kts	1.0 m	075

18-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:14	SOL	W00INV1738P1	188	4830	4733	12.0 Stbd (West)	3.8 µBar	ESE 12kts	1.5 m	076

06:44	EOL	W00INV1738P1	188	807	817	8.8 Port (East)	3.0 µBar	Variable	2.0 m	076

09:07	SOL	W00INV1558P1	8	903	1001	9.0 Stbd (East)	2.4 µBar	SE 5kts	2.0 m	077

SP 2783-5073: Early EOL d/t Gun Errors.  Reshot as Seq# 78

12:08	EOL	W00INV1558P1	8	2913	2782	1.2 Stbd (East)	4.0 µBar	SE 5 kts	1.5 m	077

Working on guns.

16:33	SOL	W00INV1558P2	8	2675	2773	5.0 Stbd (East)	N/A	NE 10 kts	2.0 m	078

20:25	EOL	W00INV1558P2	8	5083	5073	1.3 Stbd (East)	2.3 µBar	NE 10 kts	2.0 m	078

23:06	SOL	W00INV1726P1	188	4842	4745	4.2 Stbd (West)	2.0 µBar	SW 5 kts	2.0 m	079

19-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:37	EOL	W00INV1726P1	188	807	817	12.8 Port(East)	3.6 µBar	SE  5 kts	1.0 m	079

07:54	SOL	W00INV1546P1	8	914	1001	23 Stbd (East)	2.3 µBar	NE 10 kts	1.0 m	080

14:43	EOL	W00INV1546P1	8	5083	5073	2.3 Port (West)	3.5 µBar	Calm	1.5 m	080

17:40	SOL	W00INV1714P1	188	4836	4757	4.2 Port (East)	4.3 µBar	Light 15kts	1.5 m	081

20-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:28	EOL	W00INV1714P1	188	807	817	3.8 Stbd (West)	2.6 µBar	Light Air	1.5 m	081

02:42	SOL	W00INV1534P1	8	903	1001	3.8 Port (West)	3.4 µBar	Light kts	1.0 m	082

09:38	EOL	W00INV1534P1	8	5083	5073	2.7 Stbd (East)	2.5 µBar	ESE 10kts	1.5 m	082

11:47	SOL	W00INV1714I1	1880	2.3 Stbd (West)	2.7 µBar	SE 10kts	1.0 m	083

Line rejected d/t weather.  Reshot as Seq# 86

12:06	EOL	W00INV1714I1	1880	2.5 Stbd (West)	3.6 µBar	SE 10 kts	1.0 m	083

13:08	Retrieving gear prior to heading to port

21-February-00

02:15	All gear retrieved and hull transducer raised.  Heading for Portland, Victoria.

12:35	Pilot onboard

13:20	Alongside Portland

22-February-00

Alongside Portland.

Both vane wires replaced with thicker wire

Crew Change

23-February-00

01:10	Depart Portland

07:30	Deploying cables

18:00	Port vane sinks on deployment.

19:30	Vane retrieved, severely damaged after collison with sea floor.  Picking up cables

22:30	All gear retrieved and hull transducer raised.  Heading for Portland, Victoria.

24-February-00

08:00	Alongside Portland

Replacing port vane with spare.

18:23	Depart Portland

23:15	Deploying cables

25-February-00

Deploying cables.  Some delays due to rough seas and cable maintainance

26-February-00

Deploying cables.  Some delays due to rough seas and cable maintainance

27-February-00

Deploying cables.  Some delays due to rough seas and cable maintainance

21:55	All cables deployed.  Deploying guns.

28-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

04:30	Guns deployed

06:59	SOL	W00INV1534I1	8	904	1001	3.4 Port (West)	9.6 µBar	SW 10 kts	2.5 m	084

Line rejected d/t CRS problems and telemtry errors.  Reshot as Seq# 97

13:57	EOL	W00INV1534I1	8	5083	5073	0.0	11.0 µBar	SSE 10-15 kts	1.5-2 m	084

16:57	Retriveing guns

18:10	Guns onboard, retrieving cable 6 to fix telemetry errors

29-February-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

19:20	Cable 6 repaired and deployed.  Deploying guns.

21:35	Guns deployed

23:32	SOL	W00INV1522P1	8	903	1001	5.8 Port (West)	7.2 µBar	NE 20 kts	2.0 m	085

01-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

06:33	EOL	W00INV1522P1	8	5083	5073	0.6 Stbd (East)	3.5 µBar	SSE 12 kts	2.0 m	085

09:20	SOL	W00INV1714I2	188	4855	4757	7.0 Stbd (West)	5.5 µBar	SE 5  kts	1.5m	086

15:56	EOL	W00INV1714I2	188	807	817	1.7 Port (East)	2.9 µBar	E 10 kts	1.0 m	086

18:14	SOL	W00INV1510P1	8	904	1001	0.8 Stbd (East)	3.1 µBar	ESE 12-15 kts	1.5-2 m	087

02-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:11	EOL	W00INV1510P1	8	5083	5073	2.6 Port (West)	4.4 µBar	ESE 10 kts	1.5 m	087

03:39	SOL	W00INV1702P1	188	4864	4768	5.5 Port (East)	2.9 µBar	ESE 10kts	1.5 m	088

10:06	EOL	W00INV1702P1	188	807	817	2.2 Stbd (West)	2.1 µBar	N 12 kts	1.5 m	088

13:23	SOL	W00INV1678P1	8	904	1001	2.5 Stbd (East)	2.6 µBar	NNW 10 kts	0.5-1 m	089

19:54	EOL	W00INV1678P1	8	4986	4976	1.6 Stbd (East)	2.1 µBar	Light airs	Rippled	089

22:59	SOL	W00INV1498P1	188	4987	4889	5.8 Stbd (West)	1.9 µBar	Calm	Calm	090

03-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:49	EOL	W00INV1498P1	188	807	817	1.5 Port (East)	1.9 µBar	Calm	0.5 m	090

08:15	SOL	W00INV1690P1	8	904	1001	0.7 Port (West)	1.7 µBar	SW 8 kts	1.0 m	091

15:02	EOL	W00INV1690P1	8	4974	4964	6.0 Port (West)	11.5 µBar	SW 10-15 kts	2.5-3 m	091

18:38	SOL	W00INV1606I1	188	3927	3830	3.2 Port (East)	12.7 µBar	SW 15 kts	3.0 m	092

SP 1883-1346: Cable 3 : CH 1-368 Cable Depth Control.  No reshoot required

04-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:04	EOL	W00INV1606I1	188	807	817	4.0 Stbd (West)	10.2 µBar	SW 25 kts	3.0 m	092

03:05	Line 1534I2 aborted during run-in d/t cable inbalance in rough seas.  Sequence scratched.  No seismic data recorded.

Waiting for the weather to improve.

13:46	SOL	W00INV1702I1	1880	3.0 Stbd (West)	13.7 µBar	SW 10-12 kts	3.0 m	093

Line rejected d/t weather.  Reshot as Seq# 94

14:24	EOL	W00INV1702I1	1880	4.3 Stbd (West)	N/A	SW 10-12 kts	3.0 m	093

22:10	SOL	W00INV1702I2	188	4865	4768	2.3 Stbd (West)	11.3 µBar	SW 10 kts	3-3.5 m	094

22:10	EOL	W00INV1702I2	188	807	817	2.6 Port (East)	16.6 µBar	SW 12 kts	3.0 m	094

05-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

07:46	SOL	W00INV1798I1	8	904	1001	1.4 Stbd (East)	10.3 µBar	SW 10 kts	3.0 m	095

13:40	EOL	W00INV1798I1	8	4550	4530	0.4 Stbd (East)	5.8 µBar	SW 10 kts	2.0 m	095

17:35	SOL	W00INV1846I3	188	3767	0	2.6 Port (East)	15.1 µBar	SSW 12 kts	3.0 m	096

Line rejected d/t weather.  Reshot as Seq# 103

21:52	EOL	W00INV1846I3	188	1141	0	0.2 Stbd (West)	16.3 µBar	S 20 kts	3-3.5 m	096

06-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:30	SOL	W00INV1534I2	8	904	0	5.2 Port (West)	13.0 µBar	S 20-25 kts	3.0 m	097

Line rejected d/t weather.  Reshot as Seq# 98

08:24	EOL	W00INV1534I2	8	5083	0	8.0 Stbd (East)	22.0 µBar	SE 20 kts	3.5 m	097

Guns retrieved and waiting for the weather to improve.

07-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Waiting for the weather to improve.

Guns deployed

22:42	SOL	W00INV1534I3	8	904	1001	3.7 Stbd (East)	10.0 µBar	ESE 25 kts	3.0 m	098

SP 2932-5073: Early EOL d/t Gun Errors.  Reshot as Seq# 99

08-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:58	EOL	W00INV1534I3	8	3001	2931	5.5 Port (West)	N/A	ESE 25 kts	3.0 m	098

Working on guns

06:43	SOL	W00INV1534I4	80	5.3 Port (West)	13.2 µBar	SE 25 kts	3.0 m	099

Line rejected d/t weather.  Reshot as Seq# 102

10:15	EOL	W00INV1534I4	80	3.6 Port (West)	12.5 µBar	ESE 25 kts	3.0 m	099

14:16	SOL	W00INV1690I1	188	4878	4780	9.2 Stbd (West)	8.9 µBar	SSE 25-30 kts	2.5-3 m	100

SP 2519-1661: Coverage not required.  No reshoot required

20:53	EOL	W00INV1690I1	188	807	817	3.3 Port (East)	N/A	E 25 kts	3.0 m	100

09-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:05	SOL	W00INV1522I1	80	4.0 Port (West)	N/A	ESE 30 kts	4.0 m	101

Line rejected d/t weather.  Reshot as Seq# 106

00:27	EOL	W00INV1522I1	80	7.6 Port (West)	N/A	ESE 40 kts	4.0 m	101

09:51	SOL	W00INV1534I5	80	1.3 Stbd (East)	14.0 µBar	E 30 kts	2.5 m	102

Line rejected d/t weather.  Reshot as Seq# 107

13:25	EOL	W00INV1534I5	80	3.9 Port (West)	8.0 µBar	ENE 20-25 kts	2.0 m	102

17:28	SOL	W00INV1846I4	188	3777	3680	13.6 Stbd (West	6.2 µBar	E 26 kts	2.0 m	103

SP 1230-1214: Gun Errors (Even Shots Only).  No reshoot required

SP 1729-1355: Coverage not required.  No reshoot required

21:41	EOL	W00INV1846I4	188	1141	1151	1.3 Port (East)	3.3 µBar	E 25-30 kts	2.5 m	103

10-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

04:06	SOL	W00INV1738I1	8	904	1001	4.0 Port (West)	2.4 µBar	E 25 kts	2.0 m	104

SP 1001-4917: Cable 4 : CH 1-368 Telemetry Errors (Selected shots).  No reshoot required

10:51	EOL	W00INV1738I1	8	4927	4917	1.0 Port (West)	2.6 µBar	NE 5 kts	1.0 m	104

14:31	SOL	W00INV1822I1	188	4698	4600	1.6 Port (East)	2.8 µBar	Light airs	Calm	105

SP 2359-1701: Coverage not required.  No reshoot required

SP 2438-2360: Vessel movement too great.  No reshoot required

SP 3234-2621: Coverage not required.  No reshoot required

SP 4600-768: Cable 4 : CH 1-368 Telemetry Errors (Selected shots).  No reshoot required

21:08	EOL	W00INV1822I1	188	758	768	0.0	1.9 µBar	Light airs	Calm	105

23:45	SOL	W00INV1522I2	8	1402	1500	0.0	1.5 µBar	Light airs	0.5 m	106

SP 1500-5073: Cable 4 : CH 1-368 Telemetry Errors (Selected shots).  No reshoot required

11-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:54	EOL	W00INV1522I2	8	5083	5073	9.0 Port (West)	2.4 µBar	Light Airs	0.5 m	106

09:09	SOL	W00INV1534I6	188	4986	4889	1.0 Stbd (West)	1.9 µBar	Variable	1.0 m	107

SP 4889-817: Cable 4 : CH 1-368 Telemetry Errors (Selected shots).  No reshoot required

16:43	EOL	W00INV1534I6	188	807	817	8.4 Stbd (West)	1.6 µBar	Light air	Rippled	107

20:07	SOL	W00INV1642I1	8	1042	1140	7.3 Port (West)	2.8 µBar	SSW 3-5 kts	Rippled	108

SP 3176-3495: Coverage not required.  No reshoot required

12-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:13	EOL	W00INV1642I1	8	4141	4130	3.4 Port (West)	2.3 µBar	S 8 kts	0.5 m	108

04:44	SOL	W00INV1570I2	188	3083	3030	10.3 Stbd (West	2.6 µBar	ESE 10 kts	1.0 m	109

SP 1565-1191: Coverage not required.  No reshoot required

08:24	EOL	W00INV1570I2	188	807	817	8.0 Stbd (West	7.5 µBar	SSE 18 Kts	2.0 m	109

13:40	SOL	W00INV1690I2	80	7.3 Stbd (West)	14.7 µBar	S 15-18 kts	2.0 m	110

Line rejected d/t weather.  Reshot as Seq# 111

16:43	EOL	W00INV1690I2	80	6.0 Port (West)	18.0 µBar	E 25-30 kts	3.0 m	110

Line aborted on run-in due to weather.  Guns retrieved  Waiting for the weather to improve.

13-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Waiting for the weather to improve.

Guns deployed

21:58	SOL	W00INV1690I3	8	3083	3180	3.0 Port (West)	3.1 µBar	W 25 kts	2.0 m	111

14-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:51	EOL	W00INV1690I3	8	4974	4964	9.7 Stbd (East)	2.5 µBar	W 20 kts	2.0 m	111

04:37	SOL	W00INV1846I5	188	3811	3714	1.0 Stbd (West)	3.5 µBar	SW 20-30 kts	3.0 m	112

07:09	EOL	W00INV1846I5	188	2289	2300	1.3 Stbd (West)	7.6 µBar	SW 25 kts	3.0 m	112

11:59	SOL	W00INV1330P1	8	904	1001	1.8 Port (West)	8.1 µBar	WSW 25 kts	3.5 m	113

18:45	EOL	W00INV1330P1	8	5083	5073	2.3 Port (West)	5.0 µBar	SW 15 kts	3.5 m	113

21:51	SOL	W00INV1486P1	1880	2.1 Stbd (West)	9.3 µBar	SW 15 kts	4.0 m	114

Line rejected d/t weather.  Reshot as Seq# 116

22:11	EOL	W00INV1486P1	1880	3.0 Stbd (West)	N/A	SW 15 kts	4.0 m	114

Trying for line in opposite direction

15-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

08:32	SOL	W00INV1318P1	8	904	1001	1.0 Port (West)	9.1 µBar	SSW 8 kts	3.5 m	115

15:20	EOL	W00INV1318P1	8	5083	5073	6.9 Stbd (East)	11.1 µBar	SW 10 kts	2.5 m	115

18:55	SOL	W00INV1486P2	188	4986	4889	0.0	10.9 µBar	SW 12 kts	3.0 m	116

16-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:45	EOL	W00INV1486P2	188	807	817	6.0 Port (East)	3.5 µBar	L/A kts	2.5 m	116

05:06	SOL	W00INV1306P1	8	904	1001	4.2 Stbd (East)	3.7 µBar	Light Airs	0.5 m	117

11:55	EOL	W00INV1306P1	8	5083	5073	1.0 Stbd (East)	4.6 µBar	Light Airs	2.0 m	117

15:24	SOL	W00INV1486I1	188	4986	4889	6.0 Port (East)	7.0 µBar	SE 12 kts	2.5 m	118

22:20	EOL	W00INV1486I1	188	807	817	8.6 Stbd (West)	4.7 µBar	SSE 10 kts	3.0 m	118

17-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

02:00	SOL	W00INV1294P1	8	904	1001	1.9 Stbd (East)	4.2 µBar	NE 15 kts	2.0 m	119

09:04	EOL	W00INV1294P1	8	5083	5073	4.0 Port (West)	3.9 µBar	NE 15 kts	3.0 m	119

12:17	SOL	W00INV1474P1	188	4987	4889	4.1 Stbd (West)	5.0 µBar	NE 8 kts	2.5 m	120

SP 2480-2320: Cable 5 : CH 209-368 Cable tail on surface.  Replacing bird.  No reshoot required

19:07	EOL	W00INV1474P1	188	807	817	0.7 Stbd (West)	3.3 µBar	NE 12-15 kts	2.5-3 m	120

21:36	SOL	W00INV1282P1	8	904	1001	2.7 Stbd (East)	3.3 µBar	NE 18 kts	2.5 m	121

18-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

04:56	EOL	W00INV1282P1	8	5083	5073	5.0 Stbd (West)	4.0 µBar	NW 33 kts	2.5 m	121

07:29	SOL	W00INV1462P1	188	4987	4889	3.9 Port (East)	4.5 µBar	WNW 30 kts	2.0 m	122

14:29	EOL	W00INV1462P1	188	807	817	0.7 Stbd (West)	5.5 µBar	SW 15-20 kts	2.5 m	122

17:18	SOL	W00INV1270P1	8	903	1001	0.3 Port (West)	5.6 µBar	WSW 18 kts	2.5 m	123

19-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:08	EOL	W00INV1270P1	8	5083	5073	7.4 Port (West)	6.2 µBar	SW 10 kts	2.5 m	123

03:31	SOL	W00INV1462I1	188	4987	4889	2.2 Port (East)	8.0 µBar	SW 12 kts	2.5 m	124

10:33	EOL	W00INV1462I1	188	807	817	1.9 Stbd (West)	8.1 µBar	Variable	3.0 m	124

14:07	SOL	W00INV1270I1	8	904	1001	4.0 Port (West)	5.8 µBar	SW 15 kts	2.5-3 m	125

20:52	EOL	W00INV1270I1	8	5083	5073	2.1 Stbd (East)	2.8 µBar	SW 10-12 kts	2.5 m	125

23:40	SOL	W00INV1450P1	188	4987	4889	0.7 Stbd (West)	4.6 µBar	SW 10-12 kts	2.5 m	126

20-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

06:44	EOL	W00INV1450P1	188	807	817	1.1 Port (East)	5.0 µBar	SW 15 kts	2.0 m	126

10:21	SOL	W00INV1258P1	8	904	1001	1.4 Stbd (East)	10.0 µBar	SW 20 kts	3.0 m	127

17:02	EOL	W00INV1258P1	8	5083	5073	2.0 Port (West)	6.6 µBar	SSW 15 kts	2.0 m	127

19:57	SOL	W00INV1438P1	1884889	2.6 Port (East)	9.7 µBar	SSW 15 kts	3-4 m	128

Line rejected d/t weather.  Reshot as Seq# 130

22:06	EOL	W00INV1438P1	1883656	1.4 Port (East)	N/A	SE 20 kts	4.0 m	128

Trying for line in opposite direction

21-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:58	SOL	W00INV1246P1	8	903	1001	1.8 Port (West)	11.9 µBar	SE 18 kts	4.0 m	129

12:43	EOL	W00INV1246P1	8	5083	5073	1.1 Port (West)	10.1 µBar	SSE 12 kts	3.0 m	129

16:02	SOL	W00INV1438P2	188	4986	4889	7.0 Stbd (West)	8.7 µBar	SW 25 kts	3.5 m	130

22:49	EOL	W00INV1438P2	188	807	817	1.5 Port (East)	4.3 µBar	E 25 kts	3.0 m	130

22-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:56	SOL	W00INV1234P1	8	904	1001	4.7 Stbd (East)	4.2 µBar	ENE 25 kts	3.0 m	131

SP 1407-1428, 2664-2669, 2704-2708, 2734-2736, 2783-2784: Cable 5 power tripped out.  No reshoot required

08:56	EOL	W00INV1234P1	8	5083	5073	3.7 Stbd (East)	3.6 µBar	NE 20 kts	3.0 m	131

11:26	SOL	W00INV1426P1	188	4986	4889	2.4 Port (East)	2.7 µBar	N 20 kts	2.5 m	132

18:20	EOL	W00INV1426P1	188	807	817	3.0 Port (East)	2.9 µBar	W 28-30 kts	2.0 m	132

Line aborted on run-in due to weather.  Guns retrieved  Waiting for the weather to improve.

23-March-00

Waiting for the weather to improve.

24-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Waiting for the weather to improve.

06:05	Guns deployed

07:13	SOL	W00INV1222P1	8	904	1001	3.5 Stbd (East)	8.4 µBar	ESE 12 kts	3.0 m	133

13:57	EOL	W00INV1222P1	8	5083	5073	0.0	9.0 µBar	E 10-15 kts	3.5 m	133

18:20	SOL	W00INV1414P1	188	4986	4889	10.0 Stbd (West	4.8 µBar	SE 15-18 kts	2.5 m	134

25-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:02	EOL	W00INV1414P1	188	807	817	4.1 Port (East)	8.5 µBar	SE 18 kts	2.5 m	134

04:11	SOL	W00INV1210P1	8	904	1001	7.9 Stbd (East)	4.8 µBar	SE 10 kts	2.5 m	135

11:12	EOL	W00INV1210P1	8	5083	5073	1.5 Stbd (East)	6.3 µBar	E 8 kts	2.0 m	135

13:38	SOL	W00INV1414I1	188	4986	4889	3.3 Port (East)	7.4 µBar	Light airs	3.0 m	136

20:32	EOL	W00INV1414I1	188	807	817	0.8 Port (East)	2.9 µBar	E 10 kts	2.5 m	136

23:25	SOL	W00INV1198P1	8	904	1001	10.5 Stbd (East	2.8 µBar	SE 10 kts	2.5 m	137

26-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

06:16	EOL	W00INV1198P1	8	5083	5073	6.2 Port (West)	6.8 µBar	Variable	2.0 m	137

08:46	SOL	W00INV1402P1	188	4986	4889	5.6 Stbd (West)	5.0 µBar	Variable	2.0 m	138

15:48	EOL	W00INV1402P1	188	807	817	0.7 Port (East)	4.6 µBar	S 5-10 kts	2.5-3 m	138

18:20	SOL	W00INV1198I1	8	904	1001	3.3 Stbd (East)	5.5 µBar	Var 7-8 kts	2.0 m	139

27-March-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:09	EOL	W00INV1198I1	8	5083	5073	2.3 Stbd (East)	4.7 µBar	E 12-15 kts	2-2.5 m	139

03:36	SOL	W00INV1390P1	188	4986	4889	0.2 Port (East)	4.2 µBar	Calm	2.5 m	140

10:33	EOL	W00INV1390P1	188	807	817	6.8 Port (East)	4.3 µBar	SW 12 kts	3.0 m	140

13:14	SOL	W00INV1186P1	8	903	1001	5.6 Stbd (East)	3.6 µBar	SW 18 kts	3.5 m	141

20:02	EOL	W00INV1186P1	8	5083	5073	5.0 Port (West)	4.1 µBar	SW 10 kts	2.5 m	141

22:02	Retrieving gear prior to heading to port

28-March-00

21:55	All gear retrieved and hull transducer raised.  Heading for Portland, Victoria.

29-March-00

06:30	Pilot onboard

07:05	Alongside Portland

Crew Change

23:00	Depart Portland

30-March-00

03:00	Deploying cables

31-March-00

11:35	All cables deployed.  Waiting for the weather to improve before deploying guns

18:00	Deploying guns

20:00	All guns deployed

01-April-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

01:48	SOL	W00INV1342P1	8	904	1001	0.7 Stbd (West)	32.6 µBar	SW 25 kts	3.0 m	142

08:26	EOL	W00INV1342P1	8	5083	5073	0.3 Stbd (West)	19.8 µBar	SW 25 kts	3.0 m	142

12:09	SOL	W00INV1378P1	188	4987	4889	3.4 Stbd (West)	14.4 µBar	SSW 12 kts	3.0 m	143

18:59	EOL	W00INV1378P1	188	807	817	2.0 Port (East)	16.1 µBar	SSW 10 kts	3.0 m	143

02-April-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

05:37	SOL	W00INV1354P1	8	904	1001	2.0 Stbd (East)	14.2 µBar	SSW 10 kts	3.0 m	144

05:36	EOL	W00INV1354P1	8	5083	5073	1.2 Stbd(East)	9.1 µBar	S 10 kts	2.0 m	144

09:32	SOL	W00INV1366P1	188	4987	4889	0.2 Stbd (West)	6.2 µBar	S 5 kts	2.0 m	145

16:12	EOL	W00INV1366P1	188	807	817	0.8 Port (East)	13.5 µBar	S 0 kts	0.5 m	145

19:46	SOL	W00INV1366I1	8	903	1001	2.3 Stbd (East)	10.9 µBar	S 5 kts	1.0 m	146

03-April-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

02:41	EOL	W00INV1366I1	8	5083	5073	3.8 Port (West)	4.6 µBar	S 5 kts	1.0 m	146

06:30	SOL	W00INV1342I1	188	4987	4889	2.6 Port (East)	2.7 µBar	S 5 kts	1.0 m	147

11:42	EOL	W00INV1342I1	188	1754	1770	5.9 Stbd (West)	3.4 µBar	S 5 kts	1.0 m	147

3D Acquisition completed

## INVESTIGATOR 2D LINES SEQ 148-152

03-April-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

Investigator 2D acquisition commences

12:24	SOL	W00INV0006P1	112	1001	0	1.8 Stbd (West)	4.9 µBar	W 20 kts	2.0m	148

Line rejected d/t incrrect record length in CRS.  Reshot as Seq# 151

16:51	EOL	W00INV0006P1	112	2483	0	4.2 Stbd (East)	2.6 µBar	W 20 kts	2.0 m	148

Retrieving guns

19:40	Guns onboard.  Start retrieving cables 2-6

04-April-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

07:00	Only cable 1 remaining in water.  Deploying guns

09:50	All guns deployed

14:33	SOL	W00INV0004P1	10	 951	1001	1.1 Port (East)	N/A µBar	S 10 kts	2.0 m	149

Line shutdown once the boundary of block T/30P was reached.

18:58	EOL	W00INV0004P1	10	2518	2508	1.0 Port (East)	N/A µBar	S 10 kts	2.0 m	149

22:01	SOL	W00INV0007P1	188	1898	1801	3.0 Stbd (West)	N/A µBar	SE 25 kts	2.5 m	150

05-April-00

Time		Line name	Dir	Nav SP	Good SP	Feather	Noise	Wind	Sea	Seq #

00:36	EOL	W00INV0007P1	188	 899	909	3.9 Stbd (West)	N/A µBar	SE 25 kts	2.5 m	150

05:39	SOL	W00INV0006P2	291	2427	2386	N/A	N/A µBar	S 15-20 kts	2.0 m	151

Early EOL d/t fishing gear on line.

09:10	EOL	W00INV0006P2	291	 899	1114	3.9 Stbd (West)	N/A µBar	SSE 25 kts	1.5 m	151

12:42	SOL	W00INV0005P1	142	2415	2415	3.8 Stbd (West)	N/A µBar	SE 25 kts	3.0 m	152

Early EOL d/t deteriorating weather.

14:41	EOL	W00INV0005P1	142	1775	1820	5.4 Stbd (West)	N/A µBar	S 30 kts	3.5 m	152

2D Acquisition completed