DRILLING / WELLWORK REPORT 24HRS TO 0500 HRS July 12, 2006

SAFETY:

DAYS SINCE LAST TRI:	PREVIOUS BEST TRI PERIOD

| RIG 453 | 255 | 363 |
| --- | --- | --- |
| CAMERON | 5507 | 5525 |
| HALLIBURTON | 3329 | 3328 |
| SCHLUMBERGER | 2109 | 2108 |
| ISDL | 255 | 647 |
| ISS | 44 | 2350 |

Well: WKF_W31A

Rig/Contractor: 	Rig 453	Report Date: July 12, 2006

Supervisor:.	Campbell, Glenn R.

Steed, Cory

| AFE Number: | L0501G655 | Ave Angle: |  |
| --- | --- | --- | --- |
| Days to Complete: | 1.3 | AFE Cost/Days: | $7,100,000 |
| Daily Cost: | $249,434 |  |  |
| Total Cost: | $4,734,392 | Planned MD/TVD: | 3438.00/2363.00 |
| Casing Size: |  | Actual MD/TVD: | 2794.00/1942.36 |
| Mud Weight: |  | Tubing Size: |  |

| Objective: | WKF_W31A |
| --- | --- |
| Management Summary: | C/out LPR's to 4" solids. R/d Schlumberger. Pressure test BOP's, choke & standpipe manifolds, TDS & stabbing valves to 300/3000 psi. M/U 7" casing scraper assembly & RIH to 3069m. Held power choke, H2S & trip drills. |
| Current: | RIH w/ casing scraper at 3069m. |
| Planned: | WOW. RIH w/ scraper to TD. POOH. R/U & run MAXR guns. POOH & R/dn WL. |