| WELL | WKF W-19A |
| --- | --- |
| DATE | 07-06-2006 |
| DAY # | 7 |
| MIDNIGHT ACTIVITY | Pulling out of hole for logging. |  | ROP DATA (LAST 24 hours) | m/hr | DEPTH (m) |
| MIDNIGHT DEPTH | 2687.0 mMDRT |  | MINIMUM | 12.3 | 2471.0 |
| TVD | 2373.4 mTVDRT |  | MAXIMUM | 126.3 | 2683.0 |
| PROGRESS LAST 24 hrs | 428.0 m |  | AVERAGE | 48.6 | 2259.0-2687.0 |

|  | TOP (mMDRT) | TOP (mTVDRT) | TOP (mTVDSS) RTtoMSL (33.4m) | HIGH/ LOW (mTVD) | PROGNOSED TOP (mMDRT) | PROGNOSED TOP (mTVDRT) |
| --- | --- | --- | --- | --- | --- | --- |
| Base of MIocene | 1681.5 | 1496.9 | -1463.5 |  |  |  |
| Lakes Entrance | 2229.5 | 1973.1 | -1939.7 | 0.3 HIGH | 2229.0 | 1973.4 |
| Top of Latrobe | 2563.0 | 2263.2 | -2229.8 | 4.2 HIGH | 2570.9 | 2267.4 |
| M1.2UMD | 2592.5 | 2289.5 | -2256.1 | 5.9 HIGH | 2603.3 | 2295.4 |
| M1.2L Top | 2598.5 | 2294.8 | -2261.4 | 5.6 HIGH | 2609.1 | 2300.4 |
| PSB7 (Top of M1.3U) | 2612.0 | 2306.8 | -2273.4 | 5.6 HIGH | 2623.0 | 2312.4 |
| PSB6 (Top of PS5 sand) | 2616.0 | 2310.3 | -2276.9 | 4.1 HIGH | 2625.4 | 2314.4 |
| PSB5 (Top of PS4 sand) | 2620.0 | 2313.9 | -2280.5 | 4.5 HIGH | 2630.0 | 2318.4 |
| PSB4 (Top of PS3 sand) | 2632.0 | 2324.5 | -2291.1 | 4.9 HIGH | 2642.8 | 2329.4 |
| PSB3 (Top of PS2 sand) | 2642.0 | 2333.4 | -2300.0 | 3.0 HIGH | 2650.9 | 2336.4 |
| Top of M1.4 U | 2662.0 | 2351.1 | -2317.7 | 2.3 HIGH | 2670.6 | 2353.4 |
| M1.4C (Coal) | 2667.0 | 2355.6 | -2322.2 | 1.8 HIGH | 2675.2 | 2357.4 |
| Total Depth | 2687.0 | 2373.4 | -2340.0 | 10.0 LOW | 2682.2 | 2363.4 |

| Current Formation | LATROBE: 20% CLAYSTONE, 15% SILTSTONE, 65% SANDSTONE. |
| --- | --- |

| GAS DATA | DEPTH (m) | TOTAL GAS (U) | C1 % | C2 % | C3 % | iC4 % | nC4 % | C5 % |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| MAX (FCP/FGP) | 2634.5 | 278.0 | 0.933 | 0.216 | 0.327 | 0.159 | 0.243 | 0.192 |
| MAX (Reserval) | 2638.5 | 499.0 | 1.730 | 0.558 | 0.875 | 0.337 | 0.488 | 0.362 |
| BG (FCP/FGP) | 2259.0-2687.0 | 7.0 | 0.01 | 0.008 | 0.005 | 0.001 |  |  |
| BG (Reserval) | 2259.0-2687.0 | 17.0 | 0.21 | 0.023 | 0.002 | 0.001 |  |  |
| TRIP GAS (FCP) |  |  |  |  |  |  |  |  |
| TRIP GAS Reserval) |  |  |  |  |  |  |  |  |

| BIT DATA | PRESENT BIT | LAST BIT |
| --- | --- | --- |
| BIT No. | 1 |  |
| SIZE (in) | 8½ |  |
| MANUFACTURER/TYPE | Smith S73PX |  |
| JETS (/32 inch) | 6 x 20 |  |
| DEPTH IN (m) | 666.0 |  |
| DEPTH OUT (m) | IN HOLE |  |
| METRES ON RUN (m) | 2021.0 |  |
| HRS ON BTM 24hrs/total | 8.8 / 47.4 |  |
| BIT CONDITION |  |  |
| RPM RANGE LAST 24 hrs | TDRPM: 0-120 MMRPM: 176-180 |  |
| Pump Hrs 24 hrs / total | 19.0 / 94.1 |  |
| Krevs 24 hrs / total | 149 / 745 |  |
| 24 HOUR SUMMARY | Drill, steer and survey 8½" production hole from 2259.0 mMDRT to 2593.0 mMDRT. Rotate, work string and circulate at reduced pump rate whilst replacing swab in mud pump #1. Drill, steer and survey 8½" production hole from 2593.0 mMDRT to 2687.0 mMDRT. Reached T.D. of 2687.0 mMDRT at 20:00 hrs. Circulate 3x bottoms up until hole clean whilst rack back 1 std / 1/2hr from 2687.0 mMDRT to 2584.0 mMDRT. |
| 05:00 AM UPDATE 08-06-2006 DEPTH @ 05:00 hours | Pull out of hole for logging from 2584.0 mMDRT to 1047.0 mMDRT . Working minor tight spots at 1590.0 mMDRT, 1400.0 mMDRT, 1250.0 mMDRT. 2687.0 mMDRT (2373.41 mTVDRT) |