| Depth m/hr | Lith % | Glenaire-1A (Sidetrack) 152mm hole. Glenaire-1 was plugged back from 3306m (T.D.) to 3041m for sidetrack due to excessive deviation. | TG u % |
| --- | --- | --- | --- |
| 3045 (3) | 100 | Cement. | 6 (80:6:5:4:5) |
| 3048 (2.5) | 100 | Cement. | 8 (80:6:5:4:5) |
| 3051 (1.5) | 100 | Cement. | 8 (80:6:5:4:5) |
| 3054 (11) | 100 | Cement. | 11 (80:6:5:4:5) |
| 3057 (20) | 100 | Cement. | 14 (80:6:5:4:5) |
| 3060 (5) | 100 | Cement. | 15 (82:7:5:2:3) |
| 3063 (0.6) | 100 Trace | Cement. SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. | 8 (82:7:5:2:3) (82:7:5:2:3) |
| 3066 (0.7) | Trace 60 40 | Cement. SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 5 (82:7:5:2:3) |
| 3069 (1.1) | 30 70 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1 (82:7:5:2:3) |
| 3072 (1.6) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (82:8:5:5:tr) |
| 3075 (1.2) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3.0 (82:8:5:5:tr) |
| 3078 (2.1) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.2 (84:8:6:2:tr) |
| 3081 (2.3) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (84:8:6:2:tr) |
| 3084 (2.4) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 17.5 (83:9:5:2:1) |
| 3087 (2.9) | 100 | SILTY CLAYSTONE, as above. | 10.9 (83:9:5:2:1) |
| 3090 (3.1) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 14.1 (83:9:5:2:1) |
| 3093 (3.2) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 14.6 (83:9:5:2:1) |
| 3096 (3.0) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 19.2 (85:8:4:2:1) |
| 3099 (2.5) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common black coal detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 28 (85:8:4:2:1) |
| 3102 (2.3) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 16.7 (85:8:4:2:1) |
| 3105 (2.8) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 10.5 (85:7:5:3:tr) |
| 3108 (3.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 5.2 (85:7:5:3:tr) |
| 3111 (3.0) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to occasionally fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 5.4 (80:8:5:4:3) |
| 3114 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.6 (80:8:5:4:3) |
| 3117 (2.2) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 5.3 (82:8:7:3:tr) |
| 3120 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4.0 (82:8:7:3:tr) |
| 3123 (2.8) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 56 (82:8:6:3:1) |
| 3126 (3.1) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 881 (80:9:8:2:1) |
| 3129 (3.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 75 (80:9:8:2:1) |
| 3132 (3.5) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 42 (80:9:8:2:1) |
| 3135 (3.2) | 100 | SILTY CLAYSTONE, as above. | 26 (80:9:8:2:1) |
| 3138 (3.0) | 100 | SILTY CLAYSTONE, as above. | 7 (81:8:6:3:2) |
| 3141 (2.7) | 100 | SILTY CLAYSTONE, as above. | 5 (81:8:6:3:2) |
| 3144 (2.5) | 100 | SILTY CLAYSTONE, as above. | 20 (84:7:5:3:tr) |
| 3147 (2.6) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 46 (84:7:5:3:tr) |
| 3150 (2.5) | 30 70 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 235 (80:8:7:3:2) |
| 3153 (2.5) | 80 20 Trace Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, very carbonaceous in part – grades to coal, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. COAL, black, subvitreous to vitreous, subconchoidal fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 2538 (77:9:8:4:2) |
| 3156 (2.2) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 1320 (75:9:9:5:2) |
| 3159 (2.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 209 (75:9:9:5:2) |
| 3162 (2.1) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 163 (75:9:8:5:3) |
| 3165 (2.5) | 100 | SILTY CLAYSTONE, as above. | 948 (76:9:8:5:2) |
| 3168 (3.0) | 100 | SILTY CLAYSTONE, as above. | 73 (76:9:8:5:2) |
| 3171 (2.5) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, trace calcite lined fractures, hard, no visual porosity, no oil fluorescence. | 84 (76:9:8:5:2) |
| 3174 (2.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 101 (81:8:6:3:2) |
| 3177 (1.8) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 40 (81:8:6:3:2) |
| 3180 (2.0) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 330 (80:9:6:3:2) |
| 3183 (2.4) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 74 (80:9:6:3:2) |
| 3186 (22) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 81 (80:9:6:3:2) |
| 3189 (24) | 70 30 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 194 (80:9:6:3:2) |
| 3192 (40) | 40 30 30 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, very carbonaceous in part, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace fine black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular/contused fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. Well flowing oil/gas cut mud – probably from fractures associated with the sand/coal. Crude is green, waxy, on the heavier end of a light crude, Gives a bright pale greenish yellow white fluorescence with a milky white cut. | 159 (61:12:13:9:5) |
| 3195 (26) | 70 30 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to occasionally fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4561 (61:12:13:9:5) |
| 3198 (28) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3519 (61:12:13:9:5) |
| 3201 (28) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3199 (61:12:13:9:5) |
| 3204 (35) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 2248 (61:12:13:9:5) |
| 3207 (33) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 780 (61:12:13:9:5) |
| 3210 (21) | 100 | SILTY CLAYSTONE, as above. | 877 (77:8:6:5:4) |
| 3213 (24) | 100 | SILTY CLAYSTONE, as above. | 542 (77:8:6:5:4) |
| 3216 (27) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and coaly detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4056 (60:12:15:9:4) |
| 3219 (22) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 2003 (60:12:15:9:4) |
| 3222 (18) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 220 (60:12:15:9:4) |
| 3225 (3.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 290 (57:11:14:11:7) |
| 3228 (6.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 3131 (59:11:14:10:6) |
| 3231 (16) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 180 (83:7:5:2:3) |
| 3234 (18) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 453 (79:8:6:4:3) |
| 3237 (19) | 60 10 30 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, very carbonaceous in part – grades to coal, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular to blocky fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 1503 (79:8:6:4:3) |
| 3240 (11) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 173 (79:8:6:4:3) |
| 3243 (8.0) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 123 (85:6:3:8:3) |
| 3246 (2.5) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4436 (58:11:14:11:6) |
| 3249 (1.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1513 (77:8:6:5:4) |
| 3252 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4521 (60:11:13:10:6) |
| 3255 (16) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 185 (79:8:6:4:3) |
| 3258 (11) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 150 (79:8:6:4:3) |
| 3261 (11) | 90 Trace 10 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, very carbonaceous in part – grades to coal, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular to blocky fracture, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 598 (64:10:11:9:6) |
| 3264 (7) | 40 60 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4381 (64:10:11:9:6) |
| 3267 (2.5) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4451 (60:12:16:9:4) |
| 3270 (1.3) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1306 (60:12:16:9:4) |
| 3273 (1.6) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 1337 (60:12:16:9:4) |
| 3276 (20) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 124 (81:7:5:4:3) |
| 3279 (24) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 145 (81:7:5:4:3) |
| 3282 (11) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 641 (81:6:6:4:3) |
| 3285 (19) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 295 (81:6:6:4:3) |
| 3288 (31) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 287 (81:6:6:4:3) |
| 3291 (28) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 280 (81:6:6:4:3) |
| 3294 (35) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4305 (70:10:8:7:5) |
| 3297 (32) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 3485 (70:10:8:7:5) |
| 3300 (33) | 50 50 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 2011 (62:11:13:16:4) |
| 3303 (2.0) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 727 (62:11:13:16:4) |
| 3306 (1.4) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 587 (76:7:6:6:5) |
| 3309 (18) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4572 (57:11:15:12:5) |
| 3312 (12) | 100 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile | 1197 (62:11:13:16:4) |
| 3315 (11) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 347 (83:7:4:3:3) |
| 3318 (9) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 1324 (87:6:3:2:2) |
| 3321 (8) | 90 Trace 10 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, very carbonaceous in part – grades to coal, common micromica, hard, subfissile. SANDSTONE, as above. COAL, black to very dark grey, very argillaceous – grades to carbonaceous claystone, earthy lustre, irregular to blocky fracture, hard. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 639 (87:6:3:2:2) |
| 3324 (10) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 390 (70:8:10:7:5) |
| 3327 (8) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 273 (59:12:15:7:6) |
| 3330 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4578 (59:12:15:7:6) |
| 3333 (11) | 100 | SILTY CLAYSTONE, as above | 443 (76:7:6:6:5) |
| 3336 (13) | 100 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, very carbonaceous in part – grades to coal, common micromica, hard, subfissile. | 157 (63:11:13:9:4) |
| 3339 (32) | 100 | SILTY CLAYSTONE, as above | 4287 (63:11:13:9:4) |
| 3342 (20) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, common micromica, hard, subfissile SANDSTONE, as above. | 319 (65:10:11:9:5) |
| 3345 (10) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4237 (65:10:11:9:5) |
| 3348 (7) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 120 (65:10:11:9:5) |
| 3351 (6) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 85 (80:7:5:4:3) |
| 3354 (8) | 30 70 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, very fine to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 115 (80:7:5:4:3) |
| 3357 (8) | 80 20 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, common black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile SANDSTONE, as above. | 3908 (75:9:7:5:4) |
| 3360 (1.5) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 4583 (75:8:6:6:5) |
| 3363 (1.4) | 100 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, common micromica, hard, subfissile. | 472 (75:8:6:6:5) |
| 3366 (4.8) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, silty to very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, trace fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 4426 (59:11:14:11:5) |
| 3369 (10) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 211 (75:8:6:6:5) |
| 3372 (8) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 150 (75:8:6:6:5) |
| 3375 (18) | 100 | SILTY CLAYSTONE, as above. | 145 (75:8:6:6:5) |
| 3378 (15) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 170 (75:8:6:6:5) |
| 3381 (14) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white to light brown, very fine to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, rare fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. | 190 (75:8:6:6:5) |
| 3384 (8) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 155 (75:8:6:6:5) |
| 3387 (2.5) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 403 (76:7:7:6:4) |
| 3390 (1.3) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 334 (76:7:7:6:4) |
| 3393 (5) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 201 (76:7:7:6:4) |
| 3396 (6) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 364 (83:6:3:5:3) |
| 3399 (8) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 240 (83:6:3:5:3) |
| 3402 (11) | 70 10 20 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white to light brown, very fine to fine, dominantly very fine, subangular to subrounded, moderately sorted, strong silica and calcareous cements, abundant off white argillaceous matrix – matrix supported, abundant altered feldspar grains, trace green grey brown red and black volcanogenic lithics, trace quartz grains, rare fine brown mica flakes, trace black carbonaceous detritus, hard, no visual porosity, no oil fluorescence. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular to blocky fracture often contused and striated, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 317 (90:4:2:5:1) |
| 3405 (11) | 80 10 10 Fluor | SILTY CLAYSTONE, as above. SANDSTONE, as above. COAL, as above. FLUORESCENCE, as above. | 409 (87:6:3:3:1) |
| 3408 (7) | 70 10 20 Fluor | SILTY CLAYSTONE, as above. SANDSTONE, as above. COAL, as above. FLUORESCENCE, from coal as above. | 319 (85:6:4:3:2) |
| 3411 (8) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, as above. | 201 (85:6:4:3:2) |
| 3414 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 210 (85:6:4:3:2) |
| 3417 (1.3) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 207 (85:6:4:3:2) |
| 3420 (2.5) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 494 (89:4:2:3:2) |
| 3423 (7) | 90 10 Fluor | SILTY CLAYSTONE, as above. COAL, as above. FLUORESCENCE, from coal as above. | 214 (89:4:2:3:2) |
| 3426 (14) | 90 10 Fluor | SILTY CLAYSTONE, as above. COAL, as above. FLUORESCENCE, from coal as above. | 256 (89:4:2:3:2) |
| 3429 (7) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 240 (89:4:2:3:2) (89:4:2:3:2) |
| 3432 (6) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 386 (91:4:1:2:2) |
| 3435 (8) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, abundant calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, as above, with common calcite lined fractures. | 157 (91:4:1:2:2) |
| 3438 (6) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 319 (91:4:2:2:1) |
| 3441 (9) | 40 60 OIL | SILTY CLAYSTONE, as above. SANDSTONE, off white, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, abundant calcite lined fractures, very hard, no visible intergranular porosity, no intergranular oil fluorescence. FLUORESCENCE, the fracture infill material has dull yellow mineral fluorescence and 10% dull to moderately bright very pale yellow white oil fluorescence giving a weak dull milky white crush cut fluorescence. | 309 (91:4:2:2:1) |
| 3444 (10) | 40 60 OIL | SILTY CLAYSTONE, as above. SANDSTONE, as above. FLUORESCENCE, as above. | 1647 (86:7:3:2:2) |
| 3447 (9) | 30 70 OIL | SILTY CLAYSTONE, medium to dark grey to medium brown, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, abundant calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, off white, very fine to medium, dominantly fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, abundant calcite lined fractures, very hard, no visible intergranular porosity, no intergranular oil fluorescence. FLUORESCENCE, the fracture infill material has dull yellow mineral fluorescence and trace dull to moderately bright very pale yellow white oil fluorescence giving a weak dull milky white crush cut fluorescence. | 204 (86:7:3:2:2) |
| 3450 (5) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, off white, very fine to fine, dominantly fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, trace to common quartz grains, trace black coaly detritus, abundant calcite lined fractures, very hard, no visible intergranular porosity, no oil fluorescence. | 146 (86:7:3:2:2) |
| 3453 (8) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 504 |
| 3456 (8) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 2 (86:7:3:2:2)09 |
| 3459 (9) | 80 20 | SILTY CLAYSTONE, medium to dark grey to medium brown, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, common calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, off white, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, common calcite lined fractures, very hard, no visible porosity, no intergranular oil fluorescence. | 210 (86:7:3:2:2) |
| 3462 (10) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 207 (86:7:3:2:2) |
| 3465 (15) | 90 Trace 10 Fluor | SILTY CLAYSTONE, medium to dark grey to medium brown, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, trace calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, off white, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, trace calcite lined fractures, very hard, no visible porosity, no intergranular oil fluorescence. COAL, black to very dark grey, very argillaceous in part, earthy to subvitreous lustre, irregular to blocky fracture often contused and striated, hard, brittle. FLUORESCENCE, the sandstone has dull orange mineral fluorescence, no cut, the coal has no fluorescence but gives a weak pale yellow crush cut. | 1089 (90:6:2:1:1) |
| 3468 (6) | 80 10 10 Fluor | SILTY CLAYSTONE, as above. SANDSTONE, as above. COAL, as above. FLUORESCENCE, as above. | 220 (90:6:2:1:1) |
| 3471 (11) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white, silty to occasionally fine, dominantly very fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, trace calcite lined fractures, very hard, no visible porosity, no intergranular oil fluorescence. | 227 (90:6:2:1:1) |
| 3474 (13) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 228 (90:6:2:1:1) |
| 3477 (11) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 214 (90:6:2:1:1) |
| 3480 (4) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, off white, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, trace calcite lined fractures, very hard, no visible porosity, no intergranular oil fluorescence. | 190 (90:6:2:1:1) |
| 3483 (7) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, off white, silty to very fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, trace calcite lined fractures, very hard, no visible porosity, no intergranular oil fluorescence. | 197 (90:6:2:1:1) |
| 3486 (10) | 100 Trace | SILTY CLAYSTONE, medium to dark grey to medium brown, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, rare calcite lined fractures, common micromica, hard, subfissile. SANDSTONE, off white, silty to fine, dominantly very fine, subangular to subrounded, moderately sorted, abundant white argillaceous matrix – matrix supported, very strong calcite cement, moderate silica cement, trace multicoloured lithics, common quartz grains, trace black coaly detritus, rare calcite lined fractures, very hard, no visible porosity, no intergranular oil fluorescence. | 1084 (89:6:3:1:1) |
| 3489 (10) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 172 (89:6:3:1:1) |
| 3492 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 170 (89:6:3:1:1) |
| 3495 (8) | 100 Trace Trace Fluor | SILTY CLAYSTONE, as above. SANDSTONE, as above. COAL, as above. FLUORESCENCE, cut from coal as above. | 172 (89:6:3:1:1) |
| 3498 (9) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 190 (89:6:3:1:1) |
| 3501 (6) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 219 (89:6:3:1:1) |
| 3504 (7) | 100 | SILTY CLAYSTONE, as above. | 234 (89:6:3:1:1) |
| 3507 (5) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 219 (89:6:3:1:1) |
| 3510 (17) | 30 70 | SILTY CLAYSTONE, medium to dark grey to medium brown, abundant very fine altered feldspar grains in part, trace to common black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white, very fine to fine, dominantly fine, angular to subrounded, moderately to well sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix, quartzose, abundant altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, no visual porosity, no oil fluorescence. | 130 (89:6:3:1:1) |
| 3513 (22) | 100 | SANDSTONE, off white, very fine to medium, dominantly fine, angular to subrounded, moderately to well sorted, strong silica and weak calcareous cements, abundant white argillaceous matrix, quartzose, abundant altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, no visual porosity, no oil fluorescence. | 68 (89:6:3:1:1) |
| 3516 (15) | 100 | SANDSTONE, as above. | 458 (93:3:2:1:1) |
| 3519 (18) | 100 | SANDSTONE, off white, very fine to medium, dominantly fine, angular to subrounded, moderately to well sorted, moderate silica and weak calcareous cements, common white argillaceous matrix, quartzose, abundant altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, poor visual porosity, no oil fluorescence. | 628 (93:3:2:1:1) |
| 3522 (7) | 100 | SANDSTONE, off white, very fine to medium, dominantly fine, angular to subrounded, moderately to well sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, abundant altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, very poor visual porosity, no oil fluorescence. | 1809 (93:3:2:1:1) |
| 3525 (16) | 100 | SANDSTONE, off white, very fine to occasionally coarse, dominantly fine to medium, angular to subrounded, moderately to well sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, very poor visual porosity, no oil fluorescence. | 739 (94:4:1:1:tr) |
| 3528 (15) | 100 | SANDSTONE, off white, very fine to coarse, dominantly medium, angular to subrounded, moderately sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, very poor visual porosity, no oil fluorescence. | 2088 (94:4:1:1:tr) |
| 3531 (7) | 100 | SANDSTONE, off white, very fine to occasionally very coarse, dominantly medium to coarse, angular to subrounded, poorly sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, hard, poor visual porosity, no oil fluorescence. | 2332 (95:4:1:tr:tr) |
| 3534 (4) | 70 30 | SILTY CLAYSTONE, medium to dark brown to medium to dark grey, occasional very fine altered feldspar grains in part, slightly carbonaceous, trace fine black carbonaceous flecks and detritus in part, common micromica, hard, subfissile. SANDSTONE, as above. | 214 (92:4:2:1:1) |
| 3537 (6) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 128 (92:4:2:1:1) |
| 3540 (6) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, off white, very fine to fine, dominantly fine, angular to subrounded, moderately to well sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, abundant altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, very hard, no visual porosity, no oil fluorescence. | 132 (92:4:2:1:1) |
| 3543 (3) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown, common very fine altered feldspar grains in part, slightly carbonaceous, trace fine black carbonaceous flecks and detritus in part, common micromica, hard, subfissile. SANDSTONE, as above. | 129 (92:4:2:1:1) |
| 3546 (2) | 60 40 | SILTY CLAYSTONE, as above. SANDSTONE, off white, very fine to very coarse, dominantly fine, angular to subrounded, poorly sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, very hard, no visual porosity, no oil fluorescence. | 104 (92:4:2:1:1) |
| 3549 (4) | 100 Trace | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 97 (92:4:2:1:1) |
| 3552 (3) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 106 (92:4:2:1:1) |
| 3555 (5) | 40 60 | SILTY CLAYSTONE, medium to dark grey to medium brown, trace very fine altered feldspar grains in part, moderately carbonaceous, trace fine black carbonaceous flecks and detritus in part, common micromica, hard, subfissile. SANDSTONE, off white, very fine to rarely coarse, dominantly medium, angular to subrounded, poorly sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, trace to common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, very hard, no visual porosity, no oil fluorescence. | 96 (92:4:2:1:1) |
| 3558 (7) | 10 90 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 256 (92:4:2:1:1) |
| 3561 (2) | 20 80 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 149 (88:5:3:2:2) |
| 3564 (1) | 40 60 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 110 (88:5:3:2:2) |
| 3567 (2) | 30 70 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, trace very fine altered feldspar grains in part, moderately carbonaceous, trace fine black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white, very fine to rarely very coarse, dominantly medium, angular to subrounded, poorly sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, trace to common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, very hard, no visual porosity, no oil fluorescence, dull orange mineral fluorescence. | 110 (72:8:7:7:6) |
| 3570 (1) | 50 50 | SILTY CLAYSTONE, medium to dark grey to rarely medium brown grey, moderately carbonaceous, trace fine black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, off white, very fine to medium, dominantly fine, angular to subrounded, poorly sorted, strong silica and weak calcareous cements, common white argillaceous matrix, quartzose, trace to common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, very hard, no visual porosity, no oil fluorescence, dull orange mineral fluorescence. | 86 (72:8:7:7:6) |
| 3573 (1) | 50 50 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 58 (72:8:7:7:6) |
| 3576 (1) | 50 50 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 98 (72:8:7:7:6) |
| 3579 (1.2) | 90 10 | SILTY CLAYSTONE, medium to dark grey to medium brown grey, moderately carbonaceous, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 80 (77:7:6:9:7) |
| 3582 (1.7) | 70 30 | SILTY CLAYSTONE, as above. SANDSTONE, off white, very fine to medium, dominantly fine, angular to subrounded, poorly sorted, strong silica and moderate calcareous cements, common white argillaceous matrix, quartzose, common altered feldspars, trace green grey black and brown lithics, trace fine black coaly detritus, very hard, no visual porosity, no oil fluorescence, dull orange mineral fluorescence. | 98 (77:7:6:9:7) |
| 3585 (1.6) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 95 (77:7:6:9:7) |
| 3588 (1.9) | 100 | SILTY CLAYSTONE, medium grey to black, rarely medium brown, very carbonaceous in part, trace black carbonaceous flecks and detritus, trace micromica, hard to very hard, subfissile. | 83 (77:7:6:9:7) |
| 3591 (1.9) | 100 | SILTY CLAYSTONE, as above. | 57 (72:6:5:8:9) |
| 3594 (3.0) | 30 70 OIL | SILTY CLAYSTONE, as above. KAOLINITIC SANDY CLAYSTONE, off white, moderately calcareous, common to abundant very fine to occasionally fine quartz sand grains, trace black coaly laminates, firm, non fissile, very poor inferred porosity. FLUORESCENCE, the kaolinite has 50% dull patchy medium yellow oil fluorescence giving a very weak dull pale yellow crush cut. | 41 (72:6:5:8:9) |
| 3597 (5.0) | 10 90 OIL | SILTY CLAYSTONE, as above. KAOLINITIC SANDSTONE, off white, moderately calcareous, abundant very fine to fine quartz sand grains dispersed through a white kaolin clay matrix, common black coaly laminates, moderately hard, very poor intergranular porosity. FLUORESCENCE, the kaolinite has 50% very dull patchy medium yellow oil fluorescence giving a very weak dull pale yellow crush cut. | 35 (72:6:5:8:9) |
| 3600 (3.8) | 10 90 OIL | SILTY CLAYSTONE, as above. KAOLINITIC SANDSTONE, off white, moderately calcareous, abundant very fine to fine quartz sand grains dispersed through a white kaolin clay matrix, common black coaly laminates, trace grey banded cryptocrystalline chert – possible fracture infill?, moderately hard, very poor intergranular porosity. FLUORESCENCE, the kaolinite has 5% very dull patchy medium yellow oil fluorescence giving a very weak dull pale yellow crush cut. | 56 (72:6:5:8:9) |
| 3603 (4.2) | 100 OIL | SANDSTONE, off white, very fine to medium, dominantly fine, angular to subrounded, moderately sorted, strong silica and moderate calcareous cements, common to abundant white argillaceous matrix, quartzose, abundant altered feldspar grains, trace green, orange and grey lithics, trace black coaly detritus, trace grey banded cryptocrystalline chert – possible fracture infill?, very hard, no visual porosity. FLUORESCENCE, the kaolinite has trace very dull patchy medium yellow oil fluorescence giving a very weak dull pale yellow crush cut. | 78 (84:6:4:3:3) |
| 3606 (1.4) | 60 40 | SILTY CLAYSTONE, medium grey to black to medium brown, moderately carbonaceous, trace black carbonaceous flecks and detritus, common micromica, hard, subfissile. SANDSTONE, as above. | 77 (84:6:4:3:3) |
| 3609 (1.3) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, off white, very fine to fine, dominantly very fine, angular to subrounded, moderately sorted, very strong silica and moderate calcareous cements, common white argillaceous matrix, quartzose, common to abundant altered feldspar grains, trace green, orange and grey lithics, trace black coaly detritus, very hard, no visual porosity. | 39 (84:6:4:3:3) |
| 3612 (1.4) | 80 20 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 28 (84:6:4:3:3) |
| 3615 (1.3) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 21 (84:6:4:3:3) |
| 3618 (1.2) | 90 10 | SILTY CLAYSTONE, as above. SANDSTONE, as above. | 13 (84:6:4:3:3) |
| 3621 |  |  |  |
| 3624 |  |  |  |
| 3627 |  |  |  |
| 3630 |  |  |  |
| 3633 |  |  |  |
| 3639 |  |  |  |
| 3642 |  |  |  |
| 3645 |  |  |  |
| 3648 |  |  |  |
| 3651 |  |  |  |
| 3654 |  |  |  |
| 3657 |  |  |  |
| 3660 |  |  |  |
| 3663 |  |  |  |
| 3666 |  |  |  |
| 3669 |  |  |  |
| 3672 |  |  |  |
| 3675 |  |  |  |
| 3678 |  |  |  |
| 3681 |  |  |  |
| 3684 |  |  |  |
| 3687 |  |  |  |
| 3690 |  |  |  |
| 3693 |  |  |  |
| 3696 |  |  |  |
| 3699 |  |  |  |
| 3702 |  |  |  |